WEST VIRGINIA DEPARTMENT OF TRANSPORTATION

DIVISION OF HIGHWAYS

EQUIPMENT DIVISION

BIDDER'S EVALUATION REPORT

PROCUREMENT SPECIFICATIONS FOR OPEN END CONTRACT

NO. 013-2-A

9 CUBIC YARD STAINLESS STEEL

DEMOUNTABLE ABRASIVE AND CHEMICAL SPREADER (HYDRAULIC)

NOTE TO BIDDER:    Procurement Specification No. 013-2-A, Paragraph 2.0 recommends the completion and submittal of this Report with your bid.  Purpose of this Report is to enable the West Virginia Division of Highways Evaluation Committee to make full and fair evaluation of the bid.  Addendums in order, along with exception sheets, should be with Bidder’s Evaluation Report.

FAILURE TO SUBMIT THIS REPORT, COMPLETE IN ITS ENTIRETY, MAY SUBJECT THE BIDDER

TO DISQUALIFICATION.

Reference Requisition No.: ______________________

Bidder's Name:____________________________________________________________

Address:__________________________________________________________________

Telephone Number:_________________________________________________________

Years Bidder has been registered to do business with the State of West Virginia:  ______________YRS.

Years Company has been an authorized dealer for proposed unit:                        _______________YRS.

X4.2   	DELIVERY:

X4.2.1 	Delivery date of completed representative unit:________________ Calendar Days After Date of                    										Purchase Agreement

X4.2.2 	Delivery date of balance of completed units:  ________________ Calendar Days After Date of

Purchase Agreement

X5.0	AWARD CRITERIA:

X5.1	Prices in quantities of 		1-10 		________________per unit

11-20		________________per unit

21-30		________________per unit

31-40 		________________per unit

41-50		________________per unit

51 and over	________________per unit

X6.0   SPECIFICATIONS - GENERAL

X6.1   Manufacturer, model, series, and date of manufacture of proposed unit:

________________________________________________________________________

Is descriptive literature, fully describing proposed unit attached to your bid? _____ YES _____ NO

If not, why?______________________________________________________________

X6.2	Will the required number of service manuals, and complete parts list be delivered to the Equipment 	Division at Buckhannon upon completion of delivery of total units?	_____ YES _____ NO

Will the required Equipment Preventive Maintenance Form (Section X6.2 of Bidders Evaluation Report) be provided upon inspection of the pilot unit?				_____ YES _____ NO

X6.2

2-10-00

EQUIPMENT PREVENTATIVE MAINTENANCE QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY SUCCESSFUL BIDDER OR MANUFACTURER=S TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT MODEL TO THE WVDOH.

DESCRIPTION: _______________________________________	MAKE: ___________________________________

MODEL: ________________________    	YEAR: __________	PURCHASE AMOUNT: ______________________

ENGINE:	MAKE: ______________________ 	MODEL: __________________ 	FUEL TYPE: ________________________

HORSEPOWER: _______________	CYLINDER: ________	ENGINE SERIAL: __________________________

COOLING SYSTEM CAPACITY: ______________________

BELTS:		DESCRIPTION:					PART NUMBERS:

___________________________________________	_________________________________________________

___________________________________________	_________________________________________________

GVW: _______________________AXLE CAPACITY:FRONT: ______________	REAR:______________

TIRES:		FRONT MAKE & SIZE: ______________________________________________

REAR MAKE & SIZE: _______________________________________________

DIMENSIONS OF UNIT:	LENGTH: __________		WIDTH: ______________	LENGTH: ___________

VENDOR CONTACT PERSON: ____________________________________		PHONE: __________________________

PARTS:

BATTERY MAKE: ____________________	MODEL: ___________________		CCA: _______________________

TOP OR SIDE POST: __________________	DIMENSIONS: LENGTH ________ WIDTH ________ HEIGHT __________

SPARK PLUGS OR FUEL INJECTORS MAKE: ______________	PART # __________________________________________

FUEL PUMP OR INJECTION PUMP MAKE: ________________	MODEL: _________________________________________

ALTERNATOR MAKE: __________________________________	PART #:__________________________________________

STARTER MAKE: ______________________________________	PART #: _________________________________________

TURBO CHARGER MAKE: ______________________________	PART #: _________________________________________

TRANS. MAKE: ____________________	MODEL: _________________________   AUTO/MANUAL: ____________________

HYDRAULIC PUMP MAKE: _____________________________	MODEL: _________________________________________

FILTERS		MAKE	PART NO.		LUBRICANT		MANUFACTURER TYPE

OIL		__________________________________	ENGINE	__________________________________________

AIR INNER	__________________________________	TRANSMISSION__________________________________________

AIR OUTER__________________________________	POWER STEERING _______________________________________

FUEL PRIMARY ______________________________	HYDRAULIC  	__________________________________________

FUEL SECONDARY ___________________________	DIFFERENTIALS _________________________________________

COOLANT	__________________________________	BRAKE FLUID 	__________________________________________

HYDRAULIC	_______________________________	COOLANT	__________________________________________

OTHER		__________________________________ 	OTHER 	__________________________________________

X6.3	TRAINING:

Will training seminar be conducted on Preventive Maintenance, Operator and Mechanic Training                      								_____YES _____ NO

Will you conduct training with each purchase order against this open end contract?

_____ YES _____ NO

Will training be conducted within 2 working days from the delivery of the pilot unit on the individual purchase order?								_____ YES _____ NO

If NO, explain time frame_____________________________________________________________

Will an Operator’s Manual be furnished to the Training Academy?	_____ YES _____ NO

X6.4   	If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors, required in conducting the training?		         _____ YES _____ NO

X6.4.1    	Will all manuals, booklets, etc. explaining preventive maintenance, operator procedures, and service schedule be delivered with each unit?           			_____ YES_____NO

If NO, explain _____________________________________________________

X6.5	WARRANTY AND SERVICE POLICY

Will the warranty and service you provide comply with all areas as stated in Section 6.5 of specifications                               							_____ YES _____ NO

Is warranty literature attached?					_____ YES _____ NO

Is a minimum two (2) year bumper to bumper basic parts and labor warranty included?

_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

X6.5	WARRANTY AND SERVICE POLICY QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY THE SUCCESSFUL BIDDER

OR MANUFACTURERS TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT

MODEL TO THE WVDOH (If additional lines are needed, make copies of form.)

1. Define the terms of the standard warranty.  If not offered, so state.  (Attach copy)

2. Define warranty service to be performed at DOH facilities and warranty service to be performed at

manufacturer’s representative facility.  List name and location of manufacturer’s representative.

3. List locations for parts inventories that are within the State of West Virginia.  Also, list availability levels, if

known.

4. During the term of warranty, list the guarantee discount to manufacturer’s published list price for parts that

bidder will sell the parts to owner.

A.	Terms: Net 30	Manufacturer’s published list price less: __________% discount

B.	Terms: Net 60	Manufacturer’s published list price less: __________% discount

C.	Terms: Net 90	Manufacturer’s published list price less: __________% discount

5. During the term of warranty, will all manufacturers or engineering improvements be submitted to Division of

Highways?							_____ YES _____ NO

6. During the term of warranty, list the guaranteed rates charged for repair to the unit.

A.	Shop Rate		$ __________ per mechanic hour

B.	Travel Time Charge		$ __________ per mechanic hour

(Specify if one-way)		__________; port to port __________

C.	Mileage Charge		$__________ per vehicle mile

(Specify if one-way		__________; port to port __________

D.	Field Mechanic Rate		$__________ per mechanic hour

E.	Specify period of time that prices are in effect: __________________________

F.	Surcharge for miscellaneous items: ____________________%

X6.6 	EVALUATION COMMITTEE REQUIREMENTS

Is all component specifications, product literature, component models provided for Evaluation Committee bid determination?					_____ YES _____ NO

X6.7	Will all parts, equipment, accessories, material, design and performance characteristics not specified 	herein, but which are necessary to provide a complete unit, be furnished with the unit and

conform in strength, quality of material, and quality of workmanship to those which are advertised and 	provided to the market in general by the unit industry?                                    _____YES _____NO

X6.7.1	Are all parts and accessories adequate and regularly supplied as standard to be included except those 	which may be duplications of specifications herein, and except these by specification are not to be

furnished?                                        						_____YES _____NO

X6.7.2	Are all standard safety features that are required by Federal and State statutes of law included?                   											_____YES _____NO

X7.0	SPECIFICATIONS OF THE QUOTED UNIT

The bidder should complete the following schedule in order for the Division to compare the actual bid 	unit to the specifications.  Should the bidder except a requirement, then such exception may be only on 	the basis that such feature is not offered by the manufacturer.  The Division will have the sole 		discretion as to whether the bidder's substitution meets the requirements of the specifications.

Manufacturer: _____________________________	Model: ______________________

X7.1    Is spreaders offered the commercial heavy duty, self contained, hopper type?____YES _____NO

X7.2    Does spreader consist of a 12 gauge 304 stainless steel body, feeder conveyor, spinner disc, power drive, and all components necessary to make a complete operating unit?                _____YES _____NO

X7.3    Is the unit capable of uniformly spreading sand, cinders, salt, calcium chloride, or other mixtures up to 	a width of forty (40) feet?		                                                           _____YES _____NO

X7.4    Body:

X7.4.1     	Is the body of 304 stainless steel construction 100% welded inside and outside of the body?	                 	_____YES _____NO

X7.4.2     	Capacity struck: ______________ cubic yards

X7.4.3     	Inside length:________________ feet as measured from front of spreader hopper to the rear hopper gate and conveyor chain exit point

X7.4.4     	Overall height:_______________ inches

X7.4.5     	Inside width:________________ inches

X7.4.6     	Are the body sides sloped approximately 45 degree pitch to insure free flow of materials to the

conveyor                    							_____YES _____NO

X7.4.7     	Gauge of 304 stainless steel in sides and endgates is __________________Gauge.

X7.4.8     	Is a formed double crimped section on top of body for additional support?	_____YES _____NO

X7.4.9     	Sills constructed of________________gauge 304 stainless steel.

Supported on rectangular formed cross sills          _____ YES _____ NO

X7.4.10    Number of 10 gauge full slope body side supports tying the cross sills with body sides? __________

X7.4.11    Are there four (4) 304 stainless steel 5/8 inch round lifting eyes		_____ YES _____ NO

Is the inside eye opening designed to allow the passage of an alloy eye type Grade 80’ 3/8 inch grab

hook with a width dimension of 2 11/16 inch (with the top screen down in the rest position on top of

the spreader)								_____ YES _____ NO

Two (2) on each side of spreader mounted and secured in a manner that the entire unit may be safely

lifted for storage/installation purposes           				_____ YES _____ NO

X7.4.12    Is all necessary hardware stainless steel                                	_____YES _____NO

X7.4.13    Will a 12 gauge 304 stainless steel cabshield be mounted on the front of body to protect cab from

falling material when loading with slope design to fall in hopper as spreader unloads?                             								_____ YES _____ NO

Does cabsield extend 13 inches in front of the hopper at 45 degrees	_____ YES _____ NO

X7.4.14    Will a fold up ladder be mounted on the rear of spreader body at right side for easier access to top

and secured in the folded position with two (2) flexible draw latches 	_____ YES _____ NO

Does the ladder have hand holds and non slip grip strut steps		_____ YES _____ NO

X7.5    Conveyor:

X7.5.1     	Is the conveyor located in bottom of hopper and capable of engaging material along its full length

and moving material to rear adjustable metering gate?                               _____YES _____NO

X7.5.2     	Is conveyor continuous ladder type consisting of two parallel chains with cross bars on 4 2" centers

made of 1/4" x 1-1/2" steel?	                                                           _____YES _____NO

X7.5.3		Is each cross bar formed and welded both top and bottom to chain links _____ YES _____ NO

X7.5.4     	Tensile strength of each chain:_______________ pounds

X7.5.5     	Overall width of chain conveyor:_____________ inches

X7.5.6     	Are replaceable rubber wear strips provided to prevent contact of material being spread with the

chain?                    						_____YES _____NO

X7.5.7     	Is a 10 gauge 304 stainless steel heavy-duty replaceable conveyor plate at least 3/16" thick fitted?             _____YES _____NO

X7.5.8     	Is the chain drive through 1-1/2" sprockets and shafting front and rear?	_____YES _____NO

X7.5.9     	Does conveyor have adjustment provisions at rear of spreader for at least 3" lateral takeup?                         											_____YES _____NO

X7.5.10   	Is additional 7 gauge 304 stainless steel reinforcing plate welded to longitudinal webs covering the

area of the drive shaft, bearing, and idler bearing provided (if required)?	_____YES _____NO

X7.5.11    Is material composition of adjustment mechanism stainless steel	             _____YES _____NO

X7.5.12    Is conveyor drive motor mounted on reduction gear box and has a ratio of approximately 50-1   												_____YES _____NO

X7.5.13    Does conveyor gear box have its drive shaft extended through rear of gear housing?                                											_____YES _____NO

X7.5.13.1 		Is the shaft end machined to accommodate the application rate sensor shaft for the Dickey-John     Automatic Control System, Model ICS-2000?                                 _____YES _____NO

X7.5.13.2       	Is the necessary oil seal included?             				_____YES _____NO

X7.5.14    	Is a 7 gauge stainless steel adjustable greasable screw jack type discharge gate located at the body rear to adjust the flow of material to the spinner?		           _____YES _____NO

X7.5.15    	Feedgate opening: ______ inches high x ______ inches wide

X7.5.16	Is any and all exposed moving or rotating mass adequately shielded in order to protect personnel while performing required operational adjustments including gear box extended input shaft when rate sensor is installed?							_____ YES _____ NO

X7.5.17	Is the pintle conveyor chain heat treated form links with locked, non-turning pins

_____ YES _____ NO

X7.6    Distributor Spinner Assembly:

X7.6.1     	Diameter of urethane distributor disc__________inches

X7.6.1.1   		Number of fins:____________

X7.6.1.2   		Are fins designed to obtain a controlled spread of materials from four feet (4') to forty feet (40')?   								 _____YES _____NO

X7.6.2     	Is material guided from conveyor end to distributor disc by means of an externally adjustable

material flow baffles, enclosed within the chute?				_____YES _____NO

X7.6.3     	Is the spinner vertically adjustable to a full 16 inches?	                          _____YES _____NO

and _________ inch spinner position below mounting surface?

X7.6.4     	Is a deflector baffle or diverter chute provided in an enclosed distributor spinner hopper assembly so

it can be positioned in such a manner that material can be unloaded from spreader without striking

spinner?                                        					_____YES _____NO

X7.7    Baffles:

X7.7.1     	Are baffles provided to control direction and width of spread?	           _____YES _____NO

X7.7.1.2   		Are there four (4) sections over right, left, rear and front of spinners?     _____YES _____NO

X7.7.2     	Are sections easily adjusted from the full down to the horizontal position without use of tools?       											_____YES _____NO

X7.8.   Power Drive:

X7.8.1     	Is the power drive hydraulic type?              				_____YES _____NO

X7.8.1.2   		Are two (2) hydraulic motors provided - one (1) powering the spinner assembly and one (1)           powering the conveyor?     						_____YES _____NO

X7.8.2     	Spinner hydraulic motor mounted below the spinner hopper assembly?	 _____YES _____NO

X7.8.3     	The conveyor hydraulic motor of the orbital, low speed, hi-torque integrally mounted to conveyor

gear box?        								_____YES _____NO

X7.9  Screen Over Hopper:

X7.9.1    	Are four (4) sectional screens hinged to 10 gauge 304 stainless steel 4 inch x 6 inch formed box                  beam running longitudinally the full length of spreader hopper?		_____YES _____NO

If not specify: ___________________

X7.9.2    	Do screen sections have 3/8" diameter carbon steel rods welded forming 2-1/2" x  2-1/2" square

openings with reinforcing bars at the center of each section?         	_____YES _____NO

If not specify: ____________________

X7.9.3    	Do screens increase overall height of spreader more than 7 inches down the center?                                											_____YES _____NO

X7.9.4		Are screens powder coated black						_____ YES _____ NO

X7.10  Is lighting in accordance with the attached sketch?	 _____YES _____NO

X7.10.1	Is the combination and marker lights LED type				_____ YES _____ NO

X7.10.2	Are stop, tail, turn combination lights and marker lights shielded	_____ YES _____ NO

X7.10.3	Is strobe light “quad flash”						_____ YES _____ NO

X7.11  Hydraulic Components:

X7.11.1    	Are all necessary fittings for complete hookup of spreader hydraulics to DOH dump trucks central 			hydraulic system provided?	                                                           _____YES _____NO

X7.11.2    	Are all fittings of the steel type and designed for hydraulic use?              _____YES _____NO

X7.11.3    	Is the truck central hydraulic system complete to and including the rear manifold, located at the rear

cross member of truck						_____ YES _____ NO

Will the rear manifold have attached to it one (1) 3/4” I.D. pressure line with 3/4” quick disconnect,

one (1) 2” I.D. pressure line with 2 inch quick disconnect, one (1) 1” I.D. return line with 1 1/4”

quick disconnect and disconnects will be “VH” series snap-tite.	_____ YES _____ NO

Will you supply proper mating quick disconnects, metal caps, and plugs for connection to truck

manifold							_____ YES _____ NO

X7.12	Is an anodized 6061T6 aluminum grease manifold block mounted at the rear of the body which incorporates the front bearing grease extension tubes, rear bearing grease fittings and feedgate screw jack lubrication tube to allow for lubrication of the front bearings and feedgate screw jack from a single convenient location?								_____ YES _____ NO

Will other fittings be placed at convenient location for normal maintenance 	_____YES _____NO

X7.12.1	Do the anodized 6061T6 aluminum grease manifold block have a minimum of 6 ports tapped to

accept three (3) 1/8 inch straight grease zerks and three (3) 1/8 inch grease Parflex hoses to provide

adequate one location greasing of the front and rear bearings and feed gate screw jack

_____ YES _____ NO

Are unused ports properly plugged					_____ YES _____ NO

X7.12.2	Are hoses used in the grease manifold system Parflex hose by Parker Hannifin or equal, with 1/8 inch I.D., 0.34 inch maximum O.D., a maximum working pressure of 2500 PSI and a minimum burst pressure of 10,000 PSI?							_____ YES _____ NO

Are hose assemblies held in place by a sufficient number of rubber cushioned hose clamps?

_____ YES _____ NO

X7.13  Is one (1) piece of angle iron 3/8" x 4" X 90" and two (2) pieces of 1" round shafting ten inches (10") 	long provided but not installed for each unit?                                  	_____YES _____NO

X7.14 Other standard features:

List other standard features offered but not specifically addressed above:

___________________________________________________________________________________

___________________________________________________________________________________

___________________________________________________________________________________

___________________________________________________________________________________

X7.15  Paint:

Describe method of painting parts and accessories that are not required to be stainless or rustproof:

___________________________________________________________________________________

___________________________________________________________________________________

___________________________________________________________________________________

X7.16  Does unit offered meet or exceed "Occupational Safety and Health Act of 1970"?                                    										  _____YES _____NO

X7.17  Does unit conform to the advertising guidelines?                        	_____YES _____NO