ADDENDUM #2

707EC020

OPEN END CONTRACT

SKID STEER LOADER WITH ATTACHMENTS

CHANGES TO SPECIFICATIONS:

FROM:

5.1	SECOND PARAGRAPH

Prices for the units with attachments shall be in quantities of 1-5, 6-10, and 11 and over.

However, for evaluation purposes, we will use quantities 1-5 for loader and all

attachments.  DOH reserves the right to place orders in any quantity.  Orders placed may

be with one (1) or all attachments.  Attachments may be ordered as needed.

TO:

5.1	SECOND PARAGRAPH

Prices for the units with attachments shall be in quantities of 1-5, 6-10, and 11 and over.

Also, price for loader only shall be submitted as well.  However, for evaluation purposes,

we will use quantities 1-5 for loader and all attachments.  DOH reserves the right to place

multiple orders in any quantity.  Orders placed may be with one (1) or all attachments.

Attachments may be ordered as needed.

FROM:

8.4.2	Unit shall have high flow hydraulic system providing adequate flow and pressure for

specified attachments.

TO:

8.4.2	Unit shall have high flow hydraulic system (30 GPM minimum).

DELETE:

9.3	A remote attachment control device should be available for specified attachments

(marked by an “*”) to start the loader and operate the attachment from the outside the

operator control area.

707EC020

ADDENDUM #2

Page 2

RENUMBER:

9.4

to	A single control unit should be provided which will control all available attachments.

9.3

DELETE AS WRITTEN:

9.5 		The following attachments should be available:

and

sub

topics

9.5.1

to and

including

9.5.54

ADD:

9.4 		The following attachments shall be available and must be priced to award

contract.

and

sub

topics

9.4.1

through

9.4.32

as follows:

| AUGER – WOODS EQUIPMENT CORPORATION OR EQUAL | HA 25 | HA30 |
| --- | --- | --- |
| Drive Type | Planetary | Planetary |
| Flow Range | 10 – 30 gpm | 10 – 40 gpm |
| Pressure Range | 3500 psi | 3500 psi |
| Maximum Bit Size | 36” | 36” |
| Approximate Weight | 620 lb. | 650 lb. |
| Performance Guide | Heavy Duty | Heavy Duty |
| BIT SPECIFICATIONS FOR BOTH MODELS |  |  |
| Bit Specification – Hex – Single Flight Extension | 6” x 50” Head 12” x 50” Head 24” x 50” Head |  |
| Single Flight Extension | 12” extension 24” extension 48” extension |  |

| BACKHOE WITH 12 INCH BUCKET– ATTACHMENT TECHNOLOGIES INC. OR EQUAL | 509 | 511 | 609 | 611 |
| --- | --- | --- | --- | --- |
| Transport Height | 7 ft. 9 in. | 8 ft. 10 in | 7 ft. 9 in | 8 ft. 10 in |
| Transport Width | 5 ft. 0 in | 5 ft. 0 in | 4 ft. 9 in. | 4 ft. 9 in |
| Ground Clearance | 11 ft | 11 ft | 11 ft | 11 ft |
| Overall Length | 7 ft. 7 in | 7 ft 9 in | 7 ft 7 in | 7 ft 9 in |
| Boom Pivot Height | 16 in. | 16 in. | 16 in. | 16 in. |
| Operating Weight w/12 in. Bucket | 1425 lb. | 1594 lb. | 1702 lb. | 1847 lb. |
| Digging Depth Maximum | 9 ft. 8 in. | 11 ft. 1 in. | 9 ft. 8 in | 11 ft. 1 in. |
| Digging Depth (2 ft.) Flat Bottom | 9 ft. 7 in. | 11 ft. 0 in. | 9 ft. 7 in. | 11 ft. 0 in. |
| Digging Depth (8 ft.) Flat Bottom | 8 ft. 3 in. | 9 ft. 11 in | 8 ft. 3 in. | 9 ft. 11 in |
| Overall Operating Height – Fully Raised | 12 ft 10 in | 14 ft. 5 in | 12 ft. 10 in | 14 ft. 5 in |
| Loading Height | 6 ft. 10 in | 8 ft 0 in | 6 ft. 10 in | 8 ft. 0 in |
| Loading Reach | 4 ft. 2 in. | 5 ft 0 in | 4 ft. 2 in | 5 ft. 0 in |
| Reach from Swing Post | 12 ft. 9 in | 14 ft. 5 in | 12 ft. 10 in | 14 ft. 5 in |
| Bucket Rotation | 180 degrees | 180 degrees | 180 degrees | 180 degrees |
| Swing Arc | 180 degrees | 180 degrees | 180 degrees | 180 degrees |
| Straight Wall Digging Depth | 7 ft. 3 in | 8 ft. 2 in | 7 ft. 3 in | 8 ft. 2 in |
| Stabilizer Spread Operating Position | 7 ft. 11 in. | 7 ft 11 in | 9 ft. 11 in | 9 ft. 11 in |
| Stabilizer Down Below Grade | 16 in | 16 in | 17 in | 17 in |
| System Relief Valve Setting | 2500 psi | 2500 psi | 2500 psi | 2500 psi |
| Digging Force – Bucket Cylinder | 5676 lb. | 5676 lb. | 5908 lb. | 6167 lb. |
| Digging Force – Dipper Cylinder | 2754 lb. | 3056 lb. | 3232 lb | 4160 lb. |

| BACKHOE – MINI – FFC ATTACHMENTS OR EQUAL | MB 12 | MB 18 | MB 24 |
| --- | --- | --- | --- |
| Digging Depth | 5 ft. 6 in | 5 ft. 6 in | 5 ft. 6 in |
| Bucket Width | 12 in | 18 in | 24 in |
| Weight | 635 lb. | 665 lb | 695 lb. |

| BLADE – DOZER – ATTACHMENT TECHNOLOGIES INC. OR EQUAL | DB 96 |
| --- | --- |
| Width from Centerline to Inside Edge @ 15 degree Angle | 49.31 in |
| Width from Centerline to Inside Edge @ 30 degree Angle | 47.38 in |
| Dozer Blade Width @15 degree Angle | 92.73 in. |
| Dozer Blade Width @ 30 degree Angle | 83.56 in |
| Width from Centerline to Outside Edge @ 15 degree Angle | 43.41 in. |
| Width from Centerline to Outside Edge @ 30 degree Angle | 36.16 in. |
| Overall Width | 96.00 in |
| Angle Left and Right | 30 degrees |
| Overall Length | 36.68 in |
| Overall Height | 29.89 in. |
| Approximate Weight | 1460 lb. |

| BOOM – MATERIAL HANDLING – ATTACHMENT TECHNOLOGIES INC. OR EQUAL | MH 66 |
| --- | --- |
| Rated Load Capacity | 1500 lb. |
| Height | 66 in. |

| BREAKER – HYDRAULIC – KOMATSU OR EQUAL | JPB 210 |
| --- | --- |
| CIMA Tool Energy Rating | 212 ft. lb. |
| Flow Range | 22 gpm |
| Striking Rate | 1375 bpm |
| Operating Pressure | 2059 psi |
| Working Weight | 527 lb. |
| Striking Rate (blows per minute) | 1040 min |
| Adjusted Breaker Pressure | 2000 psi |
| Max. Operating Pressure | 2100 psi |
| Tool Diameter | 2.5 in. |

| BROOM – ANGLE – POLY/WIRE BRISTLES – ATTACHMENT TECHNOLOGIES INC. OR EQUAL | AB 84 |
| --- | --- |
| Overall Width | 94 in. |
| Sweeping Width | 88 in |
| Overall Height | 35.5 in. |
| Length Coupler to Brush Front | 59.60 in. |
| Transport Height On Stand | 40.0 in. |
| Maximum Angle (Left and Right) | 30 degrees |
| Sweeping Width @ 30 degree Angle | 76 in. |
| Weight | 1031 lb. |
| Brush Diameter | 32 in. |
| Wafers (Quantity) | 45 |
| Optional Water Kit with 25 Gallon Tank |  |
| Manual/Hydraulic Angle |  |

| BROOM – GENERAL PURPOSE PICK-UP – WOODS EQUIPMENT CORP. OR EQUAL | PB68 |
| --- | --- |
| Brush Width | 60 in. |
| Overall Width | 68.5 in |
| Height | 25.25 in |
| Length | 67.7 in |
| Approximate Weight | 714 lb. |
| Hopper Capacity | 13.5 cu. ft |
| Optional Gutter Broom | Cleaning next to curbs |

| BRUSH CUTTER – FFC ATTACHMENTS OR EQUAL | LAF 3772 |
| --- | --- |
| Overall Width | 75.5 in |
| Cutting Width | 72 in |
| Height | 27 in |
| GPM Range | 15-30 gpm |
| Max PSI Range | 3500 psi |
| Blade Speed Min/Max | 12474/19127 ft/min |
| Weight Approximate | 1653 lb. |

| BUCKET – BRUSH GRAPPLE – ATTACHMENT TECHNOLOGIES INC. OR EQUAL | BG 84 |
| --- | --- |
| Overall Width | 84 in |
| Overall Depth | 35.9 in |
| Grapple Width | 20.5 in |
| Tine Spacing | 6 in. |
| Grapple Height – Closed | 26.4 in. |
| Grapple Hook – Opening | 42 in. |
| Overall Weight (lbs) | 826 lb. |
| Clamping Force (lbs) | 1250 lb. |
| Number of Grapple Teeth | 4 |
| Number of Cylinders | 2 |
| Tines & End Plates | 1/2 in. T1 steel (100,000 lb. yield) |
| Bore | 2.00 in |
| Stroke | 8.25 in |
| Rod Diameter | 1.25 in. |

| BUCKET – FORKED SCRAP GRAPPLE – FFC ATTACHMENTS OR EQUAL | FSG 63 | FSG 72 |
| --- | --- | --- |
| Opening Height | 41 in. | 41 in. |
| Height Closed | 20 in. | 20 in. |
| Usable Tooth | 24.13 in. | 24.13 in |
| Width | 63.44 in. | 73.06 in. |
| Number of Teeth | 8 | 10 |
| Approximate Weight | 990 lb. | 1100 lb. |
| Cylinder Bore | 2 in. | 2 in. |
| Cylinder Stroke | 8 in. | 8 in. |

| BUCKET – GENERAL PURPOSE – WOODS EQUIPMENT CORP. OR EQUAL | GP 68S | GP 73S | GP 68L | GP 73L |
| --- | --- | --- | --- | --- |
| Type of Bottom | Short | Short | Long | Long |
| Width | 68 in | 73 in | 68 in | 73 in |
| Height | 19 in | 19 in | 19 in | 19 in |
| Length | 29 in | 29 in | 35 in | 35 in |
| Approximate Weight | 440 lb. | 469 lb. | 475 lb. | 508 lb. |
| Heaped Capacity | 13.4 cu ft | 14.4 cu ft | 16.5 cu ft | 17.8 cu ft |
| Optional Teeth | Weld on | Weld on | Weld on | Weld on |
| Optional Bolt on Cutting Edge | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible |
| Optional Bolt on Toothbar Inside Bucket Width | 66 3/8 in – 66 3/4 in | 71 3/8 in – 71 3/4 in | 66 3/8 in – 66 3/4 in | 71 3/8 in – 71 3/4 in |

| BUCKETS – GENERAL PURPOSE UTILITY & LIGHT MATERIAL – WOODS EQUIPMENT CORPORATION OR EQUAL | UT 72 | LM 72 | LM 78 | LM 84 |
| --- | --- | --- | --- | --- |
| Type | GPU | LM | LM | LM |
| Width | 72 in | 72 in | 78 in | 84 in |
| Height | 25 in | 26 in | 26 in | 26 in |
| Length | 35 in | 38 in | 38 in | 38 in |
| Approximate Weight | 553 lb. | 585 lb. | 617 lb. | 660 lb. |
| Heaped Capacity | 22.8 cu. ft | 25.8 cu ft | 28.1 cu ft | 30.3 cu ft |
| Optional Bolt on Cutting Edge | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible |
| Optional Bolt on Toothbar Inside Bucket Width | 70 3/8 in – 70 3/4 in | NA | NA | NA |

| BUCKET – HEAVY DUTY SCRAP GRAPPLE – WOODS EQUIPMENT CORP. OR EQUAL | SG 72 | SG 78 |
| --- | --- | --- |
| Width | 72 in | 78 in |
| Height | 28 in | 28 in |
| Length | 27 1/4 in | 27 1/4 in |
| Capacity | 14 cu ft | 15.2 cu ft |
| Approximate Weight | 856 lb. | 886 lb. |
| Cylinder Bore Diameter | 2 in. | 2 in. |
| Cylinder Stroke | 8 1/4 in | 8 1/4 in |
| Optional Bolt on Cutting Edge | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible |

| BUCKET – MULTI-PURPOSE – WOODS EQUIPMENT CORP. OR EQUAL | MP 73 | MP 78 |
| --- | --- | --- |
| Width | 73 in | 78 in |
| Height | 31 in | 31 in |
| Length | 33 in | 33 in |
| Heaped Capacity | 14.2 cu ft | 15.5 cu ft |
| Approximate Weight | 644 lb. | 688 lb. |
| Cylinder Rod Diameter | 1 1/2 in | 1 1/2 in |
| Cylinder Bore | 2 1/2 in | 2 1/2 in |
| Cylinder Stroke | 8 in | 8 in |
| Optional Bolt on Reversible Cutting Edge | 5/8 in x 8 in reversible | 5/8 in x 8 in reversible |
| Optional Bolt on Toothbar Inside Bucket Width | 71 3/8 in – 71 3/4 in | 76 3/8 in – 76 3/4 in |

| BUCKET – ROCK – ATTACHMENT TECHNOLOGIES INC. OR EQUAL | RB 75 |
| --- | --- |
| Overall Width | 74.35 in |
| Overall Depth | 42.45 in |
| Depth with Skid Steer Mounting | 49.80 in |
| Overall Height | 21.77 in |
| Tine Spacing (Center to Center) | 4.25 in |
| Tine Spacing (Between Tines) | 3.125 in |
| Overall Weight (lbs.) | 619 lb. |
| Number of Tines | 18 |
| Tine Rod Diameter | 1.125 in |

| COLD PLANER – WOODS EQUIPMENT CORP. OR EQUAL | CP 12 | CP 16 | CP 18 | CP 24 | CP 30 |
| --- | --- | --- | --- | --- | --- |
| Depth of Cut | 0-6 in | 0-6 in | 0-6 in | 0-6 in | 0-6 in |
| Width of Cut | 12 in | 16 in | 18 in | 24 in | 30 in |
| Number of Teeth | 28 | 50 | 56 | 70 | 77 |
| Sideshift | 22 in | 22 in | 22 in | 22 in | 22 in |
| Tilt | 19 degrees | 19 degrees | 19 degrees | 15 degrees | 11 degrees |
| Weight | 1200 lb. | 1750 lb | 2000 lb. | 2300 lb. | 2450 lb |
| Hydraulic Depth Control | Std | Std | Std | Std | Std |
| Hydraulic Tilt Control | Std | Std | Std | Std | Std |

| CONCRETE CLAW – FFC ATTACHMENTS OR EQUAL | 10024 |
| --- | --- |
| Working Width | 24 in |
| Working Depth | 48 in |
| Height OD | 21 in |
| Rear Opening Height | 7.5 in |
| Weight Approximate | 575 lb. |

| FORKS – PALLET – ATTACHMENT TECHNOLGIES INC OR EQUAL | PF 48 |
| --- | --- |
| Weight (Including mounting) | 370 lb. |
| Fork Length | 48 in |
| Fork Capacity | 4000 lb. |
| Fork Spread Range | 4 3/8 – 40 3/8 in |
| High Visibility Back Guard | Yes |
| Tooth Double Lock Downs | Yes |

| GRAPPLE – LOG FORK – FFC ATTACHMENTS OR EQUAL | LG 28 |
| --- | --- |
| Tine Length | 28.4 in |
| Opening Height | 43.1 in |
| Capacity | 6400 lb. |
| Weight | 610 lb. |

| HITCH – THREE POINT – WOODS EQUIPMENT CORP. OR EQUAL | TH3000 |
| --- | --- |
| Overall Width | 46 in |
| Height | 26 in |
| Length | 11 in |
| Approximate Weight | 180 lb. |

| POWER RAKE – FFC ATTACHMENTS OR EQUAL | PRA 90 |
| --- | --- |
| Working Width | 90 in |
| Overall Width | 101 in |
| Fully Angled Width | 86 in |
| Height | 30.3 in |
| Angle Option | Manual Hydraulic |
| Weight | 1075 lb. |

| PREPARATOR – FFC ATTACHMENTS OR EQUAL | P 76 |
| --- | --- |
| Bucket Capacity | 12.5 cu ft |
| Overall width | 85.25 in |
| Bucket Swath Width | 76 in |
| Overall Bucket Height | 25.53 in |
| Overall Bucket Length | 53 in |
| RPM-r/min@16 gpm Nominal Flow | 0-100 |
| Overall Drum Diameter | 21.5 in |
| Tooth Thickness | .19 in |
| Tooth Length | 2.19 in |
| Number of Teeth | 340 |
| Rake Drive | #80H Roller Chain |
| Brush Drive | #50H Roller Chain |
| Overall Weight | 1465 lb. |

| ROCK WHEEL WITH 50 GALLON WATER KIT – WOODS EQUIPMENT CORP. OR EQUAL | RW 12 | RW 18 | RW 24 |
| --- | --- | --- | --- |
| Depth of Cut | 0-12 in | 0-18 in | 0-24 in |
| Width of Cut | 2.5/4.5 in | 2.5/4.5 in | 2.5/4.5 in |
| Number of Teeth | 28/33 | 42/44 | 56/66 |
| Side Shift | 22 in | 22 in | 22 in |
| Weight | 1600 lb. | 1800 lb. | 2100 l.b |
| Wheel Speed | 60 rpm | 60 rpm | 60 rpm |
| Cutting Speed | Up to 15 fpm | Up to 15 fpm | Up to 15 fpm |

| ROLLER – VIBRATORY – WOODS EQUIPMENT CORP. OR EQUAL | VR 66A | VR 73A |
| --- | --- | --- |
| Drum Width | 66 in | 73 in |
| Overall Width | 73 in | 80.5 in |
| Drum Oscillation | +/-50 degrees | +/-15 degrees |
| Overall Height | 27 in | 27 in |
| Overall length | 33 in | 33 in |
| Drum Diameter | 24 in | 24 in |
| Total Output | 8740 lb. | 10,240 lb. |
| Frequency VPM | 2000 @ 15 gpm | 2000 @ 15 gpm |
| Weight lbs. Smooth | 1633 lb. | 1762 lb |
| Weight lbs. Padded | 1850 lb. | 2100 lb. |

| SCARIFIER – WOODS EQUIPMENT CORP. OR EQUAL | SF 3000 |
| --- | --- |
| Working Width | 40 in |
| Overall Width | 63 in |
| Height | 27 in |
| Length | 20 in |
| Approximate Weight | 350 lb. |
| Number of Shanks | 5 |

| SNOW BLADE – FFC ATTACHMENTS OR EQUAL | SB 96 |
| --- | --- |
| Length | 96 in |
| Height with Edge | 23.25 in |
| Angled Width | 82.9 in |
| Weight | 525 lb. |

| SNOW BLOWER – FFC ATTACHMENTS OR EQUAL | 84 | 84H |
| --- | --- | --- |
| Cutting Width | 84 in | 84 in |
| Shroud Opening | 25 in | 36 in |
| Overall Depth | 38 in | 43 in |
| Overall Height | 56.75 in | 74 in |
| Weight | 720 lb. | 1230 lb. |

| STUMP GRINDER – WOODS EQUIPMENT CORP. OR EQUAL | SG 20 | SG 40 | SG 60 |
| --- | --- | --- | --- |
| Overall Length | 64.1 in | 64.1 in | 64.1 in |
| Telescopic Extension | 7 in | 7 in | 7 in |
| Horsepower Delivered | To 20 HP | To 40 HP | To 60 HP |
| Cutting Height Above Ground | 21 in | 21 in | 21 in |
| Cutting Depth Below Ground | 16 in | 16 in | 16 in |
| Cutting Wheel Width | 3.25 in | 3.25 in | 3.25 in |
| Cutting Width | 60 in | 60 in | 60 in |
| Swing Range | 140 degrees | 140 degrees | 140 degrees |
| Type of Teeth | 0.5 in slanted, carbide tip | 0.5 in slanted, carbide tip | 0.5 in slanted, carbide tip |
| Number of Teeth | 32 | 32 | 32 |
| Wheel Diameter | 18 in | 18 in | 18 in |
| Wheel Speed (Approx | 700 rpm | 900 rpm | 900 rpm |
| Weight | 765 lb. | 775 lb. | 840 lb. |

| TILLER – WOODS EQUIPMENT CORP. OR EQUAL | TL 73 | TL 84 |
| --- | --- | --- |
| Overall Width | 86 in | 97 in |
| Cutting Width | 73 in | 84 in |
| Working Depth | 6 in | 6 in |
| Overall Height | 31 in | 31 in |
| Number of Tines | 36 | 40 |
| Tine Rotation | Bi-directional | Bi-directional |
| Weight | 1050 lb. | 1228 lb. |
| Driveline | (2) in-line gerotor motors | (2) in-line gerotor motors |
| Maximum Tine Speed | 121 rpm | 121 rpm |
| Max Flow | 25 gpm @ 2000 psi | 46 gpm @ 3500 psi |

| TREE SPADE – FFC ATTACHMENTS OR EQUAL | TS36 | TS40 | TS42 | TS44 | TS48 |
| --- | --- | --- | --- | --- | --- |
| Maximum Ball Size | 36 in | 40 in | 42 in | 44 in | 48 in |
| Weight | 258 lb. | 312 lb. | 360 lb. | 378 lb. | 425 lb./ |

| TRENCHER – ATTACHMENT TECHNOLOGIES INC. OR EQUAL | 615 | 625 | 650C |
| --- | --- | --- | --- |
| Boom Size | 36 in | 48 in | 48 in |
| Trench Depth @ Recommended Angle | 36 in | 48 in | 48 in |
| Chain Width | 6 in | 6 in | 6 in |
| Recommended Trenching Angle | 65 degrees | 65 degrees | 65 degrees |
| Length | 65 in | 86 in | 84 in |
| Width | 42 in/50.5 in | 53 in | 43 in |
| Height | 28 in | 32 in | 37 in |
| Spoil Discharge Reach | 24 in | 18 in | 27 in |
| Weight | 495 lb/775 lb | N/A | N/A |

ADDENDUM #2

707EC020

OPEN END CONTRACT

SKID STEER LOADER WITH ATTACHMENTS

CHANGES TO BIDDER’S EVALUATION REPORT:

X5.1	NO CHANGE REQUIRED

Price for loader only in quantities of		1-5		_______________ per unit

6-10		_______________ per unit

11 and over	_______________ per unit

Prices for loader and all attachments

In quantities of				1-5		_______________ per unit

6-10		_______________ per unit

11 and over	_______________ per unit

FROM:

X8.4.2	Does unit have high flow hydraulic system providing adequate flow and pressure for 	specified attachments					_____ YES _____ NO

TO:

X8.4.2	Does unit have high flow hydraulic system		_____ YES _____ NO

GPM: __________

DELETE:

X9.3	Is a remote attachment control device available for specified attachments (marked by 	an “*”) to start the loader and operate the attachment from the outside the operator 	control area						_____ YES _____ NO

RENUMBER:

X9.4

To	Is a single control unit provided which will control all available attachments

X9.3									_____ YES _____ NO

DELETE AS WRITTEN:

X9.5

And 		Attachments and pricing:

Sub

Topics

9.5.1

To and

Including

9.5.54

ADD:

X9.4

And		Are you supplying all attachments as listed in the specifications?

Sub									_____ YES _____ NO

Topics

9.4.1

Through

9.4.32

As follows:

X9.4	ATTACHMENTS:

X9.4.1	Does the AUGER you are providing meet or exceed the specification?

_____ YES _____ NO

Manufacturer:  __________________________________________

|  | MODEL: | MODEL: |
| --- | --- | --- |
| Auger | $ | $ |
| BITS – HEX: |  |  |
| 6” X 50” Head | $ | $ |
| 12” x 50” Head | $ | $ |
| 24” x 50” Head | $ | $ |
| SINGLE FLIGHT EXTENSIONS: |  |  |
| 12” Extension | $ | $ |
| 24” Extension | $ | $ |
| 48” Extension | $ | $ |

TOTAL PRICE:			$ __________________	$ ________________

X9.4.2	Does the BACKHOE WITH 12 INCH BUCKET you are providing meet or exceed 	the specification?						_____ YES _____ NO

Manufacturer: ___________________________________________

|  | MODEL: | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- | --- |
| Bucket with 12 Inch Bucket | $ | $ | $ | $ |

TOTAL PRICE:	$______________  	$______________	$_____________  $ ____________

X9.4.3	Does the BACKHOE-MINI you are providing meet or exceed specifications?

_____ YES _____ NO

Manufacturer: ___________________________________________

|  | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- |
| Backhoe – Mini | $ | $ | $ |

TOTAL PRICE:	          $________________   	$ ________________    $ ________________

X9.4.4	Does the BLADE – DOZER you are providing meet or exceed specifications?

_____ YES _____ NO

Manufacturer: ____________________________________________

|  | MODEL: |
| --- | --- |
| Blade – Dozer | $ |

TOTAL PRICE:				$ _____________________

X9.4.5	Does the BOOM – MATERIAL HANDLING you are providing meet or exceed the 	specifications?	   			_____ YES _____ NO

Manufacturer: _____________________________________________

|  | MODEL: |
| --- | --- |
| Boom – Material Handling | $ |

TOTAL PRICE:				$ ________________________

X9.4.6	Does the BREAKER – HYDRAULIC you are providing meet or exceed the 	specifications?				_____ YES _____ NO

Manufacturer: _____________________________________________

|  | MODEL: |
| --- | --- |
| Breaker – Hydraulic | $ |

TOTAL PRICE:				$ ____________________________

X9.4.7	Does the BROOM – ANGLE – POLY/WIRE BRISTLES – WATER KIT WITH 	25 GALLON TANK you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: ______________________________________________

|  | MODEL: |
| --- | --- |
| Broom – Angle – Poly/Wire Bristles – Std. Manual Angle | $ |
| Optional Water Kit with 25 Gallon Tank | $ |
| Optional Hydraulic Angle | $ |

TOTAL PRICE:				$ ________________________________

X9.4.8	Does the BROOM – GENERAL PURPOSE PICK-UP you are providing meet 	or exceed the specifications?			_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Broom – General Purpose Pick-Up | $ |

TOTAL PRICE:				$ _________________________________

X9.4.9	Does the BRUSH CUTTER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Brush Cutter | $ |

TOTAL PRICE:				$ _________________________________

X9.4.10	Does the BUCKET – BRUSH GRAPPLE you are providing meet or exceed 	specifications?				_____ YES _____ NO

Manufacturer: ________________________________________________

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Bucket – Brush Grapple | $ |

TOTAL PRICE:				$ _________________________________

X9.4.11	Does the BUCKET – FORKED SCRAP GRAPPLE you are providing meet or 	exceed specifications?				_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Bucket-Forked Scrap Grapple | $ |

TOTAL PRICE:				$ _________________________________

X9.4.12	Does the BUCKET – GENERAL PURPOSE you are providing meet or exceed the 	specifications?				_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- | --- |
| Bucket – General Purpose | $ | $ | $ | $ |
| Optional Teeth | $ | $ | $ | $ |
| Optional Bolt on Cutting Edge | $ | $ | $ | $ |
| Optional Bolt on Toothbar Inside Bucket Width | $ | $ | $ | $ |

(NOTE: ADD ALL LINES FOR EVALUATION PURPOSES)

TOTAL PRICE	$ _____________	$ ____________	$ ____________	$ _____________

X9.4.13	Do the BUCKETS – GENERAL PURPOSE UTILITY & LIGHT MATERIAL 	meet or exceed the specifications?			_____ YES _____ NO

Manufacturer: ________________________________________________

|  | MODEL (GPU): | MODEL (LM): | MODEL (LM): | MODEL (LM): |
| --- | --- | --- | --- | --- |
| Bucket (GPU) | $ |  |  |  |
| Bucket (LM) |  | $ | $ | $ |
| Optional Bolt on Cutting Edge | $ | $ | $ | $ |
| Optional Bolt on Toothbar Inside Bucket Width | $ |  |  |  |

(NOTE: ADD ALL LINES FOR EVALUATION PURPOSES)

TOTAL PRICE	$ _____________	$ _____________	$ ____________	$ ____________

X9.4.14	Does the BUCKET – HEAVY DUTY SCRAP GRAPPLE you are providing meet 	or exceed the specifications?			_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: |
| --- | --- | --- |
| Bucket – Heavy Duty Scrap Grapple | $ | $ |
| Optional Bolt on Cutting Edge | $ | $ |

(NOTE: ADD ALL LINES FOR EVALUATION PURPOSES)

TOTAL PRICE:			$ ____________________	$ ___________________

X9.4.15	Does the BUCKET – MULTI PURPOSE you are providing meet or exceed the 	specifications?					_____ YES _____ NO

Manufacturer: ________________________________________________

|  | MODEL: | MODEL: |
| --- | --- | --- |
| Bucket-Multi Purpose | $ | $ |
| Optional Bolt on Reversible Cutting Edge | $ | $ |
| Optional Bolt on Toothbar Inside Bucket Width | $ | $ |

(NOTE: ADD ALL LINES FOR EVALUATION PURPOSES)

TOTAL PRICE:			$ ______________________	$ _____________________

X9.4.16	Does the BUCKET – ROCK you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: ____________________________________________

|  | MODEL: |
| --- | --- |
| Bucket – Rock | $ |

TOTAL PRICE:				$ _________________________________

X9.4.17	Does the COLD PLANER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- | --- | --- |
| Cold Planer | $ | $ | $ | $ | $ |

TOTAL

PRICE:		$_________	$__________	$_________	$_________	$ __________

X9.4.18	Does the CONCRETE CLAW you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Concrete Claw | $ |

TOTAL PRICE:				$ _________________________________

X9.4.19	Do the FORKS – PALLET you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Forks – Pallet | $ |

TOTAL PRICE:				$ _________________________________

X9.4.20	Does the GRAPPLE – LOG FORK you are providing meet or exceed the 	specifications?				_____ YES _____ NO

Manufacturer: ______________________________________________

|  | MODEL: |
| --- | --- |
| Grapple-Log Fork | $ |

TOTAL PRICE:				$ _________________________________

X9.4.21	Does the HITCH – THREE POINT you are providing meet or exceed the 	specifications?				_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Hitch-Three Point | $ |

TOTAL PRICE:				$ _________________________________

X9.4.22	Does the POWER RAKE you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Power Rake | $ |
| Manual Angling | $ |
| Hydraulic Angling | $ |

TOTAL MANUAL ANGLING PRICE:	$ _________________________________

TOTAL HYDRAULIC ANGLING PRICE:	$ _________________________________

X9.4.23	Does the PREPARATOR you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Preparator | $ |

TOTAL PRICE:				$ _________________________________

X9.4.24	Does the ROCK WHEEL WITH 50 GALLON WATER KIT you are providing 	meet or exceed the specifications?			_____ YES _____ NO

Manufacturer: ______________________________________________

|  | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- |
| Rock Wheel with 50 Gallon Water Kit | $ | $ | $ |

TOTAL PRICE:		$ _________________	$ ________________	$ _______________

X9.4.25	Does the ROLLER – VIBRATORY you are providing meet or exceed the 	specifications?				_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: |
| --- | --- | --- |
| Roller – Vibratory | $ | $ |
| Smooth Drum | $ | $ |
| Padded Drum | $ | $ |

TOTAL SMOOTH DRUM:      $ _____________________	$ ____________________

TOTAL PADDED DRUM:	$ _____________________	$ ____________________

X9.4.26	Does the SCARIFIER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Scarifier | $ |

TOTAL PRICE:				$ _________________________________

X9.4.27	Does the SNOW BLADE you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: |
| --- | --- |
| Snow Blade | $ |

TOTAL PRICE:				$ _________________________________

X9.4.28	Does the SNOW BLOWER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: |
| --- | --- | --- |
| Snow Blower | $ | $ |

TOTAL PRICE:			$ _____________________	$ ____________________

X9.4.29	Does the STUMP GRINDER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- |
| Stump Grinder | $ | $ | $ |

TOTAL PRICE:		$ ________________	$ _______________	$ _______________

X9.4.30	Does the TILLER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: |
| --- | --- | --- |
| Tiller | $ | $ |

TOTAL PRICE:			$ ____________________	$ ___________________

X9.4.31	Does the TREE SPADE you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- | --- | --- |
| Tree Spade | $ | $ | $ | $ | $ |

TOTAL

PRICE:		$_________	$ _________	$ __________	$ _________	$_________

X9.4.32	Does the TRENCHER you are providing meet or exceed the specifications?

_____ YES _____ NO

Manufacturer: _______________________________________________

|  | MODEL: | MODEL: | MODEL: |
| --- | --- | --- | --- |
| Trencher | $ | $ | $ |

TOTAL PRICE:		$ ________________	$ _______________	$ ______________

GRAND TOTAL FOR ALL ATTACHMENTS: 	$ ____________________________