WEST VIRGINIA DEPARTMENT OF TRANSPORTATION

DIVISION OF HIGHWAYS

EQUIPMENT DIVISION

BIDDER'S EVALUATION REPORT

PROCUREMENT SPECIFICATIONS FOR OPEN END CONTRACT

NO. 131-1-F

OPEN END CONTRACT

2 WHEEL DRIVE UTILITY TRACTOR WITH UNIVERSAL

MID MOUNTED ARTICULATED BOOM MOWER/

GRASS ROTARY MOWER/SIDE FLAIL MOWER

NOTE TO BIDDER:    Procurement Specification No. 131-1-F, Paragraph 2.0 recommends the completion and submittal of this Report with your bid.  Purpose of this Report is to enable the West Virginia Division of Highways Evaluation Committee to make full and fair evaluation of the bid.  Addendums in order, along with exception sheets, should be with Bidder’s Evaluation Report.

FAILURE TO SUBMIT THIS REPORT, COMPLETE IN ITS ENTIRETY, MAY SUBJECT THE BIDDER

TO DISQUALIFICATION.

Reference Requisition No.: ______________________

Bidder's Name:____________________________________________________________

Address:__________________________________________________________________

Telephone Number:_________________________________________________________

Years Bidder has been registered to do business with the State of West Virginia:  ______________YRS.

Years Company has been an authorized dealer for proposed unit:                        _______________YRS.

X3.2	Have you complied with all mandatory specifications noted in bold print?	_____ YES _____ NO

X4.2   	DELIVERY:

X4.2.1 	Delivery date of completed representative unit:________________ Calendar Days After Date of                    										Purchase Agreement

X4.2.2 	Delivery date of balance of completed units:  ________________ Calendar Days After Date of

Purchase Agreement

X5.0	AWARD CRITERIA;

X5.1	Prices for COMPLETE 2 WHEEL DRIVE UNIT in quantities:

1-5		________________per unit

6-10 		________________per unit

11-20		________________per unit

21 and over	________________per unit

OPTIONS:

2 WHEEL DRIVE

Utility Tractor Only:						1-5		____________ per unit

6-10		____________ per unit

11-20		____________ per unit

21 and over	____________ per unit

Universal Mid Mounted Articulated Boom Mower Only:

1-5 		____________ per unit

6-10		____________ per unit

11-20		____________ per unit

21 and over	____________ per unit

Grass Rotary Mower Only:					1-5		____________ per unit

6-10		____________ per unit

11-20		____________ per unit

21 and over	____________ per unit

Side Flail Mower Only:					1-5		____________ per unit

6-10		____________ per unit

11-20		____________ per unit

21 and over	____________ per unit

X6.0   SPECIFICATIONS - GENERAL

X6.1   Manufacturer, model, series, and date of manufacture of proposed complete unit:

________________________________________________________________________

________________________________________________________________________

________________________________________________________________________

________________________________________________________________________

Is descriptive literature, fully describing proposed unit attached to your bid? _____ YES _____ NO

If not, why?______________________________________________________________

X6.2	Will the required number of service manuals, and complete parts list be delivered to the 	Equipment Division at Buckhannon upon completion of delivery of total units?

_____ YES _____ NO

Will the required Equipment Preventive Maintenance Form (Section X6.2 of Bidders Evaluation Report) be provided upon inspection of the pilot unit?			_____ YES _____ NO

X6.2

2-10-00

EQUIPMENT PREVENTATIVE MAINTENANCE QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY SUCCESSFUL BIDDER OR MANUFACTURER’S TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT MODEL TO THE WVDOH.

DESCRIPTION: _______________________________________	MAKE: ___________________________________

MODEL: ________________________    	YEAR: __________	PURCHASE AMOUNT: ______________________

ENGINE:	MAKE: ______________________ 	MODEL: __________________ 	FUEL TYPE: ________________________

HORSEPOWER: _______________	CYLINDER: ________	ENGINE SERIAL: __________________________

COOLING SYSTEM CAPACITY: ______________________

BELTS:		DESCRIPTION:					PART NUMBERS:

___________________________________________	_________________________________________________

___________________________________________	_________________________________________________

GVW: _______________________AXLE CAPACITY:FRONT: ______________	REAR:______________

TIRES:		FRONT MAKE & SIZE: ______________________________________________

REAR MAKE & SIZE: _______________________________________________

DIMENSIONS OF UNIT:	LENGTH: __________		WIDTH: ______________	LENGTH: ___________

VENDOR CONTACT PERSON: ____________________________________		PHONE: __________________________

PARTS:

BATTERY MAKE: ____________________	MODEL: ___________________		CCA: _______________________

TOP OR SIDE POST: __________________	DIMENSIONS: LENGTH ________ WIDTH ________ HEIGHT __________

SPARK PLUGS OR FUEL INJECTORS MAKE: ______________	PART # __________________________________________

FUEL PUMP OR INJECTION PUMP MAKE: ________________	MODEL: _________________________________________

ALTERNATOR MAKE: __________________________________	PART #:__________________________________________

STARTER MAKE: ______________________________________	PART #: _________________________________________

TURBO CHARGER MAKE: ______________________________	PART #: _________________________________________

TRANS. MAKE: ____________________	MODEL: _________________________   AUTO/MANUAL: ____________________

HYDRAULIC PUMP MAKE: _____________________________	MODEL: _________________________________________

FILTERS		MAKE	PART NO.		LUBRICANT		MANUFACTURER TYPE

OIL		__________________________________	ENGINE	__________________________________________

AIR INNER	__________________________________	TRANSMISSION__________________________________________

AIR OUTER__________________________________	POWER STEERING _______________________________________

FUEL PRIMARY ______________________________	HYDRAULIC  	__________________________________________

FUEL SECONDARY ___________________________	DIFFERENTIALS _________________________________________

COOLANT	__________________________________	BRAKE FLUID 	__________________________________________

HYDRAULIC	_______________________________	COOLANT	__________________________________________

OTHER		__________________________________ 	OTHER 	__________________________________________

X6.3	TRAINING:

Will training seminar be conducted on Preventive Maintenance, Operator and Mechanic Training                      								_____YES _____ NO

Will you conduct training with each purchase order against this open end contract?

_____ YES _____ NO

Will training be conducted within 2 working days from the delivery of the pilot unit on the individual purchase order?								_____ YES _____ NO

If NO, explain time frame_____________________________________________________________

Will an Operator’s Manual be furnished directly to Letha Lamb, Training Academy prior to the

delivery of the pilot?		_____ YES _____ NO

X6.4   	If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors, required in conducting the training?		         _____ YES _____ NO

X6.4.1    	Will all manuals, booklets, etc. explaining preventive maintenance, operator procedures, and service schedule be delivered with each unit?           			_____ YES_____NO

If NO, explain _____________________________________________________

X6.5	WARRANTY AND SERVICE POLICY

Will the warranty and service you provide comply with all areas as stated in Section 6.5 of specifications                               							_____ YES _____ NO

Is warranty literature attached?					_____ YES _____ NO

Is a minimum two (2) year bumper to bumper basic parts and labor warranty included?

_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

Is there a three (3) year bumper to bumper basic parts and labor warranty available_____YES_____NO

Describe: (Include cost and conditions)____________________________________________________

____________________________________________________________________________________

____________________________________________________________________________________

X6.5	WARRANTY AND SERVICE POLICY QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY THE SUCCESSFUL BIDDER

OR MANUFACTURERS TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT

MODEL TO THE WVDOH (If additional lines are needed, make copies of form.)

1. Define the terms of the standard warranty.  If not offered, so state.  (Attach copy)

2. Define warranty service to be performed at DOH facilities and warranty service to be performed at

manufacturer’s representative facility.  List name and location of manufacturer’s representative.

3. List locations for parts inventories that are within the State of West Virginia.  Also, list availability levels, if

known.

4. During the term of warranty, list the guarantee discount to manufacturer’s published list price for parts that

bidder will sell the parts to owner.

A.	Terms: Net 30	Manufacturer’s published list price less: __________% discount

B.	Terms: Net 60	Manufacturer’s published list price less: __________% discount

C.	Terms: Net 90	Manufacturer’s published list price less: __________% discount

5. During the term of warranty, will all manufacturers or engineering improvements be submitted to Division of

Highways?							_____ YES _____ NO

6. During the term of warranty, list the guaranteed rates charged for repair to the unit.

A.	Shop Rate		$ __________ per mechanic hour

B.	Travel Time Charge		$ __________ per mechanic hour

(Specify if one-way)		__________; port to port __________

C.	Mileage Charge		$__________ per vehicle mile

(Specify if one-way		__________; port to port __________

D.	Field Mechanic Rate		$__________ per mechanic hour

E.	Specify period of time that prices are in effect: __________________________

F.	Surcharge for miscellaneous items: ____________________%

X6.6 	EVALUATION COMMITTEE REQUIREMENTS

Is all component specifications, product literature, component models provided for Evaluation Committee bid determination?					_____ YES _____ NO

X6.7	Will all parts, equipment, accessories, material, design and performance characteristics not

specified herein, but which are necessary to provide a complete unit, be furnished with the unit

and conform in strength, quality of material, and quality of workmanship to those which are

advertised and provided to the market in general by the unit industry? _____YES _____NO

X6.7.1	Are all parts and accessories adequate and regularly supplied as standard to be included except

those which may be duplications of specifications herein, and except these by specification are not

to be furnished?                                        					_____YES _____NO

X6.7.2	Are all standard safety features that are required by Federal and State statutes of law included?                   											_____YES _____NO

X7.0	SPECIFICATIONS OF THE QUOTED UNIT – UTILITY TRACTOR

The bidder should complete the following schedule in order for the Division to compare the actual bid 	unit to the specifications.  Should the bidder except a requirement, then such exception may be only on 	the basis that such feature is not offered by the manufacturer.  The Division will have the sole 		discretion as to whether the bidder's substitution meets the requirements of the specifications.

Manufacturer: _______________________________	Model: _________________

X7.1	Tractor dry weight (without ballast): __________ lbs.

X7.2	Wheelbase:  __________ inches

X7.3	Is unit 2 wheel drive							_____ YES _____ NO

X7.4	Is the hood tilt up with manufacturers approved prop system	_____ YES _____ NO

X7.5	Is unit equipped with manufacturers lockable side panels		_____ YES _____ NO

X7.6	Can all daily services be done from ground level			_____ YES _____ NO

X7.7	Engine:

X7.7.1		Is engine manufacturers water cooled, diesel powered		_____ YES _____ NO

Manufacturer: ______________________	Model: __________________

X7.7.2		PTO Horsepower: __________

X7.7.3		Manufacturers standard governor with engine key shut off, wire sealed by manufacturer

_____ YES _____ NO

X7.8	Engine Lubrication System:

X7.8.1		Full pressure lubrication with oil filter and oil by pass system	_____ YES _____ NO

X7.8.2		Engine oil cooler							_____ YES _____ NO

X7.8.3		Is engine wet sleeved						_____ YES _____ NO

X7.9	Engine Cooling System:

X7.9.1		Pressurized cooling system with thermostat and by pass, supplied with Dex Cool Extended Life

protected to a freeze point of -34 degrees F			_____ YES _____ NO

X7.9.2		Is cooling system equipped with a coolant recovery tank and sight glass _____ YES _____ NO

X7.10	Air Induction System:

X7.10.1	Dry type dual element (2 stage) air cleaner with self dumping valve	_____ YES _____ NO

X7.10.2	Dash mounted air filter restriction indicator with light that is operator visible when service is 				required								_____ YES _____ NO

X7.11	Exhaust System:

X7.11.1	Is muffler under hood with  manufacturers approved vertical exhaust with rain and weather 				protection

_____ YES _____ NO

X7.12	Electrical System:

X7.12.1	Is unit electrical system manufacturers noise suppression wiring, 12 volts negative ground

_____ YES _____ NO

X7.12.2	Is neutral start switch (for safety purposes) provided			_____ YES _____ NO

X7.13	Charging System:

X7.13.1	Is charging system manufacturers heavy duty for model bid		_____ YES _____ NO

Manufacturer: _________________	Model: _____________

X7.14	Engine Fuel System:

X7.14.1	Is dual stage filtering provided						_____ YES _____ NO

X7.14.2	Is unit provided with a fuel water separator				_____ YES _____ NO

X7.14.3	If fuel tank is exposed, is manufacturers skid plate provided		_____ YES _____ NO

Is it manufactured in a manner that shall give the fuel tank maximum protection

____ YES ____ NO

X7.15	Lighting System:

X7.15.1	Two (2) high-low beam head light (halogen) with manufacturers heavy duty console mounted switch

_____ YES _____ NO

X7.15.2	Four (4) roof mounted work lights: two (2) front and two (2) rear	_____ YES _____ NO

X7.15.3	Fenders mounted rear tail lights and turn signals shock mounted	_____ YES _____ NO

X7.15.4	Four (4) roof mounted flashing warning lights; two (2) front and two (2) rear _____ YES _____ NO

X7.15.5	Unit provided with console and dome lighting				_____ YES _____ NO

X7.15.6	Unit has seven (7) terminal out socket to provide lighting for towed equipment ____ YES ____ NO

X7.15.7	Low profile high intensity dual flash strobe light mounted in front center of cab roof with

brush								_____ YES _____ NO

Does it meet Target Tech Model Multi-Flash 5X, 12/48 VDC, 11 Joules, generating no more

than .10 UV of interference on a radio receiver with 12 db of quieting_____ YES _____ NO

Manufacturer: ________________	Model: ____________

X7.15.8	OSHA approved back up alarm provided on unit				_____ YES _____ NO

X7.16	Unit Instrumentation:

X7.16.1	Tachometer								_____ YES _____ NO

X7.16.2	Speedometer								_____ YES _____ NO

X7.16.3	Hourmeter operable from engine operation not key switch		_____ YES _____ NO

X7.16.4	Coolant temperature indicator with audible buzzer or warning light	_____ YES _____ NO

X7.16.5	Oil pressure indicator with audible buzzer or warning light		_____ YES _____ NO

X7.16.6	Hydraulic oil temperature indicator with audible buzzer or warning light, to warn operator when

manufacturers recommended hydraulic oil temperature is exceeded	_____ YES _____ NO

X7.17	Clutch:

X7.17.1	Wet type, manufacturers heaviest duty available				_____ YES _____ NO

Manufacturer and Model: _______________________________________

X7.18	Transmission of the following design and arrangement:

X7.18.1	Power shift design mechanically controlled with left hand reverser	_____ YES _____ NO

X7.18.2	16 forward speeds		_____ YES _____ NO

X7.18.3	16 reverse speeds		_____ YES _____ NO

X7.18.4	Speed ranges 1.5 – 20 MPH	_____ YES _____ NO

X7.18.5	Transmission manual shift lever is console mounted	_____ YES _____ NO

X7.19	Differential has the following features:

X7.19.1	Differential manufacturers heavy duty		_____ YES _____ NO

X7.19.2	Manufacturers differential lock engagement and disengagement capability_____ YES _____ NO

X7.19.3	On-the-go differential lock engagement and disengagement capability	_____ YES _____ NO

X7.20	Axle:

X7.20.1	Front Axle:

X7.20.1.1		Front axle manufacturers heavy duty for use with boom mounted mower_____ YES _____ NO

X7.20.1.2		Front axle _____ degree oscillation

X7.20.2	Rear Axle:

X7.20.2.1		Rear axle _____ inches in diameter

X7.21	Planetary Final Drives:

X7.21.1	In board type		_____ YES _____ NO

X7.22	Tractor Hydraulic System:

X7.22.1	Hydraulic system provides sufficient pressure and flow to operate all tractor functions at peak 			efficiency								_____ YES _____ NO

Pressure and flow: ___________________________

X7.22.2	Tractor has control valves with three (3) detent position and flow	_____ YES _____ NO

X7.22.3	Hydraulic hoses can be coupled and uncoupled under pressure		_____ YES _____ NO

X7.23	Brakes:

X7.23.1	Recommended manufacturers emergency braking system provided_____ YES _____ NO

Manufacturer and Model: _______________________

X7.23.2	Hydraulic actuated service brakes					_____ YES _____ NO

X7.23.3	Wet type disc brakes							_____ YES _____ NO

X7.23.4	Self adjusting and equalizing						_____ YES _____ NO

X7.24	Wheels and Tires:

X7.24.1	Front Tires:	 ________________________________________

X7.24.2	Rear Tires: 	___________________________________________________

X7.25	Three Point Hitch:

X7.25.1	Hitch electro-hydraulically operated					_____ YES _____ NO

X7.25.2	Hitch has external switch to control raising and lowering from rear of tractor for safety

purposes								_____ YES _____ NO

X7.25.3	Three point hitch is a category 2 type					_____ YES _____ NO

X7.25.4	Hitch lift capacity __________ lbs. at _____ inches behind lift point

X7.26	Cab and Related Accessories:

X7.26.1	Cab has OSHA approved ROPS					_____ YES _____ NO

X7.26.2	Cab is insulated and pressurized						_____ YES _____ NO

X7.26.3	Cab mounted by the manufacturer					_____ YES _____ NO

X7.26.4	Cab unit equipped with heater, defroster, and air conditioning installed by manufacturer

_____ YES _____ NO

X7.26.5	Cab has safety glass, tinted at all locations				_____ YES _____ NO

X7.26.6	Cab has two (2) lockable entry doors keyed alike: one (1) left and one (1) right ____ YES ____ NO

X7.26.7	Seat is cloth covered type protected with scotchguard (or equal) and equipped with a seat belt

_____ YES _____ NO

X7.26.8	Seat has a height and weight adjustment and swivel left and right _____ degrees for easier operation

_____ YES _____ NO

X7.26.9	Seat equipped with adjustable arm rests					_____ YES _____ NO

X7.26.10	Cab and tractor provided with a type of non-skid step (or steps) and hand holds for safety purposes

_____ YES _____ NO

X7.26.11	Unit equipped with a tilt/telescoping steering wheel			_____ YES _____ NO

X7.26.12	Unit equipped with a first aid kit mounted inside of cab			_____ YES _____ NO

X7.26.13	Tool box provided, weather resistant, lockable, and mounted for operator convenience

_____ YES _____ NO

X7.26.14	Cab unit has front and rear windshield wipers and washers		_____ YES _____ NO

X7.26.15	Left and right side rear view mirrors and in cab rear view mirror provided _____ YES _____ NO

X7.26.16	All features that are considered manufacturers standard equipment that are not specifically 			addressed are provided							_____ YES _____ NO

X7.26.17	Unit will be delivered to WVDOH with all manufacturers recommended safety related decals 			and safety features intact						_____ YES _____ NO

X7.27	PTO:

X7.27.1	PTO RPM: __________

X7.27.2	PTO can be engaged and disengaged on-the-go				_____ YES _____ NO

X7.28	Paint:

X7.28.1	Tractor is painted manufacturers standard color				_____ YES _____ NO

X8.0	20 FOOT UNIVERSAL MID MOUNTED ARTICULATED HYDRAULIC POWERED BOOM 	MOWER:

Will the 20 Foot Universal Mid Mounted Articulated Hydraulic Powered Boom Mower with Universal

Frame and Hitch Assembly allow the use of a 60 Inch Side Mounted Short Arm Rotary Grass Mower or

a 74 Inch Side Mounted Flail							_____ YES _____ NO

Manufacturer: __________________________	Model: ____________________

Is a minimum two (2) year bumper to bumper basic parts and labor warranty included with the 	boom 	mower?								_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

Is a three (3) bumper to bumper basic parts and labor warranty available 	_____ YES _____ NO

Describe (include costs and conditions):___________________________________________________

___________________________________________________________________________________

X8.1	Frame:

X8.1.1		Is frame mid mounted to under side of tractor utilizing a modular center weldment with 			attaching rails adequately secured to the front bolster and rear axle (specifically excluding

frame work bolting to the bell housing of the tractor) 		_____ YES _____ NO

X8.1.2		Is frame modular construction from alloy steel				_____ YES _____ NO

X8.1.3		Does frame mount provide for unrestricted movement of the boom and offer limited 				obstructions to forward vision						_____ YES _____ NO

X8.1.4		Fore and aft boom swing spindle pin bottom of pin to ground distance __________ inches

X8.1.5		Is unit counterweighted to maintain the most possible ground pressure of tires on opposite side of 			mower during all reach out, up and down operations of boom with specified head

_____ YES _____ NO

X8.2	Hydraulic Reservoir:

X8.2.1		Manufacturer’s properly sized hydraulic oil reservoir that is capable to operate all mower functions 			including forward, aft, up, down, and rotary head.			_____ YES _____ NO

X8.2.2		Tank has a built-in oil level sight glass and thermometer		_____ YES _____ NO

X8.2.3		Hydraulic filter capable of providing suitable filtration for system	_____ YES _____ NO

X8.2.4		Tank is equipped with a shut off valve for closing when changing filter or hoses and for

draining of tank								_____ YES _____ NO

X8.2.5		Unit is equipped with front piston type pump(s) to operate all mower functions (boom, rotary 			grass and flail) at maximum operation within manufacturer’s temperature range excluding the 		use of the tractor hydraulics						_____ YES _____ NO

X8.2.6		Hydraulic GPM: __________	Is it manufacturers specified to operate all mower functions at 			maximum efficiency							_____ YES _____ NO

X8.2.7		Front pump(s) are idle during transport				_____ YES _____ NO

X8.2.8		All circuit hoses _____ inch _____ wire braid

X8.2.9		All hoses routed through conduit and securely fastened for best brush protection

_____ YES _____ NO

X8.2.10	Deck hoses four (4) wire braid fitted with cordura sleeving for brush protection

_____ YES _____ NO

X8.2.11	Mower controls five (5) section valve controlled through a single electronic joystick

_____ YES _____ NO

X8.2.12	Valve allows _____ functions simultaneously

X8.2.13	Swing, lift, and dipper section have individual relief valves to give breakaway protection

_____ YES _____ NO

X8.2.14	Mower cutter has a 6 second emergency shut down			_____ YES _____ NO

X8.2.15	Mower head motor takes 6 seconds to wind up to full RPM for a no-shock-load-startup

_____ YES _____ NO

X8.2.16	Cylinders mounted in such a way that breakaway forces are transmitted to the barrel side of cylinder 			and not the rod side							_____ YES _____ NO

X8.3	Boom Rest:

X8.3.1		A boom rest is mounted to mower frame to cradle boom during transport

_____ YES _____ NO

X8.3.2		Boom rest takes pressure off all cylinders when in transport		_____ YES _____ NO

X8.3.3		When in stow, tractor and mower _____ inches with _____ inch rotary and _____ foot high

X8.4	Safety Cage:

X8.4.1		Safety cage is installed on right side and top of operator’s position and a sloping guard or rail 			over entire hood area							_____ YES _____ NO

X8.4.2		Cage is constructed of expanded metal and permanently mounted to tractor _____ YES _____ NO

X8.4.3		A 1/2 inch lexon safety glass window is part of the safety cage	_____ YES _____ NO

This window covers the door window and hinged mounted so that it and the tractor window can be 			cleaned								_____ YES _____ NO

Are there any bungee straps	_____ YES _____ NO

Meets OSHA safety standards	_____ YES _____ NO

X8.5	Boom:

X8.5.1		Is boom two (2) piece design with all pivot points having replaceable steel bearings

_____ YES _____ NO

X8.5.2		Pivot pins _____ inch diameter

X8.5.3		Inner boom made of _____ inch x _____ inch _____ inch steel tubing

Minimum __________ lb/sq. inch yield strength

X8.5.4		Dipper boom made of _____ inch x _____ inch x _____ inch steel tubing

Minimum __________ lb/sq. inch yield strength

X8.5.5		All hinge points are T-1 steel reinforcement			_____ YES _____ NO

X8.5.6		Boom swing from stow position _____ degrees forward

X8.5.7		Boom reach up:  ________________

X8.5.8		Boom reach out: __________ from tractor centerline to outside edge or cutting blade arc

X8.5.9		Boom reach down: __________ below tractor ground level

X8.5.10	Boom mower head capable of mowing within _____ inches of rear tractor tire allowing tractor to 			stay further out of traffic lane					_____ YES _____ NO

X8.6	Brush Head:

X8.6.1		Cutting width: __________ inches

X8.6.2		Top deck made of ________________________

X8.6.3		Side skirts _____ inch steel

X8.6.4		Top deck reinforced with channel frame with a reinforced spindle mount plate ____ YES ____ NO

X8.6.5		Deck has replaceable full length skid shoes		_____ YES _____ NO

X8.6.6		Spindle bearing are tapered roller type in a sealed housing	_____ YES _____ NO

X8.6.7		Blade are _____ inches wide x _____ inches thick double edge tempered steel and full swing 			360 degree								_____ YES _____ NO

X8.6.8		Blade bolts _____ inch x _____ heat treated, grade _____ shoulder bolt with a castel nut and 			roll pin								_____ YES _____ NO

X8.6.9		Mower is direct drive, splined and totally enclosed excluding chain or flex couplers

_____ YES _____ NO

X8.6.10	Motor is cast steel and sized to match the hydraulic pump proposed by mower manufacturer

_____ YES _____ NO

X8.6.11	Front safety shield, hydraulic actuated, center feed metal door is operational from joystick control

_____ YES _____ NO

X8.6.12	Cutter deck rotation __________ degrees

X8.6.13	Rear shield rubber/fabric material		_____ YES _____ NO

X8.7	Complete unit will be delivered with all manufacturers’ safety features intact ____ YES _____ NO

X8.8	Mower is manufacturer’s standard color		_____ YES _____ NO

X8.9	Unit is interchangeable with short boom rotary grass mower and 74 inch side mounted flail 	mower									_____ YES _____ NO

X9.0	SIDE MOUNTED HYDRAULICALLY POWERED 60 INCH ROTARY M0WER (GRASS ROTARY 	MOWER):

Manufacturer: ____________________________	Model: ____________________

Is a minimum two (2) year bumper to bumper basic parts and labor warranty included with the 	grass 	rotary mower?							_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

Is a three (3) year bumper to bumper basic parts and labor warranty available _____ YES _____ NO

Describe (include costs and conditions): ___________________________________________________

____________________________________________________________________________________

X9.1	Mower Lift Assembly:

X9.1.1		Mower capable of mowing from _____ degrees up to _____ degrees down

X9.1.2		Mower capable of raising _____ inches vertically _____ inches below grade

X9.2	Deck:

X9.2.1		Cutting width: __________

X9.2.2		Deck material:

X9.2.2.1		Deck: _____ inch

X9.2.2.2		Reinforcing frame: _____ inch x _____ inch channel

X9.2.2.3		Side skirt: _____ inch thick

X9.2.2.4		Skid shoes: Full length, replaceable		_____ YES _____ NO

X9.2.2.5		Trash deflector: Chain, full length standard front and rear	_____ YES _____ NO

X9.3	Spindle:

X9.3.1		Alloy steel, tapered roller bearings, bottom in oil bath	_____ YES _____ NO

X9.3.2		Spindle housing cast steel unibody	_____ YES _____ NO

X9.4	Motor to Spindle Drive:

X9.4.1		Splined coupler, direct drive enclosed (specifically excluding chain or dodge couplers)

_____ YES _____ NO

X9.5	Blade Bar and Blades:

X9.5.1		Single leaf _____ inch x _____ inch x _____ inch

X9.5.2		Blades:  Full swing 360 degrees _____ YES _____ NO

Size _____ inch x _____ inch x _____ inch heat treated up draft, alloy steel _____YES _____ NO

X9.5.3		Blade bolts:  Forged with nut and lock washer, heat treated shouldered	_____ YES _____ NO

X9.6	Optional Equipment:

X9.6.1		Tail wheel assembly			_____ YES _____ NO

X9.6.2		Tires are laminated			_____ YES _____ NO

X9.6.3		Unit is interchangeable with 20 foot boom brush mower and 74 inch side mounted flail mower

_____ YES _____ NO

X9.6.4		Do you have a wet blade system for extended and short booms		_____ YES _____ NO

If so, cost : _______________________________________________________________________

X9.7	Paint:

X9.7.1		Manufacturer’s recommended paint preparation and standard color	_____ YES _____ NO

X9.8	Does unit meet or exceed OSHA requirements	_____ YES _____ NO

X9.9	Advertising:  Does unit comply with advertising requirements	_____ YES _____ NO

X9.10	Preventive Maintenance and Operating Orientation/Training:

X9.10.1	Describe orientation seminar and will you furnish all training aids

____________________________________________________________________________

____________________________________________________________________________

X10.0	74 INCH SIDE FLAIL MOWER:

Manufacturer: ____________________________	Model: ____________________________

Is a minimum two (2) year bumper to bumper basic parts and labor warranty included with the 	side flail mower?								_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

Is a three (3) year bumper to bumper basic parts and labor warranty available _____ YES _____ NO

Describe (include costs and conditions): ___________________________________________________

___________________________________________________________________________________

X10.1	Does mower have electronic positive wing transport lock, activated from inside cab

_____ YES _____ NO

X10.2	Does shoulder mower have electric on/off control with starter interrupt within easy reach of 	operator								_____ YES _____ NO

X10.3	Does mower cutter bar have a 6 second emergency shut down		_____ YES _____ NO

X10.4	Does mower head take 6 seconds to wind up to full RPM, no shock	_____ YES _____ NO

X10.5	Width of swath _____ inches

X10.6	Is cutting height adjustable from 1/2 inch to 6 inches			_____ YES _____ NO

X10.7	Cutter shaft _____ inch O.D. x _____ inch I.D. certified D.O.M. steel tube _____ YES _____ NO

X10.8	Are cutter shaft bearings high speed double roller bearing, self aligning, greaseable with labyrinth 	type self purging seal							_____ YES _____ NO

X10.9	Severe duty 4 oz. flail knives		_____ YES _____ NO

X10.10	 Is drive direct drive			_____ YES _____ NO

X10.11 Is cutter housing constructed entirely of T-1 steel	_____ YES _____ NO

X10.12 Rear roller ______ inches diameter, _____ inch wall with greaseable _____ inch bronze bushings

_____ YES _____ NO

X10.13 Is hydraulic motor commercial series with double tapered roller bearings for superior support to input 	shaft									_____ YES _____ NO

X10.14 Is electronic joystick adjustable, analog proportional 2 axis control 	_____ YES _____ NO

X10.15 Are all hinge pins heat treated _____ YES _____ NO	Steel: __________________________

X10.16	 Tilt cylinder mounted to a parallel linkage to allow continuous head angle throughout the full range of 	lift and 200 degrees at head tilt						_____ YES _____ NO

X10.17	Cylinders are heavy duty type with welded barrel and be externally threaded for screw on gland 	retainer rings								_____ YES _____ NO

X10.18	 Cylinders are internally cushioned on both ends of travel and have Teflon piston seals

_____ YES _____ NO

X10.19 Tilt cylinder _____ inches I.D. x _____ inch wall with _____ inch rod

X10.20 Lift cylinder _____ inches I.D. x _____ inch wall with _____ inch rod

X10.21	 Unit is interchangeable with short boom rotary grass mower and boom brush mower

_____ YES _____ NO

X10.22	 Paint:

X10.22.1	Manufacturer’s recommended paint preparation and standard color	_____ YES _____ NO

X10.23	 Does unit meet or exceed OSHA requirements	_____ YES _____ NO

X10.24	 Does unit comply with advertising requirements	_____ YES _____ NO

X10.25 Preventive Maintenance and Operators Orientation/Training:

X10.25.1	Describe orientation seminar and will you furnish all training aids

______________________________________________________________________________

______________________________________________________________________________