10-24-08

To furnish all labor, materials and equipment necessary to supply WINTER GRADE BITUMINOUS PATCHING MIXTURE (Standard and/or Modified) in the estimated quantities and at the locations specified in the bid schedules.

- SPECIFICATIONS

The following sections of the West Virginia Department of Transportation, Division of Highways' Standard Specifications Roads and Bridges, adopted 2000 and the current Supplemental Specifications, shall apply to the administration of this Contract:  Sections 101, 102.4, 102.5, 105.1, 105.3, 105.4, 105.10, 105.11, 105.12, 105.13, 106.3, 106.4, 106.5, 106.6, 106.7, 106.9, 107.1, 107.2, 107.3, 107.14, 107.19, 107.20, 108.8, 109.1, 109.2 and 109.20.

The requirements of the West Virginia Department of Transportation, Division of Highways', Standard Specifications Section 109.20, PRICE ADJUSTMENT FOR LOAD LIMIT VIOLATIONS shall apply to all material supplied under this contract.  This will include material loaded by the vendor into Division of Highways owned and/or rented trucks.

"Contractor" and "Vendor" used in the above specifications of this contract are interchangeable.  Contractor shall mean Vendor and Vendor shall mean Contractor.

West Virginia Department of Transportation, Division of Highways' Standard Specifications Roads and Bridges, adopted 2000 and the current Supplemental Specifications may be obtained from:

West Virginia Division of Highways

Engineering Division, Technical Section

State Capitol Complex

Building 5, Room A-650

Charleston, West Virginia  25305-0430

DESCRIPTION

The patching material shall be composed of a suitable aggregate plant mixed with a liquid asphalt material and chemical additives. The asphalt material with additives shall be capable of coating the aggregate without stripping.  The material shall maintain adhesive qualities for all moisture conditions in the patched areas, except those having standing water.

MATERIALS

AGGREGATE

The coarse aggregate shall be a clean material consisting of crushed stone, crushed gravel or slag, meeting the requirements of the Division of Highways' Standard Specifications subsections 703.1, 703.2 and 703.3 respectively.  Fine aggregate shall meet the requirements of the Division of Highways’ Standard Specifications meet the requirements of the Division of Highways' Standard Specifications subsection 702.3.  The gradation of the final mixture shall be the same as the Vendor's currently approved plant mix formula for Type 1 Hot-Mix Asphalt Wearing Course when Standard Winter Grade Bituminous Patching Mix is being produced.

When Modified Winter Grade Bituminous Patching Mix is being produced, the aggregate gradation shall be as recommended by the supplier of the liquid asphalt with additives.  Allowable standard aggregate sizes shall be #8, #89, #9, or a blend of these sizes.

The gradation shall be determined in accordance with AASHTO T-27 and T-11.

The aggregate fraction of the final mixture shall meet the crushed particle requirements of Subsection 703.2.2 of the Division of Highways' Standard Specifications.  Questionable aggregates shall be tested as per MP 703.00.21, except the No. 8 sieve will be used.

ASPHALT MATERIAL

1.	Standard Winter Grade Bituminous Patching Mix

The asphalt material shall conform to the requirement of the West Virginia Division of Highways' Standard Specifications, Subsection 705.1.  Tests conducted by the supplier shall be presented to the respective Division of Highways District Materials Engineers/Supervisors for review prior to production of Standard Winter Grade Bituminous Patching Mix.  This liquid asphalt shall also contain a minimum of 2.5% chemical anti-stripping additive.

or,

2.	Modified Winter Grade Bituminous Patching Mix

The asphalt material shall be liquid asphalt with a chemical anti-stripping additives conforming to the requirements of AASHTO M82 or as modified to meet the requirements of the asphalt supplier.  The asphalt shall contain a minimum of 2.5% chemical anti-stripping additive.

Results from the following test methods and any additional tests conducted by the supplier shall be presented to the respective Division of Highways District Materials Engineer/Supervisor for review prior to production of Modified Winter Grade Bituminous Patching Mix.

Modified Asphalt Test

- Flash Point °C (°F)-AASHTO T79

- Kinematic Viscosity in cSt at 60°C (140°F)

Requirement – 350 to 500 cSt-AASHTO T201

- Water (%)-Requirement-0.2% maximum-AASHTO T55

- Distillate Test-AASHTO T78

% To 225oC (437oF)

% To 260oC (500oF)

% To 315oC (600oF)

Residue (%) at 360°C(680°F)

Residue Tests

- Ductility at 25°C(77°F)-AASHTO T51

- Solubility Test-AASHTO T44

COMPOSITION OF MIXTURE

The aggregates and asphalt material shall be combined in such proportions that the composition by weight of the finished mix shall meet the requirements of the plant mix formula.

The aggregate fraction of the mixture shall be evaluated in accordance with AASHTO T-27 and T-11, and shall meet the requirements of the plant mix formula range.  Any material failing to meet specification requirements on any sieve shall not be approved.

The asphalt fraction of the Standard Winter Grade Bituminous Patching Mix shall be a minimum of 5.0% when low-absorptive aggregates (<1.5%) are used and a minimum of 6.0% when high-absorptive aggregates (>1.5%) are used.

For Modified Winter Grade Bituminous Patching Mix the minimum amount of asphalt shall be as indicated in the table below.  The amount of asphalt for all Winter Grade Bituminous Patching Mixtures shall be sufficient to thoroughly coat the aggregate particles and provide enough adhesion to hold the compacted particles together under traffic conditions when properly placed and to assure that the aggregate particles remain sufficiently coated after stockpiling.

Minimum Asphalt Content for Modified Patching Mix

#89 or Blend

Aggregate Type		#8		of #8 & #9			#9

% AsphaltNote-1		5.0%		     5.5%			6.0%

Note-1:  Add a minimum additional 1.0% asphalt to

the above values for mixtures containing high-

absorptive aggregates (>1.5%)

PLANT MIX FORMULA

The plant mix formula for Modified Winter Grade Bituminous Patching Mix shall be in accordance with the recommendations of the supplier of the liquid asphalt with additives.  The plant mix formula composition report, which shall include the percentage of chemical anti-stripping additive, shall be forwarded to the District Materials Supervisor/Engineer before the mix is produced.

A plant mix formula for Standard Winter Grade Bituminous Patching Mix shall be developed in accordance with MP 401.02.22, and as modified by the Marshall Test Procedure described in AASHTO T-245 for cutback asphalts.  Initial submission of the proposed plant mix formula for Standard Winter Grade Bituminous Patching Mix will not be considered unless accompanied by sufficient test data developed by supplier to indicate that the formula being proposed can be met.  As a minimum, this test data shall include:  three separate gradations of samples taken from the hot bin, or separate gradations from cold bins or storage facility, the percentage of each material to be used and the calculated combined gradation.  The test data submitted shall have been developed from material that is to be used in the proposed mix.  Additional data which shall be submitted includes that described in MP 401.02.22.  This data will not be required to meet the limits given in the design property tables.  The air void content for Standard Winter Grade Bituminous Patching Material shall be 4-7 percent.

The proposed plant mix formula for Standard Winter Grade Bituminous Patching Mix shall be documented on Department Form T400 and together with plant calibration test data set forth above shall be forwarded to the District Materials Engineer/Supervisor.  The percentage of chemical anti-stripping additive shall be included in the documentation.  The T400 shall then be transmitted to the Materials Control and Testing Division for final review and revision.

CHANGES IN PLANT MIX FORMULA

Should the contractor at any time propose to change the source of aggregate in the mix, the definite asphalt content or change the source of the bituminous material, the provisions of the Division of Highways' Standard Specifications subsection 401.4.2 shall apply.

QUALITY CONTROL TESTING

Quality control is the responsibility of the contractor.  Quality control testing shall include daily asphalt content and gradation analysis of the design aggregate structure during production.  Since the aggregate and asphalt material are required to be measured separately and accurately to the proportions of the plant mix formula, the asphalt content may be determined by calculating the percentage by total weight of mix.  However, all standard methods of determining the asphalt content of the mixture that are allowed for hot-mix asphalt under Section 401 of the Division of Highways’ Standard Specifications are acceptable.  The ignition oven test method (AASHTO T308) would require an asphalt content correction factor, however, due to the low flash point of most asphalts used in Winter Grade Bituminous Patching Mix, this test method is not recommended.  If the AASHTO T164 solvent extraction test method is used, a non-chlorinated solvent may be substituted for the standard specified solvent, and the test method may be modified as per the recommendations of the solvent supplier.

In addition, for each day of production, the completed mix shall be tested for aggregate coating as follows.  Obtain a 100 – 150 gram sample and allow it to cure to normal laboratory temperature.  Place the sample in a glass jar of sufficient size that the loose sample will protrude to a level of no more than half of its capacity.  Cover the sample with water to approximately three-quarters of the capacity of the jar.  Place a tight fitting cover on the jar and allow it to stand for a period of 20 to 24 hours at normal laboratory temperature.  The sample jar shall then be vigorously agitated for a period of 30 seconds.  Pour the water from the jar, remove the sample, and spread it on a flat light-colored surface (nonstick laboratory paper is recommended).  Allow the sample to air dry and visually examine it for stripping of the asphalt film from the aggregate.  Estimate the amount of coated aggregate.  Any thin brownish, translucent areas are to be considered fully coated with an asphalt film.  Document the results of this test.  The mixture shall be considered acceptable if at least 95% of the aggregate is coated.  Insufficient coating may require reworking of the mixture and/or an additional amount of anti-stripping additive.

ACCEPTANCE OF THE MIXTURE

Acceptance of Winter Grade Bituminous Patching Mix shall be the responsibility of the Division.  This shall be accomplished by monitoring the contractor’s quality control testing and reviewing all test data relevant to the mixture.

In addition, if the completed mixture shows signs of stripping, the Division shall choose to either monitor the contractor’s quality control aggregate coating test or conduct their own test and visually estimate the amount of coated particles.  Document the results of this test.  Although this is a visual estimation, the contractor should be immediately notified if the Division’s test results are below 95%.  A low coating percentage should be an indicator for the Division to closely monitor the mixture after stockpiling.  All Division testing of Winter Grade Bituminous Patching Mix shall be performed by the District Materials Section.

After the mixture is stockpiled on the Division’s lot, it shall be visually evaluated for any appearance of excessive non-fully coated aggregate particles.  If considered necessary, the Division shall evaluate the mixture in accordance with ASTM D2489 (based on two-sample average) to determine if at least 97% of the coarse aggregate particles are fully coated.  This evaluation shall take place within the first week after stockpiling.  If the mixture is less than 97% coated, the contractor will be required to provide new material or remove the existing stockpile material from the Division’s lot, rework it to an acceptable condition with additional asphalt and/or chemical anti-stripping additive as needed, and return it to the Division’s lot.

PREPARATION OF MIXTURE

The aggregate shall be heated to insure that it is surface dry at the time of mixing, however, the aggregate shall not be heated in excess of 180oF.

The asphaltic binder shall not be heated to a temperature greater than 165oF.  Care shall be taken to prevent local overheating.  The aggregate and asphalt material shall be measured separately and accurately to the proportions in which they are to be mixed.  After the aggregate and binder have been combined, they shall be thoroughly mixed until the particles of aggregate are coated.  At no time shall the finished mixture be at a temperature greater than 175oF.

Temperatures for Modified Winter Grade Bituminous Patching Mix may vary as per asphalt supplier’s recommendations.

WORKABILITY

The mixture shall be stockpiled on the vendor’s site for 14 days or until the internal mix temperature is within 10oF of ambient temperature without stripping and when taken from a stockpile, shall be capable of being shoveled, raked, spread and compacted.

At the end of the stockpiling period on the contractor’s yard, the mixture shall be tested in accordance with ASTM D2489 (based on two-sample average).  The total amount of non-fully coated particles shall not exceed 3%.  The contractor shall provide these test results to the Division on a standard worksheet provided by the District Materials Section.

If the material fails to conform to the requirements of the specifications the contractor may rework the existing material or provide new material.

STORAGE

The mix shall be maintained on the contractor’s property in stockpiles not exceeding a height of four (4) feet until the internal mix temperature is within 10o of the ambient temperature.  In addition, the top of all stockpiles shall be leveled to eliminate any peaked areas.

All Winter Grade Bituminous Patching Mix shall contain sufficient asphalt that is capable of coating the aggregate without stripping.  After stockpiling on the Division’s lot, the mixture shall have a maximum of 5% non-fully coated particles after the first week and up to 90 days from delivery when evaluated in accordance with ASTM D2489 (based on two-sample average).  This coating determination may be based on the Division’s visual inspection if coating is not a problem, or based on Division testing when the amount of non-fully coated particles appears questionable.  If stripping occurs the contractor will be required to provide new material or remove the existing stockpile material from the Division’s lot, rework it to an acceptable condition with additional asphalt and/or chemical anti-stripping additive as needed, and return it to the Division’s lot.

2.	BIDDING INSTRUCTIONS

The purpose of this contract is to provide for the delivery of WINTER GRADE BITUMINOUS PATCHING MIXTURE (Standard or Modified) to the various locations and in the estimated quantities set out in the bid schedule.

Actual quantities to be delivered to each location will be specified in a State Contract Purchase Order (SCO) which will be issued by the Division of Highways at the time delivery is required.

Vendors may bid to deliver the estimated quantities of either or both types of material at any or all of the designated delivery sites.

Any qualification of bids or any modification of the specifications or conditions governing the bids may be cause for their rejection.

3.	CONTRACT AWARD

The Division of Highways will consider Vendor's performance history in the award of this Purchase Order Contract.

Qualified Vendors who submit a valid bid "F.O.B. Division Storage Site" will be awarded a contract for those locations for which their bid is low for Standard Winter Grade Bituminous Patching Material and for which their bid is low for Modified Winter Grade Bituminous Patching Material.

In the event a Vendor fails to conform to the requirements set out in this contract document, the State Contract Purchase Order or the governing specifications, the Purchase Order Contract may be cancelled and awarded to the next low bidder.

4.	SAMPLING AND TESTING

Upon award of contract, the Vendor shall inform the Division of the location of Vendor's storage sites so that materials may be sampled and tested prior to shipment.  Information shall be directed to the respective Division of Highways District Materials Engineers/Supervisors.

5.	WEIGHING MATERIALS DELIVERED BY TRUCK

Material delivered by truck shall be weighed in accordance with Section 401.9.3 of the West Virginia Department of Transportation, Division of Highways’ Standard Specifications.

6.	SUPPLYING OTHER ORGANIZATIONAL ENTITIES

County Courts, Municipalities, School Boards, other political subdivisions and governmental entities, etc., may have a need for these materials, and Vendors may wish to supply that need.  Accordingly, bidders may wish to extend their contract prices to these other entities.  If the bidder wishes to supply these other entities, but with prices different from those quoted for the Highway Department, the bidder shall include a set of bid schedules clearly and unambiguously marked for the express use of entities other than the Division of Highways.  Failure by the bidder to include a set of bid schedules for other entities will be taken to mean that the bid schedules extended to the Division of Highways will also be extended to these other entities.

In the event any Vendor does not wish to extend the prices, terms and conditions of this bid and subsequent contract to other entities of the State, he must so indicate in a clear and unambiguous manner in his bid. This indication does not prejudice the award of the contract.  If a Vendor does not indicate his refusal to extend the prices, terms and conditions of his bid to other entities of the State he is bound to extend them upon issuance of a purchase order by these other entities.

Other organizational entities using this provision of the contract shall do so without any involvement of the Division of Highways; that is, the entity shall make its own purchase arrangements with the Vendor and shall make its own arrangement for payment.

7.	BASIS OF PAYMENT

The quantity, determined in accordance with Section Number 5, will be paid for at the delivered price per ton, which price and payment shall be full compensation for furnishing and handling all the material incorporated in the mixture and delivering the mixture to a designated storage site.

8.	PRODUCTION SCHEDULE

Vendor should produce material within two weeks of receipt of SCO.

9.	VENDOR’S INVOICES

Vendor’s invoices must be submitted in original and one copy containing the following:

a.	Division of Highway's State Contract Purchase Order Number, and this Contract Number.

b.	Total quantity and unit price with the total cost of the material furnished.

Note:  Under no circumstance will the West Virginia Division of Highways accept, or pay for, quantities of material in excess of the quantity stated on the State Contract Purchase Order.

- PURCHASING CARD ACCEPTANCE

The State of West Virginia currently utilizes a VISA Purchasing Card Program which is issued through a bank. The successful vendors must accept the State of West Virginia VISA Purchasing Card for payment of all orders placed by State DOT agency for orders as a condition of award.

11.	11.  BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 1

STANDARD		     MODIFIED

DELIVERED		    DELIVERED

ESTIMATED	PRICE PER TON	         PRICE PER TON

COUNTY	     DELIVERY SITE        NEEDS (TONS)	   FOB DIV.		     FOB DIV.

STORAGE SITE           STORAGE SITE

Clay	C.R 11	 75	______________	_________________

Kanawha	Elkview	 50	______________	_________________

Kanawha	Chelyan	 35	______________	_________________

Kanawha	St. Albans	 50	______________	_________________

Mason	Point Pleasant	100	______________	_________________

Putnam	Red House	 75	______________	_________________

Putnam	Hurricane	 75	______________	_________________

I-79 Sec. 6	Amma	20	______________	_________________

I-77 Sec. 3	Sissonsville	45	______________ 	_________________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 2

STANDARD		  MODIFIED

DELIVERED	DELIVERED

ESTIMATED	PRICE PER TON	PRICE PER TON

COUNTY	DELIVERY SITE	NEEDS (TONS	FOB DIV.	FOB DIV.

STORAGE SITE	STORAGE SITE

Cabell	Barboursville	250	______________	______________

Lincoln	West Hamlin	75	______________ 	______________

Lincoln	Yawkey	15	______________	______________

Lincoln	Harts	25	______________	______________

Logan	Chapmanville	80	______________	______________

& Corridor G

Logan	Wilkinson HQ	60	______________	______________

Logan	Man Substation	40	______________	______________

Mingo	Millers Creek HQ     	50      	______________	______________

Wayne	Wayne	100	______________	______________

Wayne	Pritchard	100	______________	______________

Wayne	Crum	75	______________	______________

I-64	Huntington	40	______________	______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 3

STANDARD		 MODIFIED

DELIVERED	DELIVERED

ESTIMATED	PRICE PER TON	PRICE PER TON

COUNTY	DELIVERY SITE	NEEDS (TONS)	FOB DIV.		 FOB DIV.

STORAGE SITE       STORAGE SITE

Calhoun	Millstone	200	_____________	_____________

Jackson	Ripley	300	_____________		_____________

Pleasants	St. Marys

(Colin-Anderson Lot)	75	_____________		_____________

Ritchie	Ellenboro	75	_____________		_____________

Roane	Spencer	225	_____________	      _____________

Roane	WV 36 Left Hand	75	_____________       _____________

Wirt	Elizabeth	75	_____________		_____________

Wood	WV 95, Parkersburg	300	_____________ 	_____________

Corridor D	Greenwood	12	_____________	_____________

I-77	Mill Run Road	35	_____________	_____________

I-77 Sec. 2	Medina	20	_____________	_____________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 4

STANDARD		     ODIFIED

DELIVERED	        DELIVERED

ESTIMATED	   PRICE PER TON	        PRICE PER TON

COUNTY	DELIVERY SITE	NEEDS (TONS)	  FOB DIV.	          FOB DIV.

STORAGE SITE	        STORAGE SITE

Doddridge	Smithburg	100	    _____________		______________

Harrison	Gore	300	_____________	______________

Marion	Fairmont	100	_____________	______________

Marion	Mannington	100	_____________	______________

Monongalia	Sabraton	150	_____________ 	______________

Monongalia	Pentress	75	_____________ 	______________

Preston	Albright	100	_____________ 	______________

Preston	Bruceton	50	_____________	______________

Preston	Terra Alta	50	_____________ 	______________

Preston	Fellowsville	50	_____________ 	______________

Preston	Aurora	50	_____________ 	______________

Taylor	Pruntytown	200	_____________ 	______________

APD-50	Tunnel Hill	50	_____________ 	______________

I-68	Coopers Rock	50	_____________ 	______________

I-79	Lost Creek Yard	100	_____________ 	______________

I-79	Goshen Road	50	_____________	______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 5

STANDARD		  MODIFIED

DELIVERED		  DELIVERED

ESTIMATED	    PRICE PER TON	      PRICE PER TON

COUNTY	DELIVERY SITE       NEEDS (TONS)	FOB DIV.		  FOB DIV.

STORAGE SITE        STORAGE SITE

Berkeley	Martinsburg & I-81	300	_____________ 	______________

Grant	Petersburg	75	_____________ 	______________

Grant	Mt. Storm	50	_____________ 	______________

Hampshire	Romney	50	_____________ 	______________

Hampshire	Capon Bridge	30	_____________	______________

Hampshire	Slanesville	50	    _____________		______________

Hardy	Moorefield	75	    _____________		______________

Hardy	Baker	75	    _____________		______________

Jefferson	Charles Town	100	_____________ 	______________

Mineral	New Creek	75	    _____________		______________

Mineral	Sky Line	50	    _____________		______________

Mineral	Short Gap	50 	    _____________		______________

Morgan	Berkeley Springs	250	_____________ 	______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 6

STANDARD		  MODIFIED

DELIVERED		 DELIVERED

ESTIMATED	     PRICE PER TON     PRICE PER TON

COUNTY		DELIVERY SITE       NEEDS (TONS)	  FOB DIV.		  FOB DIV.

STORAGE SITE      STORAGE SITE

Brooke	Wellsburg	200	______________ 	______________

Hancock	New Manchester	220	______________ 	______________

Marshall	Cameron	700	______________ 	______________

Marshall	Glen Dale	1300	______________ 	______________

Ohio	Triadelphia	150	______________ 	______________

Tyler	Centerville	100	______________ 	______________

Tyler	Sistersville	100	______________ 	______________

Wetzel	Hundred	100	______________	______________

Wetzel	New Martinsville	150	______________ 	______________

Wetzel	Pine Grove	100	______________ 	______________

I-70	Woodland (Elm Grove)	   50	______________ 	______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 7

STANDARD		  MODIFIED

DELIVERED		 DELIVERED

ESTIMATED   	   PRICE PER TON	     PRICE PER TON

COUNTY	DELIVERY SITE   NEEDS (TONS)	     FOB DIV.	 	  FOB DIV.

STORAGE SITE         STORAGE SITE

Barbour	Philippi	70	______________ 	______________

Braxton	Laurel Court	150	______________ 	______________

Gilmer	Glenville HQ	60	______________ 	______________

Lewis	Weston	100	______________ 	______________

Upshur	Buckhannon	75	______________ 	______________

Webster	Cherry Falls	25	______________ 	______________

Webster	Cowen	25	______________ 	______________

Webster	Hacker Valley	25	______________ 	______________

I-79 Sec. 4	Burnsville	25	______________ 	______________

I-79 Sec. 5	Coon Knob	25	______________ 	______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 8

STANDARD		   MODIFIED

DELIVERED		   DELIVERED

ESTIMATED    PRICE PER TON	       PRICE PER TON

COUNTY	DELIVERY SITE     NEEDS (TONS)	 FOB DIV.		   FOB DIV.

STORAGE SITE         STORAGE SITE

Pendleton	Franklin	100	_______________ 	_______________

Pocahontas	Marlinton	25	_______________ 	_______________

Randolph	Elkins	100	_______________ 	_______________

Tucker	Parsons	60	_______________ 	_______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 9

STANDARD		  MODIFIED

DELIVERED		  DELIVERED

ESTIMATED	     PRICE PER TON	      PRICE PER TON

COUNTY	DELIVERY SITE      NEEDS (TONS)       FOB DIV.		  FOB DIV.

STORAGE SITE        STORAGE SITE

Fayette	Oak Hill	60	______________ 	______________

Fayette	Lookout	100	______________ 	______________

Fayette	Falls View	25	______________	______________

Greenbrier	Lewisburg	125	______________ 	______________

Greenbrier	Crawley	100	______________ 	______________

Greenbrier	I-64, Harts Run	15	______________ 	______________

Monroe	Union	175	______________ 	______________

Monroe	Peterstown	100	______________ 	______________

Nicholas	Summersville	175	______________ 	______________

Summers	Summers Co. HQ	75	______________ 	______________

11.	BIDDING SCHEDULE

WINTER GRADE BITUMINOUS PATCHING MIXTURE

DISTRICT 10

STANDARD		    MODIFIED

DELIVERED		    DELIVERED

ESTIMATED	    PRICE PER TON	        PRICE PER TON

COUNTY		DELIVERY SITE      NEEDS (TONS)      FOB DIV.		    FOB DIV.

STORAGE SITE          STORAGE SITE

Mercer	Mercer Co. HQ	100	_______________ 	_______________