- SPECIFICATIONS

The following sections of the West Virginia Department of Transportation, Division of Highways Standard Specifications Roads and Bridges, adopted 2000, as modified by the current Supplemental Specifications at time of bid opening shall apply to the administration of this Contract:  Sections 101, 102.4, 102.5, 105.1, 105.3, 105.4, 105.10, 105.11, 105.12, 105.13, 106.3, 106.4, 106.5, 106.6, 106.7, 106.9, 107.1, 107.2, 107.3, 107.14, 107.19, 107.20, 108.8, 109.1, 109.2, and 109.20.

The terms "Contractor" and "Vendor" used in the above specifications or this contract are interchangeable.  Contractor shall mean Vendor and Vendor shall mean Contractor.

West Virginia Department of Transportation, Division of Highways' Standard Specifications Roads and Bridges, adopted 2000 and the current Supplemental Specifications at time of bid opening may be obtained from:

# West Virginia Division of Highways

State Capitol Complex

Engineering Division, Technical Section

1900 Kanawha Blvd., East, Bldg. 5, Room A-650

Charleston, West Virginia  25305

- ASPHALT MATERIAL

Material supplied under this contract shall conform to the sections of the West Virginia Department of Transportation, Division of Highways' Standard Specifications Roads and Bridges, adopted 2000, as modified by the current Supplemental Specifications at time of bid opening listed on the Bid Schedule for Anionic Liquid Asphalt Emulsion and Cationic Liquid Asphalt Emulsion, except as follows:

  - SS-1 DILUTED AND SS-1h DILUTED

SS-1 or SS-1h meeting the requirements of AASHTO, M 140, shall be diluted by the addition of one part water to each part.

  - POLYMER MODIFIED EMULSIFIED ASPHALT

Polymer modified emulsified asphalt (cationic grade) shall meet the requirements of AASHTO M208, Grade CRS-2, with the following additions and revisions.

TEST	MINIMUM	MAXIMUM

## Viscosity Saybolt Furol,	200	500

## at 50º C, seconds

## Elastic Recovery*	50

*The test procedure for the Elastic Recovery test shall be in accordance

with MP 705.11.20.

- BIDDING INSTRUCTIONS

DELIVERY:  The purpose of this Contract is to provide for the delivery of LIQUID ASPHALT MATERIAL to any location within the County set out in the Bid Schedules.  Actual quantities to be delivered to each location will be specified in a State Contract Purchase Order (SCO) which will be issued by the Division of Highways at the time delivery is required.

QUOTATIONS:  Vendors may bid to furnish any or all of the various grades of asphalt material listed on the Bid Schedules.  The bid prices shall be shown FOB Vendor's plant and/or Tank Truck Delivered to Division of Highways storage tanks or job sites within the County.

Any qualification of bids or any modification of the specifications or conditions governing the bids may be cause for their rejection.

SPECIAL NOTE:  Any qualification of the bids with a price escalation clause will not be honored by the Division of Highways and the Contract will be awarded as if the price escalation qualification by the Vendor had not been made.

DEMURRAGE:  Should a Vendor expect to collect demurrage on tank truck transport units, after a designated period of time, occasioned by delay in unloading when delivering to other than company owned storage facilities such as mentioned in the paragraph entitled "Storage Facilities", the fact shall be so stated on the bid and the rate recorded.

RETURNED LOADS:  The Vendor may quote a lump sum bid for the return of a complete or partial tank truck load of material not accepted by the Division of Highways.  For the return load charge to be applied, the material must be returned through no fault of the vendor.

STORAGE FACILITIES:  Upon request the Vendor will be required to furnish portable storage facilities at the West Virginia Division of Highways project sites.  The Vendor shall be notified a minimum of five (5) working days in advance of delivery when portable storage facilities are required.  These portable storage tanks shall have a capacity of not less than 5,000 gallons and shall meet the requirements contained in the section "Equipment".  The Vendor may elect to "drop" a transport tank trailer in lieu of furnishing a portable storage tank.  The rental thereof shall be that established for portable storage tank usage.  Should a Vendor expect to collect rental for portable storage facilities or "drop" transport trailers that fact shall be stated on the bid and the rate recorded in the paragraph entitled "Rental".

EQUIPMENT:  Insulated storage tanks and tank trucks shall be used in storage and/or delivery unless otherwise specified in shipping instructions.  All such equipment must be in good mechanical condition, equipped with standard fittings and connections and shall have the necessary facilities for sealing.  All tank trucks shall be properly cleaned by the Vendor prior to loading.  Any tank truck found not to be properly equipped and/or to contain contaminated material, will be rejected and returned to the Vendor at the Vendor's expense.

- CONTRACT AWARD

All qualified Vendors who submit a valid bid "FOB Vendor's Plant" will be awarded a contract for those items bid.

Qualified Vendors who submit a valid low bid "Tank Truck Delivery" will be awarded a contract for those locations and those items for which their bid is low.

- TESTING

All material furnished on awarded contracts shall be sampled at the Vendor's plant by a representative of the West Virginia Division of Highways and forwarded by that representative to the Division's Contract Administration Division, Materials Section for analysis and report on conformity with specifications.

When asphalt material is furnished by a supplier who is not certified under provisions of MP 401.02.25, the supplier shall be required to have each batch or lot of material, to be furnished to the Division, sampled by a Division approved agency, in accordance with MP 700.00.01 and shall have the samples tested for compliance with the governing specifications in a Division approved laboratory.

- LATE DELIVERY CHARGE

The West Virginia Division of Highways will assess a late delivery charge against the Vendor when a specified delivery time is not met.  The amount of the late delivery charge will be calculated at the rate of One Hundred Dollars ($100.00) for each one-quarter (1/4) hour of the late delivery.  A two (2) hour grace period will be allowed when assessing late delivery charges.

- BASIS OF PAYMENT

ASPHALT MATERIAL:  Unless otherwise specified, payment shall be based on the bid price for the net gallons furnished on each order at 60 degrees F.  The Vendor shall furnish certificates showing loading temperature; number of gallons loaded at loading temperatures; number of gallons allowed for shrinkage; net gallons at 60 degrees F.

DEMURRAGE:  Maximum unloading time two (2) hours free, a charge of $_______ for each additional one-quarter (1/4) hour.

RENTAL:  Portable storage tank or "Drop" tank trailer in place;  add $________ per gallon stored.

The DOH Classification for Demurrage, Rental, Return Load, and Late Delivery will be the same as material classification of the purchased item (no inventory units).

The quantities recorded in the attached list are 2004 purchases.  They may increase or decrease in accordance with normal requirements of the West Virginia Division of Highways, and as may be necessary due to prevailing conditions.

- VENDOR'S INVOICES

Vendor's invoices must be submitted in original and one copy and contain the following:

- This Purchase Order Contract number.

- The Division of Highways State Contract Order (SCO) number.

- Delivery destination, including county name.

- Total quantity and unit price with the total cost of each type of material furnished.

- Demurrage and return load charges must be shown on the invoice for the material for which they apply.

NOTE:	Under no circumstances will the West Virginia Division of Highways accept, or pay for, quantities of materials in excess of the quantity stated on the State Contract Order (SCO)

### WEST VIRGINIA DIVISION OF HIGHWAYS

MAINTENANCE OPERATIONS

2008 LIQUID ASPHALT MATERIAL USAGE

#### ANIONIC ASPHALT EMULSION	CATIONIC ASPHALT

ALL GRADES	          EMULSION

##### District	SS-1	SS-1h	POLYMER

##### RS-2	HFMS-2	DILUTED	DILUTED	CMS-2	MODIFIED

1	0	5,850	0	0	0	0

2	43,373	0	0	0	0	0

3	0	54,976	0	0	0	0

4	48,415	0	0	0	0	0

5	0	0	0	0	0	0

6	 0	51,586	0	0	0	0

7	115,084	0	0	0	0	0

8	0	0	0	0	0	0

9	0	0	0	0	0	0

10	0	0	0	0	0	0

###### TOTAL	206,872	112,412	0	0	 0	0

BID SCHEDULE

F.O.B. VENDOR'S

PLANT

ANIONIC LIQUID ASPHALTIC EMULSION (Spec. 705.2)

ITEM	DESCRIPTION	DOH CLASSIFICATION

A1	RS-1	011-020-000001  } _______________@_____________ per Gal.

A2	RS-2	011-020-000002

B1	MS-1	011-020-000003  } _______________@_____________ per Gal.

B2	MS-2	011-020-000004

C1	HFMS-1	011-020-000018  } _______________@_____________ per Gal.

C2	HFMS-2	011-020-000019

D1	SS-1 (Diluted)	011-020-000021  } _______________@_____________ per Gal.

D2	SS-1h (Diluted)	011-020-000023

CATIONIC LIQUID ASPHALTIC EMULSION  (Spec. 705.11)

ITEM	DESCRIPTION	DOH CLASSIFICATION

E1	CRS-2	011-020-000008     _______________@_____________ per Gal.

F1	CMS-2	011-020-000011     _______________@_____________ per Gal.

G1	Polymer Modified

Cationic Grade 	011-020-000024     _______________@_____________ per Gal.

Location of Vendor's Plant (s) __________________________________________________