WEST VIRGINIA DEPARTMENT OF TRANSPORTATION

DIVISION OF HIGHWAYS

EQUIPMENT DIVISION

PROCUREMENT SPECIFICATIONS

NO. 503-1-C

MULTI-PURPOSE ROAD MAINTENANCE UNIT

WITH ROTARY GRINDER, PAVING SCREED, SHOULDER BUILDING ATTACHMENT,

AND TACK TANK

1.0 	PURPOSE

It is the purpose of these specifications to describe a versatile multi-purpose road maintenance unit with a rotary grinder, paving screed, shoulder building attachment, and tack tank (hereinafter referred to as a "unit") to be purchased for use by the West Virginia Division of Highways (DOH) on an Open End Contract basis.

2.0	BIDDING PROCEDURES

The current purchasing procedures regarding bidding as established by the Department of Administration, Purchasing Division, shall apply.  Failure to submit the " Request for Quotation" forms, complete in its entirety and according to directions indicated, may subject the bidder to disqualification.  Each bid submitted shall also be accompanied by a Bidder's Evaluation Report completed in detail.  Addendums in order, along with exception sheets, should be with Bidder’s Evaluation Report.  FAILURE TO SUBMIT THE BIDDER'S EVALUATION REPORT, COMPLETE IN ITS ENTIRETY, MAY RESULT IN AUTOMATIC DISQUALIFICATION.

3.0		SPECIFICATIONS

The specifications named herein, mandatory and non-mandatory, establish the acceptable level of quality only and are not intended to reflect a preference or favor any particular brand or vendor.

3.1	EXCEPTIONS TO NON-MANDATORY SPECIFICATIONS

Exception to a non-mandatory unit specification may be made by the bidder, providing the exception is not available from the manufacturer.  Any such exception must be noted on the bidder's evaluation report and should be accompanied by supporting documentation/literature from the manufacturer.  Any exception must be indicated on a separate attachment to the bidder's evaluation report and labeled as "Exception to Specifications".  The state reserves the right to determine whether the stated exception does or does not reduce the quality and performance of the unit.  Failure to provide information for any exceptions may be grounds for rejection of the bid.  The state reserves the right to waive minor irregularities in bids or specifications in accordance with §148-1-4(f) of the WV Legislative Rules and Regulations.

3.2	MANDATORY SPECIFICATIONS

All specifications preceded by "shall, will, and/or must" or are stated as a "minimum and/or maximum" are mandatory as stated in Purchasing Divisions Policies and Procedures.  Any bid failing to meet any mandatory item shall be immediately disqualified.  Failure to respond in the appropriate evaluation section may also be grounds for immediate disqualification at the discretion of the State.

A mandatory pre-bid conference is scheduled for this equipment purchase as stated in the RFQ.  Vendors having products with variations or exceptions in specified mandatory items are expected to address any such variations or exceptions during the pre-bid conference.  The State shall review and consider any such variation or exception, and may at its sole discretion, issue an addendum to change mandatory specifications deemed to be in the State's best interest.  Bids from any vendor failing to attend the mandatory pre-bid shall be disqualified.  Bids containing any variation or exception to a mandatory specification that was not addressed during the pre-bid conference and accepted by the issuance of an Addendum shall be disqualified.

4.0	REPRESENTATIVE UNIT FOR TEST

The successful vendor must (if specified) provide DOH one (1) completed representative unit to be observed and evaluated on each order to insure compliance with specification.  If requested, the time period for testing and evaluation shall be seven (7) working days following receipt of the unit.  DOH will incur no obligation for deterioration of surfaces, finishes, seals, and mechanical or electrical parts on the unit resulting from operation and testing within the limits of these specifications; nor will DOH incur obligation for damage to the unit resulting from failure to meet specifications when due care and attention is given by DOH and testing is done within the limits of these specifications.  Failure of the pilot unit to satisfactorily meet specifications as bid shall be cause for cancellation of the purchase order, and return of the delivered unit along with all associated equipment to the vendor at the vendor’s expense.

4.1	CONDITION OF UNIT(S) UPON DELIVERY

All units must arrive at the prescribed delivery point having been completely preserviced with oil, lubricants, and coolant.  All prescribed precautions pertaining to first operations and break-in of the unit are to be posted conspicuously on the unit for ready observance by the operator.

4.2		DELIVERY

Delivery point of the completely assembled representative unit will be the DOH, Equipment Division, Route 33 at Brushy Fork Road, Buckhannon, West Virginia (26201).

The vendor is responsible for guaranteeing delivery of the completed units within the time specified and agreed to by the State.  Delivery is preferred within 120 days after receipt of purchase agreement.  The vendor is responsible for establishing and coordinating delivery terms with allied manufacturers or suppliers.  Delivery terms shall be stated in the bid and the State reserves the right to accept or negotiate such terms.  Failure to reach an agreement may result in rejection of the bid.  The successful bidder shall provide their manufacturer's confirmation of the order to the WVDOH contact person within seven (7) working days after receiving the approved purchase order.

A completed pilot model for inspection must be provided within 30 calendar days after receipt of the purchase agreement by the successful vendor.

Delivery is an integral part of this specification and failure to comply will be cause to initiate a D.O.T. Administrative Form WV-82, Vendor Performance Form.  The WV-82 Form will provide a means of officially notifying the Purchasing Division and the vendor of unsatisfactory performance; such as late deliveries, poor service, inadequate parts supplies, etc.

The decision to initiate subject Form will be at the sole discretion of the D.O.H. Commissioner's established Equipment Review Board.

Issuance of the WV-82 Vendor Complaint Form on unsatisfactory delivery against any vendor will be cause to refuse to consider similar items from those vendors on future Request For Quotations.

(NOTE: Delivery time could be altered due to labor strikes, severe inclement weather conditions, etc.)

5.0	AWARD CRITERIA

5.1	DOH will recommend the award in accordance with the RFQ evaluation criteria described in the requisition.  The award shall be made to the lowest unit cost vendor that meets or exceeds the specifications.

Prices for the units shall be in quantities of 1-5, 6-10, and 11 and over.  However, for evaluation purposes, we will use quantities 1-5.  DOH reserves the right to place multiple orders in any quantity.

6.0	SPECIFICATIONS AND GUIDELINES - GENERAL

6.1	IDENTIFICATION OF THE UNIT BEING PROPOSED

The bidder must identify the unit by manufacturer, model, series, and year of manufacture, in the bid to enable identification by DOH in the manufacturer's specifications of the proposed unit.  The bidder will submit complete descriptive literature of the proposed unit, to establish that the bid is the manufacturer's most current model, including latest engineering improvements, which have been, or will imminently be, regularly advertised and sold on the open market.  The unit specified herein and offered to be manufactured after January 1, 2008 and be clearly identified and marked with date of manufacture.

6.2		OPERATING AND SERVICE MANUALS AND PARTS LISTS

An operator's manual must be included with each unit upon delivery.  A "line sheet" (if applicable) and Equipment Preventative Maintenance Questionnaire (as shown in X6.2 of the Bidder's Evaluation Report) must be with pilot unit upon delivery.  In addition, there must be 12 service, shop, or maintenance manuals; ten (10) to be distributed to the Districts and two (2) for the Equipment Division.  Also, there must be 14 parts manuals; ten (10) to be distributed to the Districts and four (4) for Equipment Division use.  CD ROM is preferred in lieu of parts manuals.

*	NOTE: MANUALS SHALL BE DELIVERED UPON COMPLETION OF DELIVERY OF TOTAL UNITS.  FAILURE TO DO SO WILL DELAY PAYMENT.

6.3		TRAINING:

Manufacturers and/or dealers will be required to stage a thorough seminar on the subjects of Preventative Maintenance, Operator and Mechanic Training.  In order to keep the operators and mechanics updated, the successful vendor shall conduct training with each purchase order against this open end contract.  Training is preferred within 2 working days after delivery of the pilot unit on the individual purchase order.

Manufacturers and/or dealers shall be required to furnish the Training Academy with one (1) Operator's Manual to be shipped direct to WVDOH Training Academy, Post Office Box 610, Buckhannon, West Virginia 26201 prior to delivery of the pilot.

The seminar to be held at the W. Va. Division of Highways, Equipment Division, Buckhannon, West Virginia.

6.4		PREVENTIVE MAINTENANCE AND OPERATOR PROCEDURES:

Manufacturers and/or dealers will be required to submit to the Equipment Division, in addition to the operating and service manuals, booklets and pamphlets explaining the Preventive Maintenance and Operator Procedures to be used by the operators of this equipment, and must include such things as daily prestart inspection procedure, service schedule, and routine maintenance required, safety precautions, etc.

The successful vendor shall furnish all training aids; i.e., videos, projectors, etc. required in conducting the training.

6.5	WARRANTY AND SERVICE POLICY

The Manufacturers warranty or service policy is to apply to the unit.  Such warranty or service policy is to be recognized at any authorized unit dealer, representing manufacturer of proposed unit throughout the State of West Virginia.  The applicable warranty or service policy will not be contingent upon obtaining routine service, lubrication, and servicing of the unit from factory authorized agencies.  It will be the responsibility of the bidder to have available labor to repair or replace any defective replacement parts, components and materials, and to have available those replacement parts, components, and/or materials found to be defective during the terms of the warranty period.  The bidder should state the labor rates, locations where parts will be stocked, availability of parts, and discounts offered for parts, when terms of the warranty offer a pro-rated cost for parts and labor.  In addition, the successful bidder should offer field work to repair or replace defective parts, components, and materials found to be defective during the terms of the warranty and should provide mechanic's travel rates, mileage charges, field mechanic rates, and any surcharge for miscellaneous items, if applicable, for field work during the warranty period.  Submit to Division of Highways any technical or engineering improvements during the term of the warranty.  The unit must be accompanied upon delivery by the unit's manufacturer's executed warranty or service policy.

A mandatory minimum two (2) year bumper to bumper basic parts and labor warranty excluding abuse and normal wear items is required for this unit.

THE “WARRANTY AND SERVICE POLICY QUESTIONNAIRE” ATTACHED IN THE BIDDER’S EVALUATION REPORT MUST BE COMPLETED IN ITS ENTIRETY BY THE SUCCESSFUL BIDDER OR MANUFACTURER PRIOR TO DELIVERY OF THE PILOT MODEL.  (SEE SECTION X6.5  OF BIDDER’S EVALUATION REPORT).

6.6		EVALUATION COMMITTEE REQUIREMENTS

Detailed component specifications, product literature, component models, required for specification compliance determination by the Evaluation Committee should be provided with each bid.  Any information supplied that is contrary to/or conflicting with the specifications and/or attached Bidders Evaluation Report may be sufficient cause for rejection of bid.

6.7		UNSPECIFIED ACCESSORIES & FEATURES

All parts, equipment, accessories, material, design and performance characteristics not specified herein, but which are necessary to provide a complete unit, must be furnished with each unit and required to conform to strength, quality of material, and quality of workmanship to those which are advertised and provided to the market in general by the unit industry.

All parts and accessories advertised and regularly supplied as standard shall be included, except those which would represent duplication of these specified, and except those which, by specification, are not to be furnished.  All standard safety features, required by Federal and State Law, shall be included.

7.0		SPECIFICATIONS OF THE QUOTED UNIT ARE AS FOLLOWS:

Unit shall be LeeBoy Model 1200S or equal

7.1		Towing:

7.1.1		Unit shall have adjustable, heavy duty, hydraulic tongue

7.1.2		Shall be able to tow at up to 45 MPH

7.1.3		Must be easily connected and disconnected to tow vehicle

7.1.4		Movement between jobs shall be quick and efficient

7.2		Shoulder Attachment:

7.2.1		To convey and spread dirt, sand, gravel, or any asphalt material

7.2.2		Should cover 28 inches to 40 inches in widening or building up low shoulders

7.3		On-Board Tank/Emulsified Liquid Asphalt Distributor System:

7.3.1		Tank size:  Should be 100 gallon

7.3.2		Burners:  Propane

7.3.3		Pump:  Hydraulic driven

7.3.4		Hose:

7.3.4.1			Unit must have self winding hose

7.3.4.2			Unit to have minimum 40 foot of hose

7.3.4.3			Must have hand held spray wand

7.4		Power Train:

7.4.1		Engine:  Shall be Diesel Hatz Silent Pack or equal

7.4.2		74 HP

7.4.3		Engine shall have safety shutdown features

7.5		Transmission:

7.5.1		Shall be variable hydrostatic (front wheel drive)

7.6		Dimensions of unit:

7.6.1		Weight:  8500 lbs.

7.6.2		Length:  12 feet

7.6.3		Width:  8 feet 6 inches

7.6.4		Height:  8 feet

7.6.5		Receiving Hopper:

7.6.5.1			Capacity:  2.5 Tons

7.6.5.2			Width:  111 inches

7.6.6		Hopper must have hydraulic folding wings

7.7		Rotary Grinder:

7.7.1		Raising and lowering shall be done hydraulically

7.7.2		Dimensions:

7.7.2.1			Width:  24 inches

7.7.2.2			Diameter:  16 inches

7.7.3		Grinder must be able to pivot up to 15 degrees from horizontal

7.7.4		Rotary grinder shall be variable hydrostatic driven

7.8		Paving Screed:

7.8.1		Should telescope from 38 inches to 62 inches

7.8.2		Shall be able to be adjusted up to 15 degrees from horizontal

7.8.3		Must have an auger that provides even distribution of material

7.8.4		Shall have adjustable end gates that will provide square edges

7.8.5		Unit to have underlay pan that modifies the screed so operator can pave a narrow strip 	up to 24 inches wide

7.9		Tires

7.9.1		Front:  5.70 x 8.00 (8 ply)

7.9.2		Rear:  9.00 x 14.5 (12 ply)

7.10	Capacities:

7.10.1		Fuel tank:  15 gallon

7.10.2		Hydraulic reservoir:  52 gallon

7.11	Lighting:

7.11.1		Unit will have rotating yellow safety beacon

7.12	Painting:

7.12.1		Unit to be prepped and painted manufacturers standard process and colors

713		Unit shall include all other features considered as standard equipment but not

specifically addressed above.

7.14	Advertising:

7.14.1		Visible decals or name plates or painted on names representing the Manufacturer or

model number or trademark appearing on the exterior surface of the unit should be

minimal.

7.15	Vendor must certify that the unit offered will meet or exceed the "Occupational Safety and Health Act of 1970" and subsequent amendments.