WEST VIRGINIA DEPARTMENT OF TRANSPORTATION

DIVISION OF HIGHWAYS

EQUIPMENT DIVISION

BIDDER'S EVALUATION REPORT

PROCUREMENT SPECIFICATIONS FOR OPEN END CONTRACT

NO. 371-2-G

33,000 GVW CAB AND CHASSIS, STAINLESS STEEL DUMP BODY, AND

PISTON PUMP HYDRAULIC SYSTEM

NOTE TO BIDDER:    Procurement Specification No. 371-2-G, Paragraph 2.0 recommends the completion and submittal of this Report with your bid.  Purpose of this Report is to enable the West Virginia Division of Highways Evaluation Committee to make full and fair evaluation of the bid.  Addendums in order, along with a summary of exception as a separate attachment, should be with Bidder’s Evaluation Report.

FAILURE TO SUBMIT THIS REPORT, COMPLETE IN ITS ENTIRETY, MAY SUBJECT THE BIDDER

TO DISQUALIFICATION.

Reference Requisition No.: ______________________

Bidder's Name:____________________________________________________________

Address:__________________________________________________________________

Telephone Number:_________________________________________________________

Years Bidder has been registered to do business with the State of West Virginia:  ______________YRS.

Years Company has been an authorized dealer for proposed unit:                        _______________YRS.

X3.2	Have you complied with all mandatory specifications?	_____ YES _____ NO

X4.2   	DELIVERY:

X4.2.1 	Delivery date of completed representative unit:________________ Calendar Days After 												Receipt of Purchase Agreement

X4.2.2 	Delivery date of balance of completed units:  ________________ Calendar Days After Receipt of

Purchase Agreement

X5.0	AWARD CRITERIA;

X5.1	Prices for units: 				1-25		________________per unit

26-50		________________per unit

51 and over	________________per unit

X6.0   SPECIFICATIONS - GENERAL

X6.1   Manufacturer, model, series, and date of manufacture of proposed unit:

Cab and Chassis:___________________________________________________________________

Dump Body: ______________________________________________________________________

Piston Pump Hydraulics: ____________________________________________________________

Is descriptive literature, fully describing proposed unit attached to your bid? _____ YES _____ NO

If not, why?______________________________________________________________

X6.2	Will the required number of service manuals, and complete parts list be delivered to the

Equipment Division at Buckhannon upon completion of delivery of total units?

_____ YES _____ NO

Will the required Equipment Preventive Maintenance Form (Section X6.2 of Bidders Evaluation Report) be provided upon inspection of the pilot unit?			_____ YES _____ NO

X6.2

2-10-00

EQUIPMENT PREVENTATIVE MAINTENANCE QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY SUCCESSFUL BIDDER OR MANUFACTURER’S TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT MODEL TO THE WVDOH.

DESCRIPTION: _______________________________________		MAKE: ___________________________________

MODEL: ________________________    	YEAR: __________	PURCHASE AMOUNT: ______________________

ENGINE:	MAKE: ______________________ 	MODEL: __________________ 	FUEL TYPE: ________________________

HORSEPOWER: _______________	CYLINDER: ________	ENGINE SERIAL: __________________________

COOLING SYSTEM CAPACITY: ______________________

BELTS:		DESCRIPTION:					PART NUMBERS:

___________________________________________	_________________________________________________

___________________________________________	_________________________________________________

GVW: _______________________	AXLE CAPACITY: 	FRONT: ______________	REAR:______________

TIRES:		FRONT MAKE & SIZE: ______________________________________________

REAR MAKE & SIZE: _______________________________________________

DIMENSIONS OF UNIT:	LENGTH: __________		WIDTH: ______________	LENGTH: ___________

VENDOR CONTACT PERSON: ____________________________________		PHONE: __________________________

PARTS:

BATTERY MAKE: ____________________	MODEL: ___________________		CCA: _______________________

TOP OR SIDE POST: __________________	DIMENSIONS: LENGTH ________ WIDTH ________ HEIGHT __________

SPARK PLUGS OR FUEL INJECTORS MAKE: ______________	PART # __________________________________________

FUEL PUMP OR INJECTION PUMP MAKE: ________________	MODEL: _________________________________________

ALTERNATOR MAKE: __________________________________	PART #:__________________________________________

STARTER MAKE: ______________________________________	PART #: _________________________________________

TURBO CHARGER MAKE: ______________________________	PART #: _________________________________________

TRANS. MAKE: ____________________	MODEL: _________________________   AUTO/MANUAL: ____________________

HYDRAULIC PUMP MAKE: _____________________________	MODEL: _________________________________________

FILTERS		MAKE	PART NO.		LUBRICANT		MANUFACTURER TYPE

OIL		__________________________________	ENGINE	__________________________________________

AIR INNER	__________________________________	TRANSMISSION__________________________________________

AIR OUTER__________________________________	POWER STEERING _______________________________________

FUEL PRIMARY ______________________________	HYDRAULIC  	__________________________________________

FUEL SECONDARY ___________________________	DIFFERENTIALS _________________________________________

COOLANT	__________________________________	BRAKE FLUID 	__________________________________________

HYDRAULIC	_______________________________	COOLANT	__________________________________________

OTHER		__________________________________ 	OTHER 	__________________________________________

X6.3	TRAINING:

Will training seminar be conducted on Preventive Maintenance, Operator and Mechanic Training                      								_____YES _____ NO

Will you conduct training with each purchase order against this open end contract?

_____ YES _____ NO

Will training be conducted within 2 working days from the delivery of the pilot unit on the individual purchase order?								_____ YES _____ NO

If NO, explain time frame_____________________________________________________________

Will an Operator’s Manual be furnished directly to Training Academy prior to the

delivery of the pilot?								_____ YES _____ NO

X6.4   	If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors, required in conducting the training?		         _____ YES _____ NO

X6.4.1    	Will all manuals, booklets, etc. explaining preventive maintenance, operator procedures, and service schedule be delivered with each unit?           			_____ YES_____NO

If NO, explain _____________________________________________________

X6.5	WARRANTY AND SERVICE POLICY

Will the warranty and service you provide comply with all areas as stated in Section 6.5 of specifications                               							_____ YES _____ NO

Is warranty literature attached?					_____ YES _____ NO

Is a minimum two (2) year bumper to bumper basic parts and labor warranty excluding abuse 	and normal wear items included?					_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

X6.5	WARRANTY AND SERVICE POLICY QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY AND SUBMITTED WITH YOUR BID.

(If additional lines are needed, make copies of form.)

1. Define the terms of the standard warranty.  If not offered, so state.  (Attach copy)

2. Define warranty service to be performed at DOH facilities and warranty service to be performed at

manufacturer’s representative facility.  List name and location of manufacturer’s representative.

3. List locations for parts inventories that are within the State of West Virginia.  Also, list availability levels, if

known.

4. During the term of warranty, list the guarantee discount to manufacturer’s published list price for parts that

bidder will sell the parts to owner.

A.	Terms: Net 30	Manufacturer’s published list price less: __________% discount

B.	Terms: Net 60	Manufacturer’s published list price less: __________% discount

C.	Terms: Net 90	Manufacturer’s published list price less: __________% discount

5. During the term of warranty, will all manufacturers or engineering improvements be submitted to Division of

Highways?							_____ YES _____ NO

6. During the term of warranty, list the guaranteed rates charged for repair to the unit.

A.	Shop Rate		$ __________ per mechanic hour

B.	Travel Time Charge		$ __________ per mechanic hour

(Specify if one-way)		__________; port to port __________

C.	Mileage Charge		$__________ per vehicle mile

(Specify if one-way		__________; port to port __________

D.	Field Mechanic Rate		$__________ per mechanic hour

E.	Specify period of time that prices are in effect: __________________________

F.	Surcharge for miscellaneous items: ____________________%

X6.6 	EVALUATION COMMITTEE REQUIREMENTS

Is all component specifications, product literature, component models provided for Evaluation Committee bid determination?					_____ YES _____ NO

X6.7	Will all parts, equipment, accessories, material, design and performance characteristics not

specified herein, but which are necessary to provide a complete unit, be furnished with the unit

and conform in strength, quality of material, and quality of workmanship to those which are

advertised and provided to the market in general by the unit industry?

_____YES _____NO

X6.7.1	Are all parts and accessories adequate and regularly supplied as standard to be included except 	those which may be duplications of specifications herein, and except these by specification are not

to be furnished?                                        				_____YES _____NO

X6.7.2	Are all standard safety features that are required by Federal and State statutes of law included?                   									_____YES _____NO

X7.0	SPECIFICATIONS OF THE QUOTED UNIT

The bidder should complete the following schedule in order for the Division to compare the actual bid 	unit to the specifications.  Should the bidder except a requirement, then such exception may be only on 	the basis that such feature is not offered by the manufacturer.  The Division will have the sole 		discretion as to whether the bidder's substitution meets the requirements of the specifications.

X8.0	SPECIFICATIONS – CAB AND CHASSIS

Manufacturer: ________________________________	Model: _____________________

X8.1	GVW plate rating: ____________ Lbs.

X8.2	Cab to axle dimension: __________ Inches.

X8.2.1		Cab to end of frame: _________ inches

X8.3	Wheelbase: __________ inches, set forward design for our snowplow applications _____YES_____NO

X8.4	Frame: Will you provide a frame that meets or exceeds all Federal requirements for GVWR

specified that has an integral front frame extension with no frame cutouts except to allow engine

installation?									_____ YES _____ NO

Will extension extend forward of the grille area a minimum of l2 inches_____ YES _____ NO

Warranty on frame: _____ years and conform to the following:

X8.4.1		Frame steel: 120,000 PSI yield strength minimum		_____ YES _____ NO

X8.4.2		R.B.M.: ______________ Ins./Lb.

X8.4.3		Is the truck chassis frame rails free of obstructions inside the frame rails and along the left

outside frame rail 23 inches to 38 inches from the back of the cab for installation of the

spinner chute								_____ YES _____ NO

X8.4.4		Have you omitted the factory installed bumper and complied with our building of a front bumper

_____ YES _____ NO

X8.5	Cab:  Is cab manufacturer’s standard steel and/or fiberglass and/or aluminum with premium or

manufacturers highest level interior trim with inside noise level rating not to exceed 80 dba in

compliance with Federal regulations					_____ YES _____ NO

Does it have an ambient temperature display for outside temperature _____ YES _____ NO

Is hood a tilt hood and fenders either steel and/or fiberglass		_____ YES _____ NO

Is rear air bag suspension provided					_____ YES _____ NO

Inner fender panels that are adequate to keep materials from engine compartment

_____ YES _____ NO

X8.5.1		Is unit equipped with manufacturers tilt steering column with cruise control feature

_____ YES _____ NO

OR

Provide locking hand operated throttle			_____ YES _____ NO

X8.5.2		Seats:

Driver – Fully adjustable high back with head rest, air ride, bucket style; seat includes air

lumbar, hip bolsters, side bolsters, and back bolsters, with full cloth on entire seat

_____ YES _____ NO

Material is Modura _____ YES _____ NO OR approved equal: ____________________

X8.5.2.1		Passenger seat fully adjustable high back with head rest, air ride, bucket style, cloth

covered or cloth insert in vinyl			_____ YES _____ NO

Clearance between drivers and passenger seats ______ inches

X8.5.3		Floor mats: Rubber floor mats throughout cab area with non-absorbent backing under mats

_____ YES _____ NO

X8.5.4		Heater and defroster: Fresh air type, heaviest duty		_____ YES _____ NO

X8.5.5		Windshield wipers and washers: Manufacturers heaviest duty artic type with intermittent feature

_____ YES _____ NO

Wipers equipped with snow type blades			_____ 	YES _____ NO

X8.5.6		Instruments:  Are manufacturer’s gauges with visual and/or audible, and/or

programmable warning to inform driver when operating conditions are exceeded included:

X8.5.6.1		Voltmeter or ammeter					_____ YES _____ NO

X8.5.6.2		Engine RPM tachometer					_____ YES _____ NO

X8.5.6.3		Speedometer with odometer				_____ YES _____ NO

Are provisions for dual speedometers leads available_____ YES _____ NO

X8.5.6.4		Air pressure gauge(s)					_____ YES _____ NO

X8.5.6.5 		Air filter to be manufacturers heaviest element type	_____ YES _____ NO

X8.5.6.6		Air filter restriction indicator dash mounted		_____ YES _____ NO

X8.5.6.7		Engine hourmeter (controlled by engine operation) 	_____ YES _____ NO

X8.5.6.8		Fuel gauge(s) with low fuel warning indicator	_____ YES _____ NO

X8.5.6.9		Is unit equipped with front air intake			_____ YES _____ NO

Is an air actuated or cable control valve provided to enable operator to divert air

intake to engine compartment while in snow plowing application

_____ YES _____ NO

X8.5.6.10		Oil pressure gauge					_____ YES _____ NO

X8.5.6.11		Temperature gauge					_____ YES _____ NO

X8.5.6.12		Low coolant indicator					_____ YES _____ NO

X8.5.7		Accessories:

X8.5.7.1		Manufacturers dash mounted extended two (2) cup drink holder

_____ YES _____ NO

X8.5.7.2		Air horns with snow shields				_____ YES _____ NO

If cab mounted, adequate clearance for future installation of dump body cab protector

_____ YES _____ NO

Single horn without snow shield			_____ YES _____ NO

Mounted downward on frame rail under hood	_____ YES _____ NO

X8.5.7.3		Rearview Mirrors:

Heated dual, West Coast Type _____ YES _____ NO     Size: _______________

Power adjustable with convex spot mirror ___ YES ___ NO

(OR)

dual flat mirrors (Size: __________________) and power adjustable with separate dual (Size: _________________) convex spot mirrors ___ YES ___ NO

to include fore and aft breakaway feature with corrosive resistant finish equal to stainless

steel, powder coat or aluminum or molded plastic housing and mounting brackets

_____ YES _____ NO

X8.5.7.4		Grab Handle:

Right hand and left hand sides internal or external mounting to rear of door opening

_____ YES _____ NO

If inside handles, one (1) outside, left, mounted grab handle with non-slip insert for

bed aggregate inspection furnished			_____ YES _____ NO

X8.5.7.5		Glass:  Manufacturers tinted safety glass; front, sides, and rear_____ YES _____ NO

X8.5.7.5.1			Dual power windows				_____ YES _____ NO

X8.5.7.6		Radio:  Manufacturers standard AM/FM stereo	_____ YES _____ NO

Weather band radio feature			_____ YES _____ NO

X8.5.7.7		Air Conditioning:  Manufacturers fresh air type heaviest duty with APADS or equivalent

RCD system to include replaceable fresh air filter	_____ YES _____ NO

X8.5.7.8		Manufacturers stationary grille or grille with cutout area to allow tilt hood to clear

snow plow mount						_____ YES _____ NO

Bug screen provided behind grille			_____ YES _____ NO

X8.5.7.9		Front mudflaps manufacturers standard for unit bid	_____ YES _____ NO

X8.5.7.10		Emergency triangle warning kit, with hold down or stowed in the cab

_____ YES _____ NO

Make/Model: ________________________

X8.5.7.11		Does unit include kit for front mounted CB radio and all power and ground wiring to 				include co-ax cable, antenna, speaker, etc.		_____ YES _____ NO

All cable and wiring routed using grommets and wire looms

_____ YES _____ NO

Radio make and model: ______________________________________

X8.5.7.12		Two (2) front frame mounted tow hooks or eyes	_____ YES _____ NO

X8.5.7.13		Accessories included in manufacturers standard cab not listed above:

__________________________________________________________________

__________________________________________________________________

X8.6	Engine:

Make: _____________________________		Model: _______________________

__________ HP . 		Torque @ __________ Lb. Ft.

X8.6.1		Has engine manufacturer made provisions for front mounted hydraulic pump to crankshaft pulley

_____ YES _____ NO

X8.6.2		Fuel heater/water separator mounted inside engine compartment _____ YES _____ NO

Manufacturer: _________________

X8.6.3		Engine block heater ________ watt/ ________v rating includes weather proof spring 
		loaded cap over plug  	_____ YES _____ NO

X8.6.4		Single vertical exhaust pipe with horizontal muffler that meets all Federal noise

abatement requirements					_____ YES _____ NO

Exhaust frame mounted on the passenger side of unit with heat shield on vertical exhaust

_____ YES _____ NO

X8.6.5		Engine equipped with engine brake 	_____YES_____NO

Compression ____ YES ____ NO (or) Compression/Exhaust _____ YES _____ NO (or)

Exhaust _____ YES _____ NO

Manufacturer: _______________

X8.6.6		Is engine oil pan zinc nickel plated	_____ YES _____ NO

(OR)

Aluminum _____ YES _____ NO	(OR)	Non-Corrosive coated _____ YES _____NO

X8.6.7		Engine provides electronic speed control including throttle and cruise control features

_____ YES _____ NO

X8.7	Cooling System:

X8.7.1		Is cooling system capable of maintaining engine temperature within the manufacturers

recommended range during continuous winter/summer operation_____ YES _____ NO

Does unit provide an automatic “on-off” fan drive with nylon fan blades

_____YES _____NO

Manufacturer: ________________________

X8.7.2		Will the system be filled with permanent type extended life coolant Dex-Cool or equivalent

rated at a -34ºF minimum						_____ YES _____ NO

X8.7.3		Does the radiator provide adequate clearance to facilitate the installation of a crankshaft

driven PTO drive shaft						_____ YES _____ NO

The distance between the extreme tip of the radiator fan blade and the centerline of the

crankshaft is ______ inches to insure adequate clearance for PTO drive shaft

Radiator and heater hoses are silicone type or approved equivalent with constant torque clamps

or equivalent utilized on radiator hoses to minimize cold water leaks _____ YES _____ NO

X8.8	Fuel Tank:

X8.8.1		Capacity: ______ US gallons.  Does tank comply with FMVSS	_____ YES _____ NO

Filler Cap is chain tethered	_____ YES _____ NO

X8.9	Electrical System:

X8.9.1		Type: _____ volt negative ground system includes manual reset circuit breakers (main panel)

SAE Type III with trip indicators to replace all fuses except for 5 amp fuses._____YES_____NO

X8.9.2		Batteries:

X8.9.2.1		Cold Crank AMPS _________ AMPS with sealed terminals

X8.9.2.2		Jump start studs mounted on outside of battery box 		_____ YES _____ NO

X8.9.3		Alternator Capacity: __________ AMPS brushless with internal regulator

X8.9.4		Lighting:All lighting conforms to the West Virginia Motor Vehicle Code

_____YES_____NO

Unit features daytime running lights			_____ YES _____ NO

Cab marker lights are LED type with halogen headlamps.	_____ YES _____ NO

X8.9.5		Is auxiliary snow plow lighting package included			_____ YES _____ NO

X8.9.5.1		Will truck vendor eliminate rear taillights			_____ YES _____ NO

Is there at least eight (8) foot of wiring bundled at end of frame for body vendor

hookup of taillights provided in dump bed body		_____ YES _____ NO

X8.9.6		Will manufacturer _____ YES _____ NO or successful vendor _____ YES _____ NO make

provisions for manufacture approved wiring and weatherproof disconnect plug

_____YES _____NO

Manufacturer and Part number_________________________________________________

Will there be three (3) foot “pigtail” to operate front combination left and right turn/park

lights/auxiliary headlights.						_____ YES _____ NO

X8.9.6.1		Is weatherproof disconnect plug located at lower left front grille/bumper area

_____ YES _____ NO

Are all wiring connections weatherproof with wiring encased in wire looms

_____ YES _____ NO

X8.9.6.2		Are provisions for 7-way trailer connection light socket mounted at rear of truck frame

_____ YES _____ NO

Manufacturer and Part number___________________________________

X8.9.6.3		Will manufacturer provide body builder circuit interface capability with connection

Plug located at rear of frame for body builder connection to stop, tail, and marker

light circuits, ignition controlled auxiliary feed to ground to provide splice free

chassis wiring integrity					_____ YES _____ NO

X8.9.6.4		Will manufacturer provide body builder circuits – three (3) switches located in the

dash instrument panel with one (1) weather protected body builder connection box

or module located at the rear under cab.			_____ YES _____ NO

Is this power module 20 amps per channel, 80 amp maximum output														_____ YES _____ NO

Do the dash switches control the power module with LED backlighting

_____ YES _____ NO

X8.10	Transmission

Manufacturer: ___________________________________	Model: _______________________

X8.11	Driveline: __________________________________

Does it have a greasable main shaft						_____ YES _____ NO

X8.12	Rear Axle:

X8.12.1	Rated Capacity: __________ Lbs.  Single reduction includes driver controlled main locking

differential								_____ YES _____ NO

X8.12.2	Rear Spring Capacity: __________ Lbs. including __________ lb. capacity load stabilizer

Springs								_____ YES _____ NO

Does it provide sufficient clearance between spring, brake chambers, and tires to operate

with single tire chains						_____ YES _____ NO

X8.12.3	Gear ratio: ___________________

Are vehicles capable of a top speed of 70 MPH			_____ YES _____ NO

X8.12.4	Is rear axle differential, transmission, and front wheel lubrication reservoirs filled with

synthetic type lubrication and provided with magnetic drain plugs where applicable

_____ YES _____NO

X8.13	Front Axle:

X8.13.1	Capacity: __________ lbs. I-beam type

X8.13.2	Front Spring Capacity: __________ lbs.;   __________ lbs. rating for use with front plow

X8.13.3	Manufacturers heavy duty shock absorbers _____YES _____NO   Make:__________________

X8.13.4	Front wheel oil lubricated wheel seals_____ YES_____NO	  Make:_______________________

X8.14	Brakes:

X8.14.1	Type: Full air, with manufacturers ABS with traction control in compliance with the most

current FMVSS requirements					_____ YES _____ NO

X8.14.2	Compressor: Model and Make: ________________________________        ________CFM

X8.14.3	Service Brake Size:

X8.14.3.1		Front: ______________________

X8.14.3.2		Rear: _______________________

X8.14.4	Parking Brake: Spring set, air release actuating rear axle service brakes _____YES_____NO

Instrument panel control_____ YES _____ NO     __________MGM

X8.4.4.1		Are all brake chambers sealed brake chambers with epoxy exterior coat on front and rear

chambers 		_____ YES _____ NO      	Make: _________________

X8.14.5	Air dryer with heater _____ YES _____ NO    Make and Model: _________________________

X8.14.6	Manufacturer’s standard air tanks for service brakes; auxiliary tank for parking brake

_____ YES _____ NO

X8.14.7	Low air pressure warning light and buzzer			_____ YES _____ NO

X8.14.8	Do brakes meet all current Federal and State FMVSS requirements _____ YES _____NO

X8.14.9	Are brake dust covers installed on all wheels			_____ YES _____ NO

X8.14.10	Is unit equipped with tractor protection valve and hand control valve to accommodate

installation of glad hands at rear of frame rails to enable unit to pull an air-braked trailer

_____ YES _____ NO

X8.14.10.1		Are glad hand recessed as not to stick out past end of frame rails

_____ YES _____ NO

X8.15	Tires and Wheels:

X8.15.1	Wheel, Front and Rear ______ x ______ hub piloted steel disc type, to accommodate

specified tire size							_____ YES _____ NO

Make and Model: ________________________ with 0.472 inches thickness_____YES_____NO

All wheels include wheel guard separators			_____ YES _____ NO

X8.15.2	Tires: (Describe)

X8.15.2.1		Front: __________________________________________________________________

X8.15.2.2		Rear: __________________________________________________________________

X8.16	Manufacturers standard power steering for front axle specified	_____ YES _____ NO

Manufacturer: ________________________________

X8.17	Features considered as standard equipment not specifically addressed:

___________________________________________________________________________________

___________________________________________________________________________________

X8.18	Paint:

X8.18.1	Specify cab exterior and interior color and paint type:

_____________________________________________________________________________

X8.18.2	Is truck grille manufacturer’s standard similar to silver/aluminum in color?_____ YES _____NO

X8.18.3	Are fuel tanks, steps, air tanks and battery box non-corrosive coated? _____ YES _____ NO

X8.18.3.1		Is wheel paint provided as specified?			_____ YES _____ NO

X8.18.4	Detail/Decorative Stripes with Logo:

X8.18.4.1		Are stripes provided 2” type with taper at front of hood?	_____ YES _____ NO

X8.18.4.2		Does the conspicuity striping material provided meet requirements of Section

8.18.4.3 through 8.18.4.6 of the specification section? 	_____ YES _____ NO

Will you install the striping?				_____ YES _____ NO

X8.18.4.7		Is your proposed paint plan attached with your bid?		_____ YES _____ NO

If not, why?	______________________________________________________

X8.18.4.8		Will you use manufacturer’s standard plant procedures for prepping of cab for painting?

_____ YES _____ NO

X8.19	Does the proposed unit meet or exceed the “OSHA of 1970” and/or subsequent changes?

_____ YES _____ NO

X8.20	Does the unit conform to the advertising guidelines? (Describe)

________________________________________________________________________________

________________________________________________________________________________

X8.21	Preventive Maintenance and Operator’s Training School:

X8.21.1	Will a preventative maintenance and operator’s training seminar be provided?

_____ YES _____ NO

X8.21.2	If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors,

required in conducting the training?					_____ YES _____ NO

X8.21.3	Will all manuals, booklets, etc. exp0lainint preventive maintenance, operator procedures, and

service schedule be delivered with each unit?			_____ YES _____ NO

If NO, explain______________________________________________________

X9.0	SPECIFICATIONS – 304 STAINLESS STEEL COMBINATION DUMP/SPREADER BODY

The bidder should complete the following schedule in order for the Division to compare the actual bid

unit to the specifications.  Should the bidder except a requirement, then such exception may be only on

the basis that such feature is not offered by the manufacturer.  The Division will have the sole discretion

as to whether the bidder’s substitution meets the requirements of the specifications.

Reference Requisition No. on request for proposal: ______________________

Bidder’s Name: _______________________________________________________________

Address: _____________________________________________________________________

Telephone Number: ____________________________________________________________

Years Company has been an authorized dealer for proposed unit: ________________ Yrs.

Manufacturer, model, series, and date of manufacture of proposed combination dump/spreader body:

_________________________________________________________________________________

_________________________________________________________________________________

Is descriptive literature, fully describing proposed dump/spreader body attached to your bid?

_____ YES _____ NO

If NO, why __________________________________________________________________

Refer to Section 6.1 of the specification

When will required number of operating manuals, service manuals, and complete parts list be delivered

to the Equipment Division at Buckhannon?  ___________ prior to delivery of unit or _______________

Will combination dump/spreader body have minimum 2 year basis warranty including parts and labor excluding abuse and normal wear items				_____ YES _____ NO

X9.1	Body capacity ______ cubic yards water level

X9.2.	Sideboard pockets and tailgate height provide additional capacities of _____ cubic yard

X9.3	Front body bulkhead 3/16 inch 304 stainless steel				_____ YES _____ NO

X9.4	Cab shield has sufficient clearance to ensure shield will not hit exhaust when dumping on uneven 	terrain?									_____ YES _____ NO

X9.5	Two (2) front truck frame mounted tow hooks or eyes accessible through the bumper

_____ YES _____ NO

X9.6	Dimensions:

X9.6.1		Inside length of body __________ inches

X9.6.2		Inside width of body __________ inches wide to maximize capacity and lower the center of

gravity of the unit

X9.6.3		Outside width of body __________ inches at the integral fenders

X9.6.4		Body spacing from cab __________ inches

X9.6.5		Basic minimum side height __________ inches (measure from the floor to top rail)

X9.6.6		Tailgate minimum height __________ inches (measure from the floor to top rail)

X9.6.7		Body overhang __________ inches to __________ inches (measure from center of hinge pin)

X9.6.8		Cab protector __________ inches x __________ inches with adequate clearance for cab mounted

air horns

X9.7	Is cab protector sloped rearward for drainage purposes			_____ YES _____ NO

X9.8	Construction of the body sides, front, head, and tailgate conform to the following minimum

Specifications

Steel types are 304 stainless steel						_____ YES _____ NO

X9.8.1		Floor: __________ inch thickness

X9.8.2		Sides: __________ inch thickness

X9.8.3		Tailgate plate:  __________ inch thickness

X9.8.4		Top rail: __________ inch thickness

X9.8.5		Cab protector: __________ gauge

X9.8.6		Longitudinal: ______ inch ______ gauge 304 stainless steel formed inner/ ______gauge 304

stainless steel formed with internal stainless steel gussets every ______ inches

X9.8.7		For future potential pre-wet application, will the combination body be capable of accepting

frame mounted approximately 85 gallon poly liquid tanks.	_____ YES _____ NO

Will the body be designed to allow maximum protection to the tanks _____ YES _____ NO

X9.9	Is all welding inside the body continuous, not skip welded. 			_____ YES _____ NO

Are all rails and posts continuous welded					_____ YES _____ NO

X9.10	Are the rear corner posts full length, one (1) piece construction		_____ YES _____ NO

X9.10.1	Is a rear bolt on spreader apron provided 			_____ YES _____ NO

Is it integrated into the rear of the bed				_____ YES _____ NO

X9.11	Cab protector sides, formed with gussets, extend forward ______ inches.  Clearance above highest point

of cab is _____ inches

X9.12	Is the body a unibody design – no crossmembers				_____ YES _____ NO

X9.12.1	The body has one (1) piece sides and floor which incorporates a sloping floor to side radius

to adequately feed material to the conveyor chain.		_____ YES _____ NO

X9.12.2	Do the sides of the body slope to the conveyor to facilitate self cleaning of body without raising

_____ YES _____ NO

X9.13	The boxed top rail is sloped inward to shed debris				_____ YES _____ NO

X9.14	Full length 304 stainless steel integral rear fenders which incorporate prewet liquid reservoirs (85

gallon)										_____ YES _____ NO

X9.15	An integrated center conveyor provides the ability of the body to convey granular materials with

the body down 								_____ YES _____ NO

The following features are provided:

X9.15.1	Does the conveyor have no more than 12 inch truck frame to body floor height for lower center

of gravity and lower mounting height					_____ YES _____ NO

X9.15.1.1		Have you used wood ____ YES ____ NO   Type of material: ______________________

X9.15.2	1/4 inch 304 stainless steel conveyor floor	_____ YES _____ NO or ¼ inch abrasion resistant

steel (AR400)								_____ YES _____ NO

X9.15.3	2 inch diameter front and rear shafts with eight (8) tooth sprockets	_____ YES _____ NO

X9.15.4	Drive sprockets are double keyed to shaft				_____ YES _____ NO

X9.15.5	Conveyor width – 25 inches or more					_____ YES _____ NO

X9.15.6	Conveyor is reversible						_____ YES _____ NO

X9.15.7	Conveyor is driven with 25:1 planetary gearbox drives or equal on both the front and rear shafts

with 5.0 CIR hydraulic motors					_____ YES _____ NO

One (1) motor has an integral conveyor speed sensor		_____ YES _____ NO

X9.15.8	Conveyor chain is D667K pintle type (24,500 lb. tensile/strand) with minimum 3/8 inch x 1 1/2 			inch conveyor crossbars welded to every link			_____ YES _____ NO

X9.15.9	A 10 gauge 304 stainless steel bolt in pan under the conveyor to keep material off chassis frame

_____ YES _____ NO

X9.16	The body has the capability to convey to the front or the rear with a material spinner for

distributing material:

X9.16.1	For front spreading, a front feedgate integrated into the head sheet of the body _____ inches x

_____ inches

X9.16.2	A 304 stainless steel front spinner chute is mounted between chassis frame rails and with

the body down be completely enclosed to prevent material from dropping on chassis drive

shaft  									_____ YES _____ NO

X9.16.3	For rear spreading, a _____ gauge 304 stainless steel _____ inch x _____ inch rear feedgate

in the body tailgate 							_____ YES _____ NO

X9.16.4	Is the rear feed gate lever operated ____ YES ____ NO or screw adjustable _____YES_____NO

Is the feedgate capable of being positively locked into position	_____ YES _____ NO

X9.16.5	The front spinner bracket and chute is mounted to the truck chassis frame and for rear

spreadingcapability the rear spinner chute and brackets are installed by the successful vendor								_____ YES _____ NO

X9.16.6	The spinner assembly is universal and may be used at front or rear_____ YES _____ NO

X9.16.7	Spinner assembly is adjustable left to right, and up and down to assure accurate

placement of material on spinner disc to facilitate control of spread pattern.

_____ YES _____ NO

X9.16.8	10 gauge 20 inch diameter spinner disc has replaceable machined hub _____ YES _____ NO

X9.16.9	Is the spinner 409 or 304 stainless steel				_____ YES _____ NO

X9.16.10	If spinner hydraulic motor is mounted on top of spinner disc, is the motor enclosed in a

removable material shedding protective cover			_____ YES _____ NO

X9.17	Hydraulic Hoist:

X9.17.1	Trunnion Mount _____ YES _____ NO

X9.17.2	Telescopic hoist is no less than N.T.E.A. Class 40			_____ YES _____ NO

X9.17.3	Single hoist cylinder is trunnion mount _____ YES _____ NO

X9.17.4	Hoist cylinder has three (3) stages with _____ inches of stroke with a four (4) inch diameter

first Stage								_____ YES _____ NO

Manufacturer and part number: _________________________

X9.17.5	The cylinder has wear and corrosion resistant nitrided cylinder tubes _____ YES _____ NO

X9.17.6	Cylinder warranty: ______ years

X9.17.7	A five (5) degree oscillating cylinder collar protects the cylinder against side stress 													_____ YES _____ NO

X9.17.8	The body has 6 inch x 8 inch x 1/2 inch structural angle rear hinge assembly installed in the

truck chassis frame							_____ YES _____ NO

X9.17.9	The rear hinge assembly has cold roll steel hinge pins connecting to 2 1/2 inch

hinge blocks with grease zerks					_____ YES _____ NO

X9.18	The following features are included:

X9.18.1	Warning light (bed raised) control console mounted		_____ YES _____ NO

X9.18.2	Hydraulic oil level reading						_____ YES _____ NO

X9.18.3	Safety decals as required						_____ YES _____ NO

X9.18.4	304 stainless steel mud guards, 10 gauge x 24 inches x 30 inches permanently attached in

front of rear wheels							_____ YES _____ NO

Will exhaust stack be aligned for body clearance			_____ YES _____ NO

X9.18.5	304 stainless steel shovel bracket					_____ YES _____ NO

X9.18.6	304 stainless steel gussets (board pockets) for 4 inch x 6 inch lumber (rough) located at

front and rear and mid-rail						_____ YES _____ NO

4 inch x 6 inch (rough) oak sideboards supplied and bolted through the gussets

_____ YES _____ NO

Painted aluminum to match the body				_____ YES _____ NO

X9.18.7	Does the unit have air operated tailgate with dual brake chamber air tailgate latches (one

on each side) 								_____ YES _____ NO

Pivot shafts included stainless steel bushings to eliminate seizing_____ YES _____ NO

X9.18.8	1 1/2 inch 304 stainless steel grip strut walk rail installed on both sides of the body

_____ YES _____ NO

X9.18.9	OSHA approved backup alarm, electronic ambient, adjusts to background noise, 112 dba

shock mounted at the rear						_____ YES _____ NO

X9.18.10	OSHA approved body support, both sides				_____ YES _____ NO

X9.18.11	Unit equipped with 49,000 lb. capacity pintle hook centered between rear frame rails

_____ YES _____ NO

Manufacturer and Model: ___________________________________

Height from ground level to center line of pintle “eye”: _____ inches

X9.18.12	Air deflector-hood mounted, blue or smoke			_____ YES _____ NO

Deflector manufacturer’s standard width for truck mode	_____ YES _____ NO

Width: _________________

Access to front end hood tilt handle				_____ YES _____ NO

Extra handle								_____ YES _____ NO

X9.18.13	Is screen over hopper provided with 3/8 inch rod across 3/8 inch rod for 2 ¾ inch grid

opening (to prevent oversize material from entering hopper during filling)

_____ YES _____ NO

X9.18.14	Is screen frame ¼ inch by 1 ½ inch angle iron welded to rods and hinged to 5 inch I-beams

_____ YES _____ NO

X9.19	Lighting: Weather/shock resistant lights LED type with average amp draw between .045 - .72

_____ YES _____ NO

Manufacturer and Model: _____________________________________

All connections have sure snap plug assemblies and epoxy sealed electronics to protect against shock

and vibration									_____ YES _____ NO

X9.19.1	All marker lights 2 1/2 inch diameter flush mount sealed beam lights with integral reflector

mounted in rubber base						_____ YES _____ NO

X9.19.2	All ground wires attached with plated steel fasteners			_____ YES _____ NO

X9.19.3	Rear lights shock mounted, recessed oval stop, tail, turn, and recessed oval back up lights

mounted in back post							_____ YES _____ NO

Strobe lights marked and switched from dash board location	_____ YES _____ NO

Make and Model: ___________________________________

X9.19.4	Center rear I.D. lights three (3) located in truck chassis		_____ YES _____ NO

X9.19.5	Two (2) amber oval LED strobe lights mounted at the front corners of the cab protector, and two

(2) amber oval LED strobe lights mounted at each outside corner of the cab protector

_____ YES _____ NO

Make and Model: ____________________________________

Strobe lights marked and switched at dash board location		_____ YES _____ NO

X9.19.6	Auxiliary headlights for snowplowing application shock mounted on fender of unit

_____ YES _____ NO

Make and Model: _____________________________________

X9.19.7	Two (2) oval amber LED strobe lights mounted at top of rear corner posts right and left sides and

switched in combination with cab protector strobe			_____ YES _____ NO

Manufacturer and Model: ___________________________________

X9.19.8	Two (2) rear frame mounted tow hooks				_____ YES _____ NO

X9.19.9	Lighted license plate bracket						_____ YES _____ NO

X9.20	Are the following at the front or rear both sides of the body:

X9.20.1	304 stainless steel fold down ladder that locks into position when either in the down or up

position								_____ YES _____ NO

X9.20.2	Two (2) 304 stainless grab handles					_____ YES _____ NO

X9.21	Tailgate (304 stainless steel):							_____ YES _____ NO

X9.21.1	Tailgate hinged at top, flame cut hardware, pork chop type off-set hardware to achieve maximum

opening of tailgate, but has provision for pivoting at the bottom	_____ YES _____ NO

X9.21.2	Flush mount, 1/2 inch flame cut 304 stainless steel tailgate pivots	_____ YES _____ NO

X9.21.3	Heavy duty offset hinge plates, one (1) inch flame cut 304 stainless steel_____ YES _____ NO

X9.21.4	3/4 inch 304 stainless steel latch hooks with 3/8 inch 304 stainless steel latch plates

_____ YES _____ NO

X9.21.5	Full perimeter 304 stainless steel boxing with all horizontal edges sloped outward

_____ YES _____ NO

X9.21.6	Two (2) 10 gauge 304 stainless steel sloped horizontal braces that are flush with perimeter

Boxing								_____ YES _____ NO

X9.21.7	7 gauge 304 stainless steel 10-12 inch x 24-26 inch rear feedgate _____ YES _____ NO

X9.21.8	Cold roll steel upper pins with grease zerks				_____ YES _____ NO

X9.21.9	Top hinge channel has removable, chain tethered keeper pins	_____ YES _____ NO

X9.21.10	Latching action at the bottom of gate operable by the truck driver without leaving the truck cab

_____ YES _____ NO

X9.21.11	Gate is self aligning							_____ YES _____ NO

X9.21.12	Tailgate lower latch pins 304 stainless steel 1 1/4 inch diameter	_____ YES _____ NO

X9.21.13	Body integrated or bolt on 304 stainless steel 15 inch spreader apron_____ YES _____ NO

X9.22	Design and strength characteristic of the entire body such that the unit structural members and the

hoisting system will not suffer any deformation, damage, or structural failure resulting from raising a

distributed full payload							_____ YES _____ NO

X9.23	Bumper:

X9.23.1	Bumper formed out of 1/4 inch roll steel _____ YES _____ NO

Weighs _____ lbs. per square foot

X9.23.2	Bumper face covers all of truck frame (_____ inches) with two (2) flanges of _____ inches top

and bottom 								_____ YES _____ NO

X9.23.3	Overall width of bumper: ________ inches

X9.23.4	Bumper straight across front from centerline of truck chassis _____ inches each side of

Centerline, making bumper straight ______ inches long in center with ends swept back

______ degrees and ______ inches each side.

X9.23.4.1		Does bumper have two (2) access holes for utilization of tow hooks _____YES_____NO

X9.23.5	Upper and lower flanges cut and welded solid at point where bumper is bent and ground off

smooth									_____ YES _____ NO

X9.23.6	Bumper mounted by two (2) mounting angles bolted to front of truck frame with two (2)

5/8 inch bolts each side						_____ YES _____ NO

X9.23.7	Mount angle ______ inch x ______ inches x ______ long with four (4) 5/8 inch holes

_____ YES _____ NO

X9.23.8	Paint on front bumper: ______________________________________________________

X9.24	Underbody Tool Box:

X9.24.1	One (1) tool box mounted under body on right side frame rail	_____ YES _____ NO

X9.24.2	Tool box ______ inches high, ______ inches wide, ______ inches deep cradled by a heavy steel

angle frame attached to the truck frame				_____ YES _____ NO

X9.24.3	Construction ______ gauge, ______ galvanneal steel with all seams welded

_____YES_____NO

X9.24.4	Tool box has horizontal hinged fold down door			_____ YES _____ NO

X9.24.5	Tool box door has cable or chain to hold the door in a horizontal position _____ YES _____ NO

X9.25	Load covering system electrically or air controlled				_____ YES _____ NO

X9.25.1	Electric motor assembly includes 12 volt direct drive motor with forward and reverse action, cab

mounted control switch, resettable circuit breaker			_____ YES _____ NO

X9.25.2	Pivot arm assembly constructed in a two (2) piece bent arm configuration of _____ inch

_____ gauge steel tubing						_____ YES _____ NO

X9.25.3	Bent arm extensions constructed of ______ inch ______ gauge steel tubing

X9.25.4	Rear cross constructed of _____ inch _____ gauge steel tubing

X9.25.5	Pivot arm rests included						_____ YES _____ NO

X9.25.6	Underbody spring extension spring ______ inches in length attached to base of pivot arm and of

body with articulating spring mounting bracket			_____ YES _____ NO

X9.25.7	All steel components finished with manufacturer’s recommended rust preventative system with

adequate primer and paint						_____ YES _____ NO

X9.25.8	Steel cab protector mounted triple bend wind deflector provided	_____ YES _____ NO

X9.25.9	Load covering system provided with a _____ oz. black vinyl tarp to fit 14 foot 6 inch body

_____ YES _____ NO

X9.25.10	Load covering system supplied with all necessary hardware and delivered to the West

Virginia Division of Highways as a complete and operational unit._____ YES _____ NO

X9.26	Paint:  Describe proposed method of painting

X9.26.1 – X9.26.4

__________________________________________________________________________________________

__________________________________________________________________________________________

__________________________________________________________________________________________

X9.27	Detail/Decorative Stripes with Logo:

Will striping and detailing you provide comply with requirements of Section 9.27.1 through 9.27.7

_____ YES _____ NO

X9.28	All body features considered as standard, but not specifically addressed:

__________________________________________________________________________________________

__________________________________________________________________________________________

X9.29	Does the proposed unit meet or exceed the “OSHA OF 1970” and/or subsequent changes

_____ YES _____ NO

X10.0	SPECIFICATIONS - CENTRAL HYDRAULIC SYSTEM

Is the central hydraulic system designed to operate the following:

A front mounted telescopic dump body hoist cylinder, a hydraulically driven integrated salt and abrasive

spreader system requiring the simultaneous operation of two (2) hydraulic motors in two (2) different

modes with conveyor reverse, a single acting snowplow lifting cylinder, a snowplow power angle

system, and an auxiliary equipment drive circuit			_____ YES _____ NO

Are provisions made for a future add on hydraulic driven pre-wet system_____ YES _____ NO

Bidder: _____________________________________________________________________________

Address: ____________________________________________________________________________

Telephone Number: ___________________________________________________________________

Years company has been an authorized dealer for proposed unit: __________ years

Manufacturer, model, series, and date of manufacture of proposed central hydraulic system:

____________________________________________________________________________________

____________________________________________________________________________________

Is descriptive literature full describing proposed central hydraulic system attached to your bid

proposal?	 								_____ YES _____ NO

If NO, refer to specification statement Section 6.6

When will required number of operating manuals, service manuals, and complete parts list be delivered

to the Equipment Division at Buckhannon?__________ prior to deliver of unit or __________________

Pre-Wet system:

Does spreader control contain the ability to control a closed loop pre-wet system

_____ YES _____ NO

Does system operate using a flow meter feedback circuit			_____ YES _____ NO

Does controller software allow for adjustability of pre-wet output by operator, presented in gallons per to

Ton										_____ YES _____ NO

Is information related to pre-wet application rate and total flow in gallons displayed on the screen while

Pre-wet system is active							_____ YES _____ NO

Will central hydraulic system have minimum 2 year basis warranty including parts and labor excluding abuse and normal wear items					_____ YES _____ NO

X10.1	Pump System:

X10.1.1	Pump: Variable volume pressure compensated load sensing axial piston type

_____ YES _____ NO

X10.1.2	Front mounting flange and main housing/case of cast iron construction_____ YES _____ NO

Inlet and outlet port section of high strength ductile iron with SAE split flange porting

_____ YES _____ NO

X10.1.3	Is suction port and associated plumbing sized to allow for minimum inlet restriction

between the pump and the suction port on the reservoir		_____ YES _____ NO

Does installation comply with pump manufacturers allowable inlet condition specifications											_____ YES _____ NO

Is suction plumbing equal to or greater than pump inlet or suction size ____ YES ____ NO

X10.1.4	Is pressure port of the SAE split flange type or ORB side mounted for direct bolt mounting of solenoid shut down valve assembly					_____ YES _____ NO

X10.1.5	Case drain and load sense signal ports of the SAE O-ring type	_____ YES _____ NO

Case drain line taken directly to tank without passing through the return line filter

_____ YES _____ NO

X10.1.6	Input shaft has a minimum continuous torque rating equal to _____% of the imposed load

when pump is operated at maximum engine rpm, maximum displacement and system

pressure								_____ YES _____ NO

SAE “C” keyed							_____ YES _____ NO

X10.1.7	Front input shaft bearing heavy duty ball or roller type designed for high axial and radial loading

_____ YES _____ NO

Rear shaft bearing of the high speed and load sleeve type design	_____ YES _____ NO

Bearings fully lubricated by flooded case oil				_____ YES _____ NO

X10.1.8	Ramp/swashplate supported by pressure lubricated bearings of the rocker cam or saddle type for

high piston load support						_____ YES _____ NO

Ramp angle positioning by means of dual servo control cylinders for rapid pump response and

precise pump output control						_____ YES _____ NO

X10.1.9	Adjustable load sense and high pressure compensator control valve assembly of the full cartridge

or of bolt on housing design for ease of replacement and repair	_____ YES _____ NO

X10.1.9.1		System design and components provide flow, pressure and performance

requirements 	with a maximum operating load sense differential pressure of

______ PSI and a maximum standby pressure of ______ PSI for maximum

efficiency.

If pilot control shifted valving is used, is it designed to be fully functional within this

pressure range  						_____ YES _____ NO

X10.1.9.2		High pressure compensator valve preset to limit the maximum pump output pressure to

maximum required operating pressure plus load sense differential and margin pressure to

prevent premature de-stroking of ramp resulting in reduced or insufficient pump output

_____ YES _____ NO

X10.1.10	Pump Output:  Is it capable of providing hoist cylinder extension required for a 50 degree

Body dump angle in 13 seconds at 1500 engine RPM at a 1000 PSI system load

_____ YES _____ NO

X10.1.11	Is the make and model bid in compliance with overall quality of construction, design, and

performance of the pump supplied 					_____ YES _____ NO

X10.1.12	Pump:

Manufacturer and Model: ______________________________________________________

X10.1.13	Is pump manufacturers standard product release and design	_____ YES _____ NO

X10.1.14	Is pump driveline assembly of the keyed shaft design utilizing a 4 bolt driveshaft flange and

matching drive yoke on the pump 					_____ YES _____ NO

X10.1.14.1		Does driveline have a minimum continuous torque rating equal to 200% of the

imposed load when pump is operating at maximum system requirements

_____ YES _____ NO

Manufacturer and Model: _________________________________________________

X10.1.14.2		Are dual journals and yokes incorporated to connect the pump shaft and engine drive

flange with an angular misalignment no greater than six (6) degrees and not less than two

(2) degrees							_____ YES _____ NO

X10.2	Pump Shutdown System:

X10.2.1	Normally closed, energize to open, solenoid operated control valve of the cartridge and manifold

design to be directly bolted to pump pressure port			_____ YES _____ NO

Is solenoid electrical connection of the Packard “Weatherpack” type with “SO” cable wiring

_____ YES _____ NO

X10.2.2	Is valve controlled by a console mounted “Master On” switch with pilot lamp for normal system

operation and by a float switch located in hydraulic reservoir to automatically shut off pump

pressure port flow to all down stream functions in the event of low hydraulic oil level

_____ YES _____ NO

X10.2.3	Pressure drop across valve _____ PSI at _____ GPM flow when in the switched position

Nominal valve rating _____ GPM at _____ PSI

X10.2.4	SAE #6 gauge port equipped with Parker Hannifin Model PD361 diagnostic coupling nipple and

protective cap provided for pump output pressure testing to be installed in valve manifold and

within an easily accessible mounting position			_____ YES _____ NO

X10.2.5	Is valve designed to protect the pump from damage when the system is shut down at high

pressure and flow operation						_____ YES _____ NO

X10.2.6	Valve manufacturer and model: _________________________________________________

X10.2.7	Central control console mounted audio alarm and warning lamp indicating pump pressure/flow

shutdown								_____ YES _____ NO

X10.2.8	Warning lamp press-to-test light and incorporate a switching system into the automatic shutdown

assembly to simulate low oil level, shut off pump output flow and test float switch wiring and

connection								_____ YES _____ NO

X10.2.9	A console mounted electrical override function switch provided to allow momentary operation of

hydraulic functions in emergency situations				_____ YES _____ NO

X10.3	Directional Control Valve Assembly:

X10.3.1	Valve stacked section type and of closed center circuit design	_____ YES _____ NO

X10.3.2	Each work section pressure and flow compensated with fully integrated load sense network

_____ YES _____ NO

Flow output is relative to spool travel with preset maximum flow rate obtained at maximum

spool stroke providing feathering control of operated function	_____ YES _____ NO

X10.3.3	Dump body, snowplow lift, and snowplow power angle section of the manual cable shift type

_____ 	YES _____ NO

Auxiliary circuit section of the electric solenoid shift type		_____ YES _____ NO

Both ends of each section valve spool sealed with weather resistant caps or cable entry bonnets

_____ YES _____ NO

X10.3.4	Valve assembly flow capacity rating and pressure drop characteristics sufficient to provide

for the required pump output and circuit flow rates at the specified maximum load sense

differential pressure settings					_____ YES _____ NO

X10.3.5	All valve ports of the SAE o-ring seal type and of sufficient size to handle required section flow

rates at stated load sense differential pressure			_____ YES _____ NO

X10.3.6	Pressure compensation of the spinner and auger sections and also a priority section

installed to allow for operation of the plow hoist in any circumstance_____ YES _____ NO

X10.3.7	Main pressure inlet relief valve provided to reduce system pressure shock loads

_____ YES _____ NO

Is it preset at pressure so as not to interfere with pump pressure compensator and to prevent

premature relief opening at system high demand operation		_____ YES _____ NO

X10.3.8	If pilot pressure reducing valve is required for solenoid section control, design meets

operating requirements as set forth in Section 10.1.9.1		_____ YES _____ NO

Pilot supply and tank venting internal within the valve assembly section_____ YES _____ NO

X10.3.9	Load sense network high pressure relief provided and preset to limit system maximum operating

pressure								_____ YES _____ NO

Set point provides proper pressure margin to pump pressure compensator and high pressure relief

valve as to prevent premature loss of required flow rates and pressure capability

_____ YES _____ NO

X10.3.10	SAE #6 gauge port equipped with Parker Hannifin PD361 diagnostic coupling nipple with

protective cap for load sense testing to be installed in an easily accessible location

_____ YES _____ NO

X10.3.11	Dump body control section 3-way three (3) position spring centered cylinder spool for operation

of a single acting hoist cylinder					_____ YES _____ NO

X10.3.11.1		Full flow workport relief valve installed in power up port	_____ YES _____ NO

Set point to prevent operating pressure from exceeding hoist cylinder normal operating

pressure rating							_____ YES _____ NO

X10.3.11.2		Flow limiting system preset at required flow rates provides performance as stated in

Section 10.1.10 as maximum for dump body up and down to reduce system over demand

operation							_____ YES _____ NO

X10.3.12	Snowplow lift control section is 3-way three (3) position spring centered cylinder spool with

float detent for operation of a single acting lift cylinder with pilot controlled load lock valve

_____ YES _____ NO

Does the valve design require a load holding check valve to properly carry the plow weight

_____ YES _____ NO

X10.3.12.1		Full flow workport relief valve preset at maximum required unlock pressure installed in

power down workport						_____ YES _____ NO

Workport relief valve installed in power up workport if maximum system pressure output

setting exceeds normal operating pressure limit of plow lift cylinder

_____ YES _____ NO

Is a three (3) way valve provided for plow hoist circuit	_____ YES _____ NO

X10.3.12.2		Adjustable flow control installed to limit downward speed of

snowplow							_____ YES _____ NO

Flow limiting control system preset for proper plow lift speed to be supplied to reduce

over demand operation and to increase system efficiency	_____ YES _____ NO

X10.3.13	Snowplow power angle control section is 4 way three (3) position spring centered motor spool

for operation of worm gear driven type reversing system		_____ YES _____ NO

X10.3.13.1		Flow limiting control system preset for proper plow reversing speed to be supplied to

reduce over demand operation and to increase system efficiency _____YES _____NO

X10.3.14	Auxiliary equipment drive circuit control section 3-way three (3) position spring centered

solenoid operated motor spool					_____ YES _____ NO

Is the circuit separate and distinct from the spreader control system	_____ YES _____ NO

X10.3.14.1		Flow limiting control system preset to provide _____ GPM at a system load pressure

of _____ PSI.

Pump is capable of supplying this flow rate with engine speed of _____ RPM

_____ YES _____ NO

X10.3.14.2		Is an inline mounted control valve supplied for this operation in place of directional

control valve section						_____ YES _____ NO

If supplied, is proper interconnections and venting of load sense network system

provided							_____ YES _____ NO

X10.3.14.3		Is pressure line 3/4” SAE 100R2 hose and manifold mounted at rear of chassis and

equipped with Parker Hannifin SH6-62 quick disconnect coupler and protective metal

plug 								_____ YES _____ NO

Is mating nipple SH6-63 with protective cap supplied	_____ YES _____ NO

X10.3.14.4		Manufacturer and model of directional and auxiliary circuit valves:

_____________________________________________________________________

X10.3.15	Is directional control valve assembly with tank in an enclosure to protect it from the

elements								_____ YES _____ NO

X10.3.16	Pre-Wet Circuit:

X10.3.16.1		Is a separate circuit provided to control an add-on pre-wet system

_____ YES _____ NO

X01.3.16.2		Is the hydraulic valve of the sectional type ___ YES OR of the cartridge style contained in a manifold ___ YES

X10.3.16.3		Is a manifold type valve supplied _____ YES _____ NO  Is it attached to the main valve assembly						_____ YES _____ NO

X10.3.16.4		Is all wiring to the pre-wet hydraulic circuit provided as part of the system

_____ YES _____ NO

X10.3.16.5		Is the wiring to control console related to the rest of the pre-wet system (low level float, flow meter connection, etc.) provided as part of the pre-wet package at the time of pre-wet system install				_____ YES _____ NO

X10.4	Spreader Control Valve Assembly:

X10.4.1	Are spinner and conveyor solenoid flow controls of the PWM proportional solenoid type and

equipped with manual overrides 					_____ YES _____ NO

Are overrides manually adjustable over operating flow range in the event of electrical system

failure									_____ YES _____ NO

X10.4.2	Flow control circuits are pressure compensated			_____ YES _____ NO

Provides spinner flow rate of __________ GPM and a conveyor flow rate of __________ GPM

Pressure relief valve system limit circuits to __________ PSI

X10.4.3	Load sense circuits connected to directional control valve network for proper pump control

_____ YES _____ NO

Does design prevent improper high pressure load sense signal and pressure line loading

when spreader valve is not in use and when spreader quick disconnects are uncoupled

_____ YES _____ NO

X10.4.4	Is PWM solenoid control supplied by microprocessor spreader control system

_____ YES _____ NO

Are solenoids capable of 100% PWM signal without failure		_____ YES _____ NO

X10.4.5	Solenoid operated directional control valve and in-cab mounted electrical switch operates

spreader conveyor reverse required for front or rear material discharge selection provided

_____ YES _____ NO

X10.4.6	Is electrical switching and indicator light for spreader clogged indication provided

_____ YES _____ NO

X10.4.7	Manufacturer and model of valve: ________________________________________________

X10.5	Spreader Control System:

X10.5.1	Dual flow, ground speed oriented spreader control system of the closed loop microprocessor

based type with nonvolatile control memory				_____ YES _____ NO

X10.5.2	Automatic calibration and flexibility of programming		_____ YES _____ NO

X10.5.3	System is capable of operation in ground speed oriented closed loop conveyor feed back,

open loop, manual set, blast and unload modes and fully functional in both front and rear

material discharge selection						_____ YES _____ NO

X10.5.4	Automatic switchover with display indication from closed loop to open loop operation in the

event of loss of feed rate sensor signal is provided			_____ YES _____ NO

X10.5.5	Control console digital readouts capable of displaying actual application rate, vehicle ground

speed, distance of spread route driven and total quantity of material spread

_____ YES _____ NO

X10.5.6	Programming and output cable connection for material and trip information printer and program

uploading is provided							_____ YES _____ NO

X10.5.7	Control unit capable of accumulating display information up to 999,999 miles and 999,999 tons

of discharged material							_____ YES _____ NO

X10.5.8	Console programming capable of selection, calibration and display of four (4) separate spread

materials with independent application rates of each material capable of being set to fixed rates

or to rate increments of a preset maximum application rate		_____ YES _____ NO

X10.5.9	A variable digital access code lockout for application rate selection and for system operating

parameters is provided						_____ YES _____ NO

Is it a key switch							_____ YES _____ NO

X10.5.10	Backlighted switches and LCD screen utilized for on-board programming and for display

readout and application rate selection				_____ YES _____ NO

X10.5.11	Is material spread width selectable by no less than a 10 position switch with minimum and 			maximum spinner speed totally programmable through entire flow range

_____ YES _____ NO

Is spinner speed capable of linking to ground speed for on-off control _____ YES _____ NO

X10.5.12	Does display enunciate error message and sound audio alarm when microprocessor system

detects any loss of control or accuracy				_____ YES _____ NO

X10.5.13	Will system be fully functional at time of delivery		_____ YES _____ NO

X10.5.14	Is truck speed sensor compatible with type of speedometer drive system supplied on chassis

_____ YES _____ NO

X10.5.15	Is a built-in ground speed simulator provided either internal to the control or located in the

control console							_____ YES _____ NO

X10.5.16	Are all components required for proper installation and operation of control system onto

truck and spreader units supplied					_____ YES _____ NO

X10.5.17	Manufacturer and model of proposed control system	:

____________________________________________________________________________

X10.6	Central Control Console:

X10.6.1	Mounted between seats within easy access of the driver		_____ YES _____ NO

X10.6.1.1		Is warning light (bed raised) control console mounted	_____ YES _____ NO

X10.6.2	Will all wiring, valve control cables and electrical harness entry into cab and console

sealed with grommets						_____ YES _____ NO

X10.6.3	Are remote control valve levers console mounted			_____ YES _____ NO

Are all levers clearly marked as to function and operation		_____ YES _____ NO

X10.6.3.1		Remote control levers to operate push-pull type cables with .250” diameter stainless steel

rod ends							_____ YES _____ NO

X10.6.3.2		Is inner cable member 18-8 stainless steel armor wrapped construction with a low

resistance nylon liner and polyethylene covered tempered steel wire conduit

_____ YES _____ NO

X10.6.3.3		Is cable to valve connection of the weather resistant bonneted type_

____ YES _____NO

X10.6.3.4		Is hoist control lever OSHA compliant (hoist interlock)	_____ YES _____ NO

X10.6.4	Are central control console or dash mounted rocker switches with indicator lamps provided for

strobe lights, spreader light and plow lights isolated from all hydraulic system control circuits												_____ YES _____ NO

X10.6.4.1		Are interconnections and cables installed and ready for operation _____ YES _____ NO

X10.6.4.2		Is hydraulic system automatic shutdown system and control switching relay controlled 												_____ YES _____ NO

X10.6.4.3		Relay mounted within the cab		_____ YES _____ NO

X10.6.4.4		Is an access plate to internal wiring provided _____ YES _____ NO

X10.7	Hydraulic Reservoir and Valve Enclosure Assembly:

X10.7.1	Hydraulic reservoir _____ gallon operated capacity flex mounted to the chassis frame rail and

valve enclosure assembly						_____ YES _____ NO

X10.7.2	Tank constructed of _____ gauge 304 stainless steel		_____ YES _____ NO

X10.7.3	Tank equipped with a combination oil level sight glass and thermometer _____ YES _____ NO

X10.7.4	Tank equipped with a pressurized ten (10) micron filler/breather cap with removable 500 micron

strainer								_____ YES _____ NO

X10.7.5	Is an internal steel baffle provided within the tank			_____ YES _____ NO

X10.7.6	Tank stenciled with minimum of 1 1/2” high “Hydraulic Oil”	_____ YES _____ NO

X10.7.7	Tank level switch connection “SO” type wiring and mounted within tank/valve enclosure to

protect it from elements 						_____ YES _____ NO

X10.7.8	Pump supply suction port _____ inches NPT and system report port ______ inches NPT

X10.8	Filtration:

X10.8.1	Manufacturers standard filtration to adequately protect the hydraulic system from damage													_____ YES _____ NO

X10.8.2	Return line filter isolated from reservoir by a full flow non-restrictive type quarter turn brass ball

valve if filter is not installed in the reservoir				_____ YES _____ NO

X10.8.3	Each filter equipped with a differential pressure switch to indicate filter clogged condition by

means of a console mounted indicator lamp				_____ YES _____ NO

X10.8.4	One (1) extra replacement filter for each assembly is provided for each truck

_____ YES _____ NO

X10.8.5	Filter assemblies positioned as close to reservoir as possible and in an easily accessible service

location								_____ YES _____ NO

X10.9	Hoses and Fittings:

X10.9.1	Each hose assembly (hose with hose ends) except for suction hose is fitted with JIC swivel

connections on ends where connection to system component is made _____ YES _____ NO

X10.9.2	All pressure line hoses meet or exceed SAE Specification 100R2 and are equal to Gates high

pressure hose, type C2AT for sizes up to and including 1 inch ID	_____ YES _____ NO

X10.9.3	Suction hose 2 inch nominal ID and meet SAE Specification 100R4, braided fiber, spiral wire

reinforced, rubber covered hose with replaceable bolt-on type fittings _____ YES _____ NO

X10.9.4	All hydraulic hoses fully cleaned on interior, installed, and ready for operation

_____ YES _____ NO

X10.9.5	Are grommets used when routing hoses through steel bracketing or frame members

_____ YES _____ NO

X10.9.6	Snap tite quick disconnects (manifold mounted) supplied for the forward and rear spinner

1/2 Inch pressure and return lines					_____ YES _____ NO

X10.9.7	Are all fittings and connectors steel type designed for high pressure hydraulic system use

_____ YES _____ NO

X10.9.8	Pipe thread ported components and connectors are only used when the specific component is not

available with SAE or JIC porting					_____ YES _____ NO

X10.9.9	Are all pipe thread connectors used coated with liquid Teflon pipe sealer prior to assembly

_____ YES _____ NO

X10.9.10	Hoses that run to the front of truck chassis for snowplow functions are manifold mounted behind

the front bumper with sufficient access for pump service and snowplow hitch installation

_____ YES _____ NO

X10.9.11	Are snowplow lines equipped with complete 1/2 inch “VH” series Snap-tite quick disconnects

(coupler and nipple supplied) and metal caps and plugs		_____ YES _____ NO

X10.10	 Items not specifically stated but are necessary for proper system installation and operation are

supplied and comply with recommended hydraulic industry standards:

___________________________________________________________________________________

___________________________________________________________________________________

X10.11	Will initial servicing and pre-testing of hydraulic system be included for:

X10.11.1	Initial fill of reservoir with a high grade 32 AW hydraulic fluid to approximately 40 gallon level,

marked on sight glass			:				_____ YES _____ NO

X10.11.2	Start-up and initial run of hydraulic system, checking for leaks, excessive heat, system efficiency

_____ YES _____ NO

Will you replace any defective component				_____ YES _____ NO

Will you cover any defects discovered at time of plow installation if equipment is not available at

time of initial test of plow circuits					_____ YES _____ NO

X10.11.3	Refill reservoir to the 40 gallon operating level			_____ YES _____ NO

X10.12	 If any hydraulic lines are located within 10 inches of exhaust system are they metal lines and insulated

_____ YES  ____ NO

X10.13	 Are detailed component specifications, product literature, system component layout drawing with bill of

materials and full functional hydraulic system schematics in accordance with JIC and ANSI-Y32 format

attached with your bid							_____ YES _____ NO

X10.14	 If successful vendor, will you provide WVDOH with a complete list of all filters required for

normal maintenance on proposed unit					_____ YES _____ NO

X10.15	 Explain your training sessions with each purchase order (based on a purchase 1-25 units) covering the

operation, maintenance, trouble shooting and calibration/programming of the hydraulic system and

spreader controls and where will they be held:

___________________________________________________________________________________

___________________________________________________________________________________

___________________________________________________________________________________