WEST VIRGINIA DEPARTMENT OF TRANSPORTATION

DIVISION OF HIGHWAYS

EQUIPMENT DIVISION

BIDDER'S EVALUATION REPORT

PROCUREMENT SPECIFICATIONS FOR OPEN END CONTRACT

NO. 839-1-L

TRAILER MOUNTED SOLAR POWERED ELECTRIC ARROWBOARD

NOTE TO BIDDER:    Procurement Specification No. 839-1-L, Paragraph 2.0 recommends the completion and submittal of this Report with your bid.  Purpose of this Report is to enable the West Virginia Division of Highways Evaluation Committee to make full and fair evaluation of the bid.  Addendums in order, along with a summary of exception as a separate attachment, should be with Bidder’s Evaluation Report.

FAILURE TO SUBMIT THIS REPORT, COMPLETE IN ITS ENTIRETY, MAY SUBJECT THE BIDDER

TO DISQUALIFICATION.

Reference Requisition No.: ______________________

Bidder's Name:____________________________________________________________

Address:__________________________________________________________________

Telephone Number:_________________________________________________________

Years Bidder has been registered to do business with the State of West Virginia:  ______________YRS.

Years Company has been an authorized dealer for proposed unit:                        _______________YRS.

X3.2	Have you complied with all mandatory specifications?	_____ YES _____ NO

X4.2   	DELIVERY:

X4.2.1 	Delivery date of completed representative unit:________________ Calendar Days After 												Receipt of Purchase Agreement

X4.2.2 	Delivery date of balance of completed units:  ________________ Calendar Days After Receipt of

Purchase Agreement

X5.0	AWARD CRITERIA;

X5.1	Price per unit: 						________________per unit

X6.0   SPECIFICATIONS - GENERAL

X6.1   Manufacturer, model, series, and date of manufacture of proposed unit:

________________________________________________________________________

Is descriptive literature, fully describing proposed unit attached to your bid? _____ YES _____ NO

If not, why?______________________________________________________________

X6.2	Will the required number of service manuals, and complete parts list be delivered to the

Equipment Division at Buckhannon upon completion of delivery of total units?

_____ YES _____ NO

Will the required Equipment Preventive Maintenance Form (Section X6.2 of Bidders Evaluation Report) be provided upon inspection of the pilot unit?			_____ YES _____ NO

X6.2

2-10-00

EQUIPMENT PREVENTATIVE MAINTENANCE QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY SUCCESSFUL BIDDER OR MANUFACTURER’S TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT MODEL TO THE WVDOH.

DESCRIPTION: _______________________________________	MAKE: ___________________________________

MODEL: ________________________    	YEAR: __________	PURCHASE AMOUNT: ______________________

ENGINE:	MAKE: ______________________ 	MODEL: __________________ 	FUEL TYPE: ________________________

HORSEPOWER: _______________	CYLINDER: ________	ENGINE SERIAL: __________________________

COOLING SYSTEM CAPACITY: ______________________

BELTS:		DESCRIPTION:					PART NUMBERS:

___________________________________________	_________________________________________________

___________________________________________	_________________________________________________

GVW: _______________________AXLE CAPACITY:FRONT: ______________	REAR:______________

TIRES:		FRONT MAKE & SIZE: ______________________________________________

REAR MAKE & SIZE: _______________________________________________

DIMENSIONS OF UNIT:	LENGTH: __________		WIDTH: ______________	LENGTH: ___________

VENDOR CONTACT PERSON: ____________________________________		PHONE: __________________________

PARTS:

BATTERY MAKE: ____________________	MODEL: ___________________		CCA: _______________________

TOP OR SIDE POST: __________________	DIMENSIONS: LENGTH ________ WIDTH ________ HEIGHT __________

SPARK PLUGS OR FUEL INJECTORS MAKE: ______________	PART # __________________________________________

FUEL PUMP OR INJECTION PUMP MAKE: ________________	MODEL: _________________________________________

ALTERNATOR MAKE: __________________________________	PART #:__________________________________________

STARTER MAKE: ______________________________________	PART #: _________________________________________

TURBO CHARGER MAKE: ______________________________	PART #: _________________________________________

TRANS. MAKE: ____________________	MODEL: _________________________   AUTO/MANUAL: ____________________

HYDRAULIC PUMP MAKE: _____________________________	MODEL: _________________________________________

FILTERS		MAKE	PART NO.		LUBRICANT		MANUFACTURER TYPE

OIL		__________________________________	ENGINE	__________________________________________

AIR INNER	__________________________________	TRANSMISSION__________________________________________

AIR OUTER__________________________________	POWER STEERING _______________________________________

FUEL PRIMARY ______________________________	HYDRAULIC  	__________________________________________

FUEL SECONDARY ___________________________	DIFFERENTIALS _________________________________________

COOLANT	__________________________________	BRAKE FLUID 	__________________________________________

HYDRAULIC	_______________________________	COOLANT	__________________________________________

OTHER		__________________________________ 	OTHER 	__________________________________________

X6.3	TRAINING:

Will training seminar be conducted on Preventive Maintenance, Operator and Mechanic Training                      								_____YES _____ NO

Will you conduct training with each purchase order against this open end contract?

_____ YES _____ NO

Will training be conducted within 2 working days from the delivery of the pilot unit on the individual purchase order?								_____ YES _____ NO

If NO, explain time frame_____________________________________________________________

Will an Operator’s Manual be furnished directly to Training Academy prior to the

delivery of the pilot?		_____ YES _____ NO

X6.4   	If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors, required in conducting the training?		         _____ YES _____ NO

X6.4.1    	Will all manuals, booklets, etc. explaining preventive maintenance, operator procedures, and service schedule be delivered with each unit?           			_____ YES_____NO

If NO, explain _____________________________________________________

X6.5	WARRANTY AND SERVICE POLICY

Will the warranty and service you provide comply with all areas as stated in Section 6.5 of specifications                               							_____ YES _____ NO

Is warranty literature attached?					_____ YES _____ NO

Is a minimum two (2) year bumper to bumper basic parts and labor warranty excluding abuse 	and normal wear items included?					_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

X6.5	WARRANTY AND SERVICE POLICY QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY AND SUBMITTED WITH YOUR BID.

(If additional lines are needed, make copies of form.)

1. Define the terms of the standard warranty.  If not offered, so state.  (Attach copy)

2. Define warranty service to be performed at DOH facilities and warranty service to be performed at

manufacturer’s representative facility.  List name and location of manufacturer’s representative.

3. List locations for parts inventories that are within the State of West Virginia.  Also, list availability levels, if

known.

4. During the term of warranty, list the guarantee discount to manufacturer’s published list price for parts that

bidder will sell the parts to owner.

A.	Terms: Net 30	Manufacturer’s published list price less: __________% discount

B.	Terms: Net 60	Manufacturer’s published list price less: __________% discount

C.	Terms: Net 90	Manufacturer’s published list price less: __________% discount

5. During the term of warranty, will all manufacturers or engineering improvements be submitted to Division of

Highways?							_____ YES _____ NO

6. During the term of warranty, list the guaranteed rates charged for repair to the unit.

A.	Shop Rate		$ __________ per mechanic hour

B.	Travel Time Charge		$ __________ per mechanic hour

(Specify if one-way)		__________; port to port __________

C.	Mileage Charge		$__________ per vehicle mile

(Specify if one-way		__________; port to port __________

D.	Field Mechanic Rate		$__________ per mechanic hour

E.	Specify period of time that prices are in effect: __________________________

F.	Surcharge for miscellaneous items: ____________________%

X6.6 	EVALUATION COMMITTEE REQUIREMENTS

Is all component specifications, product literature, component models provided for Evaluation Committee bid determination?					_____ YES _____ NO

X6.7	Will all parts, equipment, accessories, material, design and performance characteristics not

specified herein, but which are necessary to provide a complete unit, be furnished with the unit

and conform in strength, quality of material, and quality of workmanship to those which are

advertised and provided to the market in general by the unit industry?

_____YES _____NO

X6.7.1	Are all parts and accessories adequate and regularly supplied as standard to be included except 	those which may be duplications of specifications herein, and except these by specification are not

to be furnished?                                        				_____YES _____NO

X6.7.2	Are all standard safety features that are required by Federal and State statutes of law included?                   									_____YES _____NO

X7.0	SPECIFICATIONS OF THE QUOTED UNIT

The bidder should complete the following schedule in order for the Division to compare the

actual bid unit to the specifications.  Should the bidder except a requirement, then such exception

may be only on the basis that such feature is not offered by the manufacturer.  The Division will

have the sole discretion as to whether the bidder's substitution meets the requirements of the

specifications.

Does unit have built in auxiliary battery charger which would enable batteries to be 	hooked up to

an AC power source at the storage yard or off of a generator in the field

_____ YES _____ NO

Is charge time and charger version based on manufacturer’s battery configuration

_____ YES _____ NO

Describe: ____________________________________________________________________

Manufacturer: ______________________________ Model: __________________

X7.1	Arrowboard:

X7.1.1	Is the arrowboard panel weather-tight:			_____YES _____NO

Describe weather-tight design and materials used:

____________________________________________________________________

Arrow Board panel dimensions:   _____ inches high x _____ inches wide

X7.1.2		Height from bottom of panel to roadway _____ feet above roadway

X7.1.3	Is the face of the panel flat black, with fifteen (15) hooded lamps?												_____YES_____NO

X7.1.3.1 	Does lamp have five (5) inch amber LED with minimum angularity of 33 degrees

_____ YES _____ NO

X7.1.4	Modes of operation capability:

X7.1.4.1 	Right arrow – 10 lamps flashing in unison		_____YES _____NO

X7.1.4.2 	Left arrow – 10 lamps flashing in unison		_____YES _____NO

X7.1.4.3 	Double arrow – 5 lamps in each arrowhead and 3 lamps in shaft, all flashing in

unison							_____YES _____NO

X7.1.4.4 	Warning bar – 7 horizontal lamps flashing in unison	_____YES _____NO

X7.1.4.5 	Four Point Caution – 4 outermost corner lamps flashing in unison													_____YES _____NO

X7.1.4.6 	Indicator lights on back of panel			_____YES _____NO

X7.1.5		Is the unit flash rate 30 flashes per minute with a flash cycle time of two (2) seconds

with 50 percent on time?					 _____YES _____NO

X7.1.6		Will the unit reduce lamp brightness when the ambient light level drops below five

(5) foot candles, plus or minus one (1) foot candle, and increase lamp brightness

when the ambient light level increases to five (5) foot candles, plus or minus one (1)

foot candle?						_____YES _____NO

X7.1.7	Unit's minimum distance of legibility: __________ mile(s)

X7.2	Electrical System:

X7.2.1		Does the solar generator incorporate a 12 Volt DC photovoltaic solar panel mounted

on a self-erecting automatic positioning device located above the unit?												_____YES _____NO

X7.2.2	Is the battery bank of sufficient size and capacity to power the unit for 30 days

without solar assist?					_____YES _____NO

X7.2.3		Are the batteries protected in a manner that will prevent damage due to overcharging

or discharging to deeply at any temperature?		_____YES _____NO

X7.2.4		Does the unit have an external warning light, or other warning signal device, to

indicate when the unit is in need of auxiliary charging prior to arrow shutoff?												_____YES _____NO

X7.2.5	Is the battery compartment vented, protected by an acid-resistant finish, and lockable?

_____ YES _____ NO

X7.2.6	Is the arrowboard controller housed in a lockable weatherproof enclosure?											_____YES _____NO

X7.2.7	Is unit safe guarded from any unwanted outside RF interference which would include but

not be limited to VHF/FM receiver, 2-way radio receiver, cell phones, etc.

_____ YES _____ NO

X7.2.8	Is the unit equipped with an operational hour meter?	_____YES _____NO

X7.3	Trailer:

X7.3.1	Is the trailer equipped with the following:

X7.3.1.1 	2,000 lb. axle with leaf springs			_____ YES _____ NO

X7.3.1.2 	Tubeless standard tread tires and wheels		_____YES _____NO

X7.3.1.3 	Heavy duty pintle eye hitch				_____YES _____NO

X7.3.1.4 	Adjustable jack stand on trailer tongue		_____YES _____NO

X7.3.1.5 	Adjustable jack stands to stabilize unit while in operation														_____YES _____NO

X7.3.1.6 	Approved lighting and safety chains for highway use_____YES _____NO

X7.3.1.7 	Heavy duty light wiring for towing of unit with quick disconnect plug Cole

Hersee Part Number 12081 male or equal		_____YES _____NO

X7.3.1.8 	License plate brackets					_____YES _____NO

X7.3.1.9 	Wheel fenders						_____YES _____NO

X7.3.1.10 	Arrowboard raised and lowered using a hand operating winch ( or hydraulic

pump/ram) locked into place using latches of steel pins with keeper chains

permanently attached to the unit			_____YES _____NO

X7.4      Paint:

X7.4.1	Describe proposed method of painting the unit: _____________________________

_______________________________________________________________________

_______________________________________________________________________

_______________________________________________________________________

X7.5	Does the proposed unit meet or exceed the "Occupational Safety and Health Act of 1970" requirements and/or any subsequent changes at the time manufactured?											_____YES _____NO

X7.6	Does the unit conform to advertising guidelines?		_____YES _____NO

X7.7	List all other standard features considered as standard equipment but not specifically addressed in the specifications: _______________________________________________________________________

________________________________________________________________________

________________________________________________________________________

________________________________________________________________________

X7.8	Preventive Maintenance and Operator’s Training School:

Will a preventative maintenance and operator’s training seminar be provided with each 	order?								_____ YES _____ NO

If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors,

required in conducting the training?				_____ YES _____ NO

Will all manuals, booklets, etc. preventive maintenance, operator procedures, and

service schedule be delivered with each unit?		_____ YES _____ NO

If NO, explain______________________________________________________

Have you attached a copy of the proposed program with your bid, stating the time

required to perform the program and brief description of program _____ YES _____ NO