- SPECIFICATIONS

The following sections of the West Virginia Department of Transportation, Division of Highways Standard Specifications, Roads and Bridges, adopted 2010, as modified by the January 1, 2011 Supplemental Specifications, shall apply to the administration of this contract:  Sections 101, 102.4, 102.5, 105.1, 105.3, 105.4, 105.10, 105.11, 105.12, 105.13, 106.3, 106.4, 106.5, 106.6, 106.7, 106.9, 107.1, 107.2, 107.3, 107.14, 107.19, 107.20, 108.8, 109.1, 109.2, and 401.9.3.

The requirements of the West Virginia Department of Transportation, Division of Highways, Standard Specifications, Roads and Bridges, Section 109.20, PRICE ADJUSTMENT FOR LOAD LIMIT VIOLATIONS shall apply to all material supplied under this contract.  This will include material loaded by the vendor into Division of Highways owned and/or rented trucks.

The terms “Contractor” and “Vendor” used in the above specifications of this Contract are interchangeable.  Contractor shall mean Vendor and Vendor shall mean Contractor.  West Virginia Division of Highways shall mean WVDOH.

West Virginia Department of Transportation, Division of Highways’ Standard Specifications Roads and Bridges, adopted 2010, and the January 1, 2011 Supplemental Specifications may be obtained from:

## West Virginia Division of Highways

Contract Administration

Building 5, Room 722

1900 Kanawha Boulevard, East

Charleston, West Virginia  25305

(Phone) 304-558-2885

http://www.transportation.wv.gov/highways/contractadmin/specifications/2010StandSpec/Pages/default.aspx

# MATERIAL SPECIFICATIONS ARE AS FOLLOWS:

WVDOH STANDARD

SPECIFICATION

MATERIAL (NOTE 1)						          SECTION

Fine Aggregate	   702 (Note 5)

Coarse Aggregate	   703 (Note 5)

Riprap	   704.2

Stone for Gabions	   704.3

Shot Rock	   704.8

Abrasives (Note 2)	   Note 3

Aggregate for Base and Sub-base	   704.6 (Note 5)

#8 Modified and #9 Modified					     Note 4

NOTE 1:	Fine aggregate on the bid schedule shall be considered to be fine aggregate for Portland cement concrete or mortar sand, the particular type to be specified in the Agency Release.  Coarse aggregate on the bid schedule is identified by an AASHTO standard size; e.g., AASHTO Size No. 1, AASHTO Size No. 467, etc.  Aggregate for base and sub-base on the bid schedule is identified by class; e.g., Class 1, Class 2, and Class 9, etc.

NOTE 2:	Abrasives shall conform to the following specifications:

- Quality

- Crushed sandstone shall not be used as an abrasive.

- The liquid limit shall not exceed 25 and the plasticity index shall not exceed 6.

- Total deleterious substances including but not limited to metal, glass, clay, shale, and thin or elongated pieces shall not exceed 3% of the dry weight of the total sample.  Deleterious content shall be determined on that fraction of material retained on the U.S. Standard #4 (4. 75 mm) sieve.

- When gravel is used as an abrasive, the material retained on the #8, sieve shall have a majority of crushed particles.

- Gradation

- The material shall conform to the following gradation requirements determined in accordance with AASHTO T-27.

SIEVE SIZE	% PASSING BY WEIGHT

#### Standard              Modified

1/2 inch	          100                      100

3/8 inch	        85–100                 85–100

#100	          0–10                     0–4

NOTE 3:	In addition to meeting the gradation requirements of AASHTO #8 and #9 aggregate in table 703.4, Modified AASHTO #8 and Modified AASHTO #9 aggregate shall have a maximum of 2.5% passing the #200 sieve as determined by AASHTO T-11 and T-27.  Modified AASHTO #8 and Modified AASHTO #9 aggregate shall meet all other requirements for AASHTO #8 and AASHTO #9 aggregate.

NOTE 4:	With exception of the following contract items, grading on all specified sieve sized for material furnished shall be determined by AASHTO T-27 (Dry Test Only) or by AASHTO T-27 with AASHTO T-11:

##### Item J, AASHTO #7

Item K, AASHTO #8

Item L, AASHTO #9

Item S, AASHTO #8 Modified

Item T, AASHTO #9 Modified

The grading for the above items shall be determined by AASHTO T-27 and AASHTO T-11.

NOTE 5:      Cinders (Power Plant Slag) shall conform to the following specifications:

# Definition

# Cinders (Power Plant Slag) consists of Wet Bottom Boiler Slag (shiny, black, glassy material) formed when molten ash from the burning of coal drops into water and shatters at the bottom of the boiler, and/or Bottom Ash formed when ash particles from the burning of pulverized coal is allowed to air cool at the bottom of the furnace.

# Quality

Total deleterious substances (including but not limited to metal, glass, clay, shale, and thin or elongated pieces) shall not exceed 3% of the dry weight of the total sample.  Deleterious content shall be determined on that fraction of material retained on the US Standard #4 (4.75 mm) sieve.

# Gradation

The material shall conform to the following gradation requirements determined in accordance with AASHTO T-27.

SIEVE SIZE                   % PASSING BY WEIGHT

1/2 inch                                      100

3/8 inch                                    85-100

#100                                         0-20

NOTE 6:      Number 11 Limestone for SRIC shall conform to the following specifications:

A.	Quality

1.	The liquid limit shall not exceed 25 and the plasticity index shall not exceed 6.

2.	Total deleterious substances including but not limited to metal, glass, clay, shale, and thin or elongated pieces shall not exceed 1% of the dry weight of the total sample.  Deleterious content shall be determined on that fraction of material retained on the U.S. Standard #8 (2.36 mm) sieve.

B.	Gradation

1.	The material shall conform to the following gradation requirements determined in accordance with AASHTO T-27.

SIEVE SIZE                   % PASSING BY WEIGHT

3/8 inch	100

#4                                          40-90

#8                                          10-40

#100	                          0-5

- BIDDING INSTRUCTIONS

Vendors may bid any or all items on the bid schedule.  Vendors shall provide the information requested in Subsection 12.1 paragraphs (a), (b), (c) and (d) on the bid schedule.  Failure to provide required information will be sufficient grounds to invalidate the bid.

Any qualification of bids or any modification of the specifications or conditions governing the bids may be cause to reject bids.

The WVDOH may purchase aggregate and stone F.O.B. Vendor’s Storage Site.  The bid price F.O.B. Vendor’s Storage Site shall include the loading of WVDOH’s trucks by Vendor.

Vendor shall have the capacity to deliver a minimum quantity of 300 tons per day to any designated site when directed by the District Engineer/Manager.

- DETERMINING LOW BID

Bids will be evaluated by the WVDOH on the basis of cost per cubic yard F.O.B. at the designated site.  Cost per cubic yard will be determined by multiplying the Vendor’s bid price in dollars per ton by a “Tons per cubic yard factor” which is listed in the following table:

###### AGGREGATE

###### TONS PER CUBIC YARD FACTORS

|  | TYPE OF MATERIAL |
| --- | --- |
|  |  |  |  | BLAST |  |
| ITEM | LIMESTONE | SANDSTONE | GRAVEL | FURNANCE SLAG | STEEL SLAG |
| Class 1, 2, 9, 10 | 1.46 | 1.46 (2920) | 1.46 (2920) | 1.36 (2720) | 1.81 (3620) |
| AASHTO Sizes #1 thru Size #7 | 1.30 (2600) | 1.30 (2600) | 1.30 (2600) | 1.04 (2080) | 1.61 (3220) |
| AASHTO Sizes #8 thru Size #10 | 1.32 (2640) | 1.32 (2640) | 1.32 (2640) | 1.20 (2400) | 1.61 (3220) |
| Gabions | 1.31 (2620) | 1.31 (2620) | 1.31 (2620) | ----- | ----- |
| Fine Aggregate | 1.40 (2800) | 1.40 (2800) | 1.40 (2800) | 1.36 (2720) | 1.77 (3540) |
| Abrasives | 1.36 (2720) | 1.36 (2720) | 1.36 (2720) | 1.28 (2560) | 1.75 (3500) |
| Riprap/Shot Rock | 1.31 (2620) | 1.31 (2620) | ----- | ----- | ----- |

*Numbers in parenthesis are pounds per cubic yard.

## CINDERS

Source  (Note 1)	Tons per Cubic Yard Factor  (Note 2)

Albright Power	0.90  (1,792)

Albright, WV

Burger Power	1.29  (2,579)

Dilles Bottom, OH

Fort Martin Power	0.94  (1,883)

Fort Martin, WV

Harrison Power	0.95  (1,900)

Haywood, WV

John Amos Power	0.82  (1,631)

Winfield, WV

Pleasants Power Plant	1.09  (2,185)

Willow Island, WV

Mountaineer Power	0.65  (1,305)

New Haven, WV

Bruce Mansfield Plant	1.09  (2,160)

Shippingport, PA

Virginia Electric Power	0.79  (1,585)

Mt. Storm, WV

Hatfield Power                                                 	0.85  (1,700 )

Masontown, Pa

Note 1:	In the event the bidding source is not listed, it will be necessary for the WVDOH

to establish the weight per unit volume of said source prior to award.

Note 2:	Numbers in parenthesis are pounds per cubic yard.

- CONTRACT AWARD

All qualified Vendors who submit a valid bid “F.O.B. Vendor’ Storage Site” will be awarded a contract to establish a unit price for those items bid (See Subsection 12.1):

- An Agency Release, specifying WVDOH pick up or Vendor delivery to project site, will be issued to the low bidder when a specific type and quantity of material is to be purchased for use on a designated project.

b.	An Agency Release, specifying WVDOH F.O.B. Vendors’ Storage Site, may only be issued when material for routine highway maintenance operations at various locations is to be purchased.  When material is secured on an Agency Release of this nature, the District Engineer/Manager shall take those steps necessary to assure that material is secured from the Vendor which results in the lowest cost to the WVDOH.  Factors to be considered shall include, but are not limited to; bid price of material, haul cost at $1.50 for the first ton-mile and $0.25 for each additional mile.

Qualified Vendors who submit a valid bid “F.O.B. Division Storage Site” will be awarded a contract to establish a unit price for those locations and items for which their bid is low based on cost per cubic yard (see Subsection 12.2).  An Agency Release, with the required delivery schedule, will be issued for the actual quantity of material to be delivered to the location specified.  If the Vendor is unable to furnish material in accordance with the specified delivery schedule the District Engineer/Manager shall be advised in writing within five (5) working days of the reason for failure to conform to delivery requirements.

- All qualified Vendors who are awarded F.O.B. Division Storage Sites must have the awarded items available for delivery thirty (30) days after the contract award date.

In the event a Vendor fails to conform to the requirements stated in this contract document, the Agency Release or the governing specifications, the Agency Release may be cancelled and reissued to the next lowest bidder.

The Vendor is not authorized to ship, nor is the WVDOH authorized to receive materials prior to the

issue of an Agency Release.

- SUPPLYING OTHER ORGANIZATIONAL ENTITIES

In accordance with Chapter 5A, Article 3, Section 9 of the Code of West Virginia the commodities or services contracted for herein shall be available to all local governmental bodies in accordance with the same prices, terms and conditions afforded to the State of West Virginia.

In the event any Vendor does not wish to extend the prices, terms and conditions of his bid and subsequent contract to all political sub-divisions of the State, he must so indicate in a clear and unambiguous manner in his bid.  This indication does not prejudice the award of the contract.  If a Vendor does not indicate his refusal to extend the prices, terms and conditions of his bid to political sub-divisions of the State he is bound to extend them upon issuance of a purchase order by these other entities.

Other organizational entities using this provision of the contract shall do so without any involvement of the WVDOH.  That is, the entity shall make its own purchase arrangements with the Vendor and shall make its own arrangement for payment.

- HAULING AGGREGATE TO STATE PROJECTS BY CONTRACTOR

The most direct suitable route from the Vendor’s aggregate storage site to the midpoint of the project will be determined by the WVDOH and used to compute haul distance for the purpose of determining low bid, and also for the purpose of determining payment.  The Contractor shall deposit aggregates at the project site at the locations and in the manner directed by the WVDOH.  This may include tailgating the aggregate into an aggregate spreader or onto a roadway, or dumping the aggregate into a stockpile.

- WEIGHING MATERIALS DELIVERED BY TRUCK

Material delivered by truck shall be weighed in accordance with Section 401.9.3 of the West Virginia Department of Transportation, Division of Highways Standard Specifications Roads and Bridges, adopted 2010, as modified by the January 1, 2011 Supplemental Specifications.

- WEIGHING MATERIALS DELIVERED BY MODES OF TRANSPORTATION OTHER THAN TRUCKS

Materials delivered to the designated site by barge, or other non-truck modes shall have their weight determined by a means acceptable to the WVDOH, and the weights of materials so shipped shall be certified, by the Vendor or his authorized agent, to be correct.

The minimum barge delivery requested will be approximately 6,500 tons per the Agency Release.  When barge delivery is required contract item will be ordered in 1500 ton increments.

9.	SAMPLING AND TESTING

Sampling and testing for quality of all items furnished in this contract will be the responsibility of the WVDOH.  Minimum frequency of sampling and testing for quality on all materials (other than those sources already covered by the WVDOH’s “commercial source” approval) will be at least one sample every six days of shipment (or if tested during production, at least one sample every six (6) days of production).

#### Other minimum frequencies shall be in accordance with the following:

Property                                       Frequency

Gradation-Delivered Material	One sample per each day of shipment (or if tested

during production, one sample per each day of

production).  See Note 1 below.

Gradation-WVDOH Pick-up	(WVDOH pick up; A-1 Source) One sample per each

week of shipment per MP 700.00.52; or if tested during

production, one sample per each day of production.  See

Note 1 below.

(WVDOH pick up; A-2 Source)

One sample per 250 tons shipped and a minimum of one

per week of shipment.

#### Moisture Content  (See Note 2)

All samples taken by the Vendor shall be by a Certified Aggregate Sampler or Certified Aggregate Inspector.  Tests shall be performed by a Certified Aggregate Inspector.

NOTE 1:	The Vendor will be responsible for providing test results attesting to the gradation of materials delivered.  Gradation results from the production source will be acceptable.

NOTE 2:	In the event visual inspection of the aggregate indicates excess or unusual moisture beyond that normally expected in the aggregate, the WVDOH reserves the right to determine the moisture content by standard methods.  If this becomes necessary, the net weight of the portion represented will be adjusted utilizing the test results obtained by the WVDOH in accordance with MP 700.00.22.  Items “O” & “P” (Abrasives) will be considered fine aggregate outlined in MP 700.00.22.

- ACCEPTANCE PLAN

Material failing to comply with the quality requirements will not be accepted.  Acceptance for gradation shall be on the basis of test results, provided and certified by the Vendor to be true test results and representative of the material supplied to the WVDOH, on consecutive random samples from a lot.  A lot shall consist of a quantity of material represented by an average value (not to exceed 5 sublots).  A sublot shall consist of the quantity of material represented by a single gradation test.  In the case where only one sample is taken to represent the total quantity, the sublot and lot will be considered the same.  Frequency of sampling and testing shall be in accordance with the Vendor’s quality control plan outlined in MP 700.00.51.  The Vendor shall provide the gradation test results to the WVDOH within 72 hours.

Gradation test results shall be averaged in accordance with MP 300.00.51.  When the average falls outside the applicable limits, the lot of material represented thereby will be considered nonconforming to the extent that the last of its sublots is nonconforming.  When a lot of material is nonconforming, then the last sublot contained therein shall have its degree of nonconformance determined as set forth below.

When a sublot of material is to have its price adjusted, the percentage point difference between the nonconforming test value and the specification limit shall be determined for each sieve size determined to be nonconforming, and this value shall be multiplied by its appropriate multiplication factor as set forth in Table I.

TABLE 1

NONCONFORMING				MULTIPLICATION

SIEVE SIZE     				       FACTOR

Plus #40					1

#40					1.5

#50					1.5

#100					2.0 (1.3 for abrasives and cinders)

#200					2.5

1/2"					1

3/8"					1

The total measure of nonconformance of an individual sublot is the sum of all nonconformances on the various sieve sizes of that sublot.  In no case, however, shall a sublot of material have its price adjusted more than once, and the first adjustment which is determined shall apply.

When the total degree of nonconformance has been established and it is 12 or less, the material will be paid for at an adjusted contract price as specified in Table 2.

###### TABLE 2

DEGREE OF				PERCENT OF CONTRACT

NONCONFORMANCE			 PRICE TO BE REDUCED

1.0 TO 3.0	        2

3.1 TO 5.0	        4

5.1 TO 8.0	        7

8.1 TO 12.0	       11

Greater than 12	        *

*The WVDOH will make a special evaluation of the material and determine the appropriate action.

In the event a Vendor delivers a specific quantity of material from a stockpile, and said quantity is less than the total quantity contained in the stockpile, and it has been determined from his certified test data that a nonconforming sublot(s) is contained in said stockpile, the price reduction shall be calculated for the specific quantity as follows:

The percent price reduction shall be determined as set forth above for the nonconforming sub-lot.  The quantity represented by the nonconforming sublot shall then be calculated as a percent of the total (total material contained in the stockpile).  To determine the price reduction on the specific quantity delivered, multiply the percent of nonconforming material contained in the stockpile by the quantity delivered, and reduce this quantity by the percent price reduction as determined.

Example:

If it has been determined that a stockpile of 100 tons contains 10 percent failing material, and said material is to have its price reduced by 4 percent, then the actual quantity delivered, say 15 tons, will be multiplied by 0.10 (10 percent failing material) which equals 1.5 tons.  These 1.5 tons will thus have its price reduced by 4 percent.  The remaining 13.5 tons will be paid for at full contract price.

PQn

TD	1 -		= AP (price to be paid

100Qt	after adjustment)

WHERE	T:	=	tonnage delivered

P	=	percent price reduction

D	=	cost per ton

Qn	=	quantity of nonconforming sublot(s)

Qt	=	quantity of total stockpile

If two (2) sublots are nonconforming within the stockpile, calculate each separately for the adjusted payment on the quantity delivered (as above).  Add these two adjusted payments together and subtract from the total the price to be paid before adjustment for tonnage delivered (TD).  If three (3) sublots are nonconforming, calculate each separately and subtract twice the price to be paid before adjustment for tonnage delivered, and so on.  Example:

(AP1 + AP2) – TD = Final price to be paid after adjustments

OR

(AP1 + AP2 + AP3) – 2 TD = Final price to be paid after adjustments

WHERE:	AP = price to be paid after initial adjustment for one nonconforming

sublot determined by the above equation.

T = tonnage delivered

D = cost per ton

In the event material is delivered from a continuous stockpile, that is, a stockpile which is continuously being replenished while also having material removed for these applications, certification shall be based on the shipment samples.

- PURCHASING CARD ACCEPTANCE

The State of West Virginia currently utilizes a VISA Purchasing Card Program which is issued through a bank.  The successful vendors must accept the State of West Virginia VISA Purchasing Card for payment of all orders placed by WVDOH Agency Releases as a condition of award.

Vendors are encouraged to utilize a paperless invoice process submitting the following information via e-mail to the WVDOH ordering locations:

- All weigh ticket numbers for material delivered during the invoicing period.

- WVDOH Agency Release number and this contract number.

- Total quantity and unit price with the total cost of each type of material furnished.  (Total quantity invoiced shall be scale weights (supported by weigh tickets) adjusted in accordance with Section 9, Note 2.)

NOTE:		Under no circumstances will the WVDOH accept, or pay for, quantities of material in excess of the quantity stated on the Agency Release.

- BIDDING SCHEDULE

12.1	Bidding F.O.B. Vendor’s Storage Site

- SOURCE OF MATERIAL (State all sources for which bid prices apply) (e.g., Quarry location if Sandstone or Limestone; dredging or pit location if Gravel; production plant name and location if Slag)

b)	EXACT LOCATION OF VENDOR'S STORAGE SITE(S) A separate bid schedule must be submitted when bid price varies between Vendors storage sites.

Bid Price per Ton

Contract Item	     Description of Material                                   F.O.B. Vendor’s Storage Site

LIMESTONE	BLAST

SANDSTONE,	FURNACE	STEEL

GRAVEL, SAND	SLAG	SLAG

A		Class 1 Aggregate	_____________	____________	__________

B		Class 2 Aggregate	_____________	____________	__________

C		Class 10 Aggregate	_____________	____________	__________

D		AASHTO #1 Aggregate	_____________	____________	__________

E		AASHTO #3 Aggregate	_____________	____________	__________

F		AASHTO #4 Aggregate	_____________	____________	__________

G		AASHTO #467 Aggregate	_____________	____________	__________

H		AASHTO #57 Aggregate	_____________	____________	__________

I		AASHTO #67 Aggregate	_____________	____________	__________

J		AASHTO #7 Aggregate	_____________	____________	__________

K		AASHTO #8 Aggregate	_____________	____________	__________

L		AASHTO #9 Aggregate	_____________	____________	__________

M		Stone for Gabions	_____________	____________	__________

N		Fine Aggregate	_____________	____________	__________

O		Standard Abrasives	_____________	____________	__________

BIDDING SCHEDULE (Continued)

12.1      Bidding F.O.B. Vendor’s Storage Site (Continued)

Bid Price per Ton

Contract Item	     Description of Material                                   F.O.B. Vendor’s Storage Site

LIMESTONE	BLAST

SANDSTONE,	FURNACE	STEEL

GRAVEL, SAND	SLAG	SLAG

P		Modified Abrasives	_____________	____________	__________

Q		Riprap	_____________          ____________          __________

R		Shot Rock	_____________	____________	__________

S		AASHTO #8 Modified	_____________	____________	__________

T		AASHTO #9 Modified	_____________	____________	__________

U		Pea Gravel	_____________	____________	__________

V		#11 Limestone Abrasives	_____________	____________	__________

W		Haul by Vendor (Except Items R and Q):

@ _______________ $ for First Ton-Mile

@ _______________ $ for Each Additional Ton Mile

X		Haul by Vendor (Items R and/or Q):

@ _______________ $ for First Ton-Mile

@ _______________ $ for Each Additional Ton-Mile

Bid Price per Ton

Contract Item	     Description of Material                               F.O.B. Vendor’s Storage Site

AA		     Cinders (See Note 1.)	                          ____________

Note 1:  Bid price shall include cost of Vendor Loading Department trucks.

c)        SOURCE OF MATERIAL Name and Location of plant which produces the material:

d)	EXACT LOCATION OF VENDOR'S STORAGE SITE(S) A separate bid schedule must be submitted when bid price varies between Vendors storage sites.