PREBID ADDENDUM

7011EC12

TRUCK MOUNTED HYDRAULIC EXCAVATOR, SINGLE ENGINE

CHANGES TO SPECIFICATIONS:

FROM:

4.2	DELIVERY  - 3rd Paragraph

A completed pilot model for inspection must be provided within 60 calendar days

after receipt of the purchase agreement by the successful vendor.

TO:

4.2 	DELIVERY – 3rd Paragraph

A completed pilot model for inspection must be provided within 90 calendar days

after receipt of the purchase agreement by the successful vendor.

FROM:

7.2.3	The telescope section to be equipped with a two-position quick-change bucket adapter

and telescope hydraulically through a distance of not less than 12 feet 6 inches.

TO:

7.2.3	The telescope section to be equipped with a one-position quick-change bucket adapter

and telescope hydraulically through a distance of not less than 12 feet 6 inches.

FROM:

7.4.6	The controls shall be self-centering deadman type consisting of two (2) hydraulic

joysticks mounted on armrests and one (1) rocker switch for all upperstructure

movements.

TO:

7.4.6	The controls shall be self-centering deadman type consisting of two (2) electronic

joysticks mounted on armrests and one (1) rocker switch for all upperstructure

movements.

DELETE:

7.4.11	There shall be a rocker switch on the control panel to select high or low speed for

the remote travel.

FROM:

7.6.1	The carrier shall be powered by a turbo charged after cooled diesel engine

TO:

7.6.1	The carrier shall be powered by a Tier 4 turbo charged after cooled diesel engine

FROM:

7.6.5	The electrical system to be 12 volt

TO:

7.6.5	The electrical system to be 24 volt

FROM:

7.7.1	The carrier to be equipped with a 9-speed transmission Fuller RTX14609B or equal

TO:

7.7.1	The carrier to be equipped with a 6-speed automatic transmission Allison 3500RDS or

Equal

DELETE:

7.8	Clutch:

7.8.1	The clutch shall be a minimum of 14 inches two-plate, pull type

FROM:

7.11.2	The front tires shall be single 15.00 x 22.5 16 PR with highway tread.

TO:

7.11.2	The front tires shall be single 38565Rx22.5 18 ply on/off highway tread.

FROM:

7.11.3	The eight (8) rear tires shall be 10.00 x 20 14 PR with traction tread.

TO:

7.11.3	The eight (8) rear tires shall be 11R x 24.5 16 ply with traction tread

PREBID ADDENDUM

7011EC12

TRUCK MOUNTED HYDRAULIC EXCAVATOR, SINGLE ENGINE

CHANGES TO BIDDER’S EVALUATION REPORT

FROM:

X4.2	DELIVERY:

X4.2.1	Delivery date of completed representative unit: ___Calendar Days After Receipt of

Purchase Agreement

X4.2.2	Delivery date of balance of completed units: ___Calendar Days After Receipt of

Purchase Agreement

TO:

X4.2	DELIVERY:

X4.2.1	Delivery date of completed pilot unit: ______ Calendar Days After Receipt of

Purchase Agreement

X4.2.2	Delivery date of balance of completed units: ______ Calendar Days After Receipt of

Purchase Agreement

FROM:

X7.2.3	Is telescope section equipped with a two-position quick-change bucket adapter/telescope

hydraulic through a distance of not less than 12 feet 6 inches __YES__NO

TO:

X7.2.3	Is telescope section equipped with a one-position quick-change bucket adapter/telescope

hydraulic through a distance of not less than 12 feet 6 inches 	_____YES ____NO

FROM:

X7.4.6	Are controls self-centering deadman type consisting of 2 hydraulic joysticks

mounted on armrest/1 rocker switch for all upperstructure movement__YES__NO

TO:

X7.4.6	Are controls self-centering deadman type consisting of 2 electronic joysticks

mounted on armrest/1 rocker switch for all upperstructure movement

_____YES _____NO

DELETE:

X7.4.11	Does unit have a rocker switch on the control panel to select high/low speed for the

remove travel __YES__NO

FROM:

X7.6.1	Will carrier be powered by turbo charged after cooled diesel engine__YES__NO

TO:

X7.6.1	Will carrier be powered by Tier 4  turbo charged after cooled diesel engine

_____ YES _____ NO

FROM:

X7.6.5	Will unit electrical system be 12 volt? __YES__NO

TO:

X7.6.5	Will unit electrical system be 24 volt?		_____ YES _____ NO

FROM:

X7.7.1	Manufacturer: ___ Model: ___

Will carrier be equipped with a 9 speed transmission __YES__NO

TO:

X7.7.1	Manufacturer: _______________________	Model: ____________________

Will carrier be equipped with a 6 speed automatic transmission  _____ YES _____ NO

DELETE:

X7.8	Clutch:

X7.8.1	Size: __inch 2 plate pull type __YES __NO

FROM:

X7.11.2	Front Tires

Size: ____highway tread __YES__NO

TO:

X7.11.2	Front Tires

Size: ____________________________on/off highway tread	_____YES ____NO

NO CHANGE REQUIRED:

X7.11.3	Size eight (8) rear tires: ____________ traction tread	_____ YES _____ NO