WEST VIRGINIA DEPARTMENT OF TRANSPORTATION

DIVISION OF HIGHWAYS

EQUIPMENT DIVISION

BIDDER'S EVALUATION REPORT

PROCUREMENT SPECIFICATIONS FOR OPEN END CONTRACT

NO. 377-2-F

64,000 GVW CAB AND CHASSIS, STAINLESS STEEL

COMBINATION DUMP/SPREADER MUNI BODY, AND PISTON PUMP HYDRAULIC SYSTEM

NOTE TO BIDDER:    Procurement Specification No. 377-2-F, Paragraph 2.0 recommends the completion and submittal of this Report with your bid.  Purpose of this Report is to enable the West Virginia Division of Highways Evaluation Committee to make full and fair evaluation of the bid.  Addendums in order, along with a summary of exception as a separate attachment, should be with Bidder’s Evaluation Report.

FAILURE TO SUBMIT THIS REPORT, COMPLETE IN ITS ENTIRETY, MAY SUBJECT THE BIDDER

TO DISQUALIFICATION.

Reference Requisition No.: ______________________

Bidder's Name:____________________________________________________________

Address:__________________________________________________________________

Telephone Number:_________________________________________________________

Years Bidder has been registered to do business with the State of West Virginia:  ______________YRS.

Years Company has been an authorized dealer for proposed unit:                        _______________YRS.

X3.2	Have you complied with all mandatory specifications?	_____ YES _____ NO

X4.2   	DELIVERY:

X4.2.1 	Delivery date of completed representative unit:________________ Calendar Days After 									Receipt of Purchase Agreement by successful vendor

X4.2.2 	Guaranteed delivery date of balance of completed units:  ___________ Calendar Days After

Receipt of Purchase Agreement by successful vendor

X5.0	AWARD CRITERIA;

X5.1	Price per completed unit including minimum 2 year bumper to bumper parts and labor

warranty : 						________________per unit

If a 3 year bumper to bumper basic parts and labor warranty excluding normal wear items

and misuse is available, please state price for completed unit:

________________per unit

X6.0   SPECIFICATIONS - GENERAL

X6.1   Manufacturer, model, series, and date of manufacture of proposed unit:

________________________________________________________________________

Is descriptive literature, fully describing proposed unit attached to your bid? _____ YES _____ NO

If not, why?______________________________________________________________

X6.2	Will the required number of service manuals, and complete parts list be delivered to the

Equipment Division at Buckhannon upon completion of delivery of total units?

_____ YES _____ NO

Will the required Equipment Preventive Maintenance Form (Section X6.2 of Bidders Evaluation Report) be provided upon inspection of the pilot unit?			_____ YES _____ NO

X6.2

2-10-00

EQUIPMENT PREVENTATIVE MAINTENANCE QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY BY SUCCESSFUL BIDDER OR MANUFACTURER’S TECHNICAL REPRESENTATIVE PRIOR TO DELIVERY OF PILOT MODEL TO THE WVDOH.

DESCRIPTION: _______________________________________	MAKE: ___________________________________

MODEL: ________________________    	YEAR: __________	PURCHASE AMOUNT: ______________________

ENGINE:	MAKE: ______________________ 	MODEL: __________________ 	FUEL TYPE: ________________________

HORSEPOWER: _______________	CYLINDER: ________	ENGINE SERIAL: __________________________

COOLING SYSTEM CAPACITY: ______________________

BELTS:		DESCRIPTION:					PART NUMBERS:

___________________________________________	_________________________________________________

___________________________________________	_________________________________________________

GVW: _______________________AXLE CAPACITY: FRONT: ______________	REAR:______________

TIRES:		FRONT MAKE & SIZE: ______________________________________________

REAR MAKE & SIZE: _______________________________________________

DIMENSIONS OF UNIT:	LENGTH: __________		WIDTH: ______________	LENGTH: ___________

VENDOR CONTACT PERSON: ____________________________________		PHONE: __________________________

PARTS:

BATTERY MAKE: ____________________	MODEL: ___________________		CCA: _______________________

TOP OR SIDE POST: __________________	DIMENSIONS: LENGTH ________ WIDTH ________ HEIGHT __________

SPARK PLUGS OR FUEL INJECTORS MAKE: ______________	PART # __________________________________________

FUEL PUMP OR INJECTION PUMP MAKE: ________________	MODEL: _________________________________________

ALTERNATOR MAKE: __________________________________	PART #:__________________________________________

STARTER MAKE: ______________________________________	PART #: _________________________________________

TURBO CHARGER MAKE: ______________________________	PART #: _________________________________________

TRANS. MAKE: ____________________	MODEL: _________________________   AUTO/MANUAL: ____________________

HYDRAULIC PUMP MAKE: _____________________________	MODEL: _________________________________________

FILTERS		MAKE	PART NO.		LUBRICANT		MANUFACTURER TYPE

OIL		__________________________________	ENGINE	__________________________________________

AIR INNER	__________________________________	TRANSMISSION__________________________________________

AIR OUTER__________________________________	POWER STEERING _______________________________________

FUEL PRIMARY ______________________________	HYDRAULIC  	__________________________________________

FUEL SECONDARY ___________________________	DIFFERENTIALS _________________________________________

COOLANT	__________________________________	BRAKE FLUID 	__________________________________________

HYDRAULIC	_______________________________	COOLANT	__________________________________________

OTHER		__________________________________ 	OTHER 	__________________________________________

X6.3	TRAINING:

Will training seminar be conducted on Preventive Maintenance, Operator and Mechanic Training                      								_____YES _____ NO

Will you conduct training with each purchase order against this open end contract?

_____ YES _____ NO

Will training be conducted within 2 working days from the delivery of the pilot unit on the individual purchase order?								_____ YES _____ NO

If NO, explain time frame_____________________________________________________________

Will an Operator’s Manual be furnished directly to Training Academy prior to the

delivery of the pilot?		_____ YES _____ NO

X6.4   	If you are the successful vendor, will you furnish all training aids, i.e., videos, projectors, required in conducting the training?		         _____ YES _____ NO

X6.4.1    	Will all manuals, booklets, etc. explaining preventive maintenance, operator procedures, and service schedule be delivered with each unit?           			_____ YES_____NO

If NO, explain _____________________________________________________

X6.5	WARRANTY AND SERVICE POLICY

Will the warranty and service you provide comply with all areas as stated in Section 6.5 of specifications                               							_____ YES _____ NO

Is warranty literature attached?					_____ YES _____ NO

Is a minimum two (2) year bumper to bumper basic parts and labor warranty excluding abuse 	and normal wear items included?					_____ YES _____ NO

Describe:

____________________________________________________________________________________

____________________________________________________________________________________

Will the equipment have a valid and current state inspection sticker?	_____ YES _____ NO

List all extended service contract coverages, published and not published, along with a cost as options.

Also, provide manufacturers hours vs. miles conversion.

___________________________________________________________________________________

___________________________________________________________________________________

___________________________________________________________________________________

X6.5	WARRANTY AND SERVICE POLICY QUESTIONNAIRE

THIS FORM MUST BE COMPLETED IN ITS ENTIRETY AND SUBMITTED WITH YOUR BID.

(If additional lines are needed, make copies of form.)

1. Define the terms of the standard warranty.  If not offered, so state.  (Attach copy)

2. Define warranty service to be performed at DOH facilities and warranty service to be performed at

manufacturer’s representative facility.  List name and location of manufacturer’s representative.

3. List locations for parts inventories that are within the State of West Virginia.  Also, list availability levels, if

known.

4. During the term of warranty, list the guarantee discount to manufacturer’s published list price for parts that

bidder will sell the parts to owner.

A.	Terms: Net 30	Manufacturer’s published list price less: __________% discount

B.	Terms: Net 60	Manufacturer’s published list price less: __________% discount

C.	Terms: Net 90	Manufacturer’s published list price less: __________% discount

5. During the term of warranty, will all manufacturers or engineering improvements be submitted to Division of

Highways?							_____ YES _____ NO

6. During the term of warranty, list the guaranteed rates charged for repair to the unit.

A.	Shop Rate		$ __________ per mechanic hour

B.	Travel Time Charge		$ __________ per mechanic hour

(Specify if one-way)		__________; port to port __________

C.	Mileage Charge		$__________ per vehicle mile

(Specify if one-way		__________; port to port __________

D.	Field Mechanic Rate		$__________ per mechanic hour

E.	Specify period of time that prices are in effect: __________________________

F.	Surcharge for miscellaneous items: ____________________%

X6.6 	EVALUATION COMMITTEE REQUIREMENTS

Is all component specifications, product literature, component models provided for Evaluation Committee bid determination?					_____ YES _____ NO

X6.7	Will all parts, equipment, accessories, material, design and performance characteristics not

specified herein, but which are necessary to provide a complete unit, be furnished with the unit

and conform in strength, quality of material, and quality of workmanship to those which are

advertised and provided to the market in general by the unit industry?

_____YES _____NO

X6.7.1	Are all parts and accessories adequate and regularly supplied as standard to be included except 	those which may be duplications of specifications herein, and except these by specification are not

to be furnished?                                        				_____YES _____NO

X6.7.2	Are all standard safety features that are required by Federal and State statutes of law included?                   									_____YES _____NO

X7.0	SPECIFICATIONS OF THE QUOTED UNIT

The bidder should complete the following schedule in order for the Division to compare the actual bid 	unit to the specifications.  Should the bidder except a requirement, then such exception may be only on 	the basis that such feature is not offered by the manufacturer.  The Division will have the sole 		discretion as to whether the bidder's substitution meets the requirements of the specifications.

X8.0	Specifications – Cab and Chassis

Manufacturer: _______________________________  Model: _______________________

Will a minimum 2 year basic bumper to bumper warranty including parts and labor be

furnished?									_____ YES _____ NO

X8.1	GVWR Rating: __________ Lbs.

X8.2	Cab to Axle Dimensions: __________ Inches usable

X8.2.1		After frame length: __________ Inches

X8.3	Wheelbase: __________ Inches and is set forward design for snowplow application for various

plows					_____ YES _____ NO

X8.3.1		Have you adjusted wheelbase and CA dimension to provide the optimum legal weight

distribution?						_____ YES _____ NO

X8.3.2		BBC (Bumper to Back of Cab) __________ Inches excluding frame extension

X8.4	Frame:

Does the frame meet or exceed all Federal requirements for GVWR specified that extends forward

beyond the grille a minimum of 14 inches?			_____ YES _____ NO

X8.4.1		Frame material __________ PSI yield strength.  Is frame extension a “parent rail” material?

_____ YES _____ NO

X8.4.2		RBM:  __________ million Ins/Lb. per rail	Is an integral frame and frame extension

Included 	_____ YES _____ NO

X8.4.2.1		Where engine and radiator adjustments are required, __________ million in lb. per rail

(RBM).

X8.4.3		Is main frame and any required liners _____ straight channel or _____ offset channel, full length

X8.4.4		Is frame RBM approved by manufacturers Engineering Department?

_____ YES _____ NO

Is it bolt on or welded extension?			_____ YES _____ NO

X8.4.5		Does front frame accommodate the Department’s standard hydraulic PTO shaft and

pump, and the plow frame?					_____ YES _____ NO

Does it provide easy service accessibility?		_____ YES _____ NO

X8.4.5.1		Front frame mounted tow hooks		_____ YES _____ NO

X8.4.5.2		Has the factory installed front bumper to be omitted		_____ YES _____ NO

X8.5	Cab:

Manufacturers standard steel, aluminum and/or fiberglass with premium or manufacturers highest level

interior trim with inside noise level rating not to exceed 80 dba in compliance with Federal regulations

_____ YES _____ NO

Ambient temperature display for outside temperature			_____ YES _____ NO

Is hood a tilt hood						_____ YES _____ NO

Fenders steel and/or fiberglass				_____ YES _____ NO

Is rear air bag suspension provided				_____ YES _____ NO

Are inner fender panels adequate to keep materials from engine compartment	_____YES_____NO

X8.5.1		Cab door locks, both doors, keyed alike		_____ YES _____ NO

X8.5.2		Dual sun visors					_____ YES _____ NO

X8.5.3		Arm rests, both sides					_____ YES _____ NO

X8.5.4		Seats:  Fully adjustable air ride high back with head rest, cloth covered both left hand and right

hand sides						_____ YES _____ NO

Clearance between seats __________ inches

X8.5.5		Floor mats:  Rubber floor mats throughout cab area with non-absorbent backing under mats

_____ YES _____ NO

X8.5.6		Turn signals:  Manufacturers standard with hazard warning switch _____ YES _____ NO

X8.5.7		Heater and defroster:  Fresh air type, heaviest duty	_____ YES _____ NO

X8.5.8		Windshield wipers and washers:  Manufacturer’s heaviest duty “artic type” with intermittent

feature with manufacturers largest reservoir filled with antifreeze type solvent

_____ YES _____ NO

X8.5.9		Instruments:  Are all instruments dash mounted except where specified otherwise?

_____ YES _____ NO

Are all standard instruments supplied, including but not limited to the following:

_____ YES _____ NO

X8.5.9.1		Coolant, oil pressure gauges, to have both dial type readout and either an audible or

visual alarm to warn operator when safe operating conditions are exceeded

_____ YES _____ NO

X8.5.9.2		Voltmeter or ammeter				_____ YES _____ NO

X8.5.9.3		Engine RPM tachometer			_____ YES _____ NO

X8.5.9.4		Speedometer with odometer			_____ YES _____ NO

X8.5.9.4.1			Are provisions for dual speedometer leads made available

_____ YES _____ NO

X8.5.9.5		Primary air pressure gauge			_____ YES _____ NO

X8.5.9.6		Auxiliary air pressure gauge			_____ YES _____ NO

Is it combined with primary air pressure gauge_____ YES _____ NO

X8.5.9.7		Air filter manufacturers heaviest duty dual element type that meets all requirements of

extended engine warranty			_____ YES _____ NO

X8.5.9.8		Does unit have front air intake		_____ YES _____ NO

Is an air actuated or cable control valve provided to enable operator to divert air

intake to engine compartment while in snow plowing application

_____ YES _____ NO

X8.5.9.9		Is air filter restriction indicator gauge dash mounted	_____ YES _____ NO

X8.5.9.10		Engine hourmeter controlled by engine operation		_____ YES _____ NO

X8.5.9.11		Fuel level reading						_____ YES _____ NO

X8.5.9.12		Parking brake dash controlled with indicator light		_____ YES _____ NO

X8.5.9.13		Manufacturers best sound/weather insulation package for proposed cab

_____ YES _____ NO

X8.5.9.14		Outside temperature control with in cab digital read out	_____ YES _____ NO

X8.5.10	Rearview Mirrors:

X8.5.10.1		West coast type power adjustable with convex spot mirror	_____ YES _____ NO

Size: __________________

X8.5.10.2		Both mirrors heated type with stainless steel _____ composite _____ powder coated

_____ or aluminum hardware _____ with corrosion resistance, heads, and

fasteners 							_____ YES _____ NO

X8.5.11	Grab Handle: Right hand and left hand sides, internal or external mounting to rear of door 			opening  								_____ YES_____NO

Are inside handles featured _____ YES _____ NO  Is one (1) outside, left, mounted grab 
		handle with non-slip insert for bed aggregate inspection furnished

X8.5.12	Air horns, with snow shields if cab mounted, with adequate clearance for future installation of

body dump cab protector						_____ YES _____ NO

Does it have single air horn used without snow shield if mounted downward on frame rail under 			hood									_____ YES _____ NO

X8.5.13	Unit includes lockable hand operated throttle control or electronic control for idle up and idle

down for hydraulic flow rate						_____ YES _____ NO

X8.5.14	Will manufacturer provide for stationary grille or grille with cutout area to allow tilt hood to

clear snow plow mount						_____ YES _____ NO

Is stone/gravel guard provided					_____ YES _____ NO

X8.5.15	Air conditioning:  Manufacturers fresh air type heaviest duty with APADS or equal RCD system

including replaceable fresh air filter					_____ YES _____ NO

X8.5.16	Radio: AM/FM stereo with weatherband radio feature		_____ YES _____ NO

X8.5.17	Glass: Manufacturers tinted safety glass (all locations)		_____ YES _____ NO

X8.5.17.1		Dual power windows						_____ YES _____ NO

X8.5.18	Manufacturers engine cover or dash mounted extended two (2) cup drink holder

_____ YES _____ NO

X8.5.19	Front mudflaps manufacturers standard for unit bid			_____ YES _____ NO

X8.5.20	Emergency triangle warning kit, with hold down stowed (fastened) in the cab

_____ YES _____ NO

Manufacturer & Model: ________________________________

X8.5.21	Manufacturers tilt steering column with cruise control feature	_____ YES _____ NO

OR

Locking hand operated throttle steering wheel			_____ YES _____ NO

Diameter: ______ inches

X8.5.22	Fire extinguisher – rechargeable with vehicle mount.  Mounted in the cab for easy and quick

access									_____ YES _____ NO

Manufacturer & Model: __________________________

X8.5.23	List any accessories not indicated above but are included in the manufacturer’s standard

cab

__________________________________________________________________________

__________________________________________________________________________

X8.5.24	If you are the successful vendor, will you provide WVDOH with complete list of all filters

required for normal maintenance on proposed unit.		_____ YES _____ NO

X8.6	Engine:

Is engine diesel	_____ YES _____ NO	__________ liter

Peak HP __________ at __________ RPM		Torque __________ lb ft. at __________ RPM

Is engine compliant and certified to meet US EPA 210 Emission Standards without using Federal

EPA credits								_____ YES _____ NO

Manufacturer: _______________________________	Model: ________________________

X8.6.1		Will engine manufacturer make provisions for front mounted hydraulic pump to crankshaft

pulley									_____ YES _____ NO

Manufacturer & Model: __________________________________________________

X8.6.1.1		In block engine heater 1500 watt				_____ YES _____ NO

X8.6.1.1.1			Is electrical cable from the heater to plug one piece and waterproof, located left 					side under driver door					_____ YES _____ NO

X8.6.1.2		Fuel heater/water separator provided inside of engine compartment

_____ YES _____ NO

Manufacturer: __________________________

X8.6.1.2.1			Engine fuel system equipped with primer pump	_____ YES _____ NO

X8.6.1.3		Exhaust:

X8.6.1.3.1			Single vertical exhaust pipe with underbody muffler that will meet all Federal 					noise abatement requirements				_____ YES _____ NO

Exhaust to the passenger (right) side of unit		_____ YES _____ NO

X8.6.1.3.2			Is tail pipe shielded or insulated to protect personnel from burns when

entering or exiting the cab				_____ YES _____ NO

The shield is ____ degrees to _____ degrees and of non-rustable material

such as stainless steel or aluminum			_____ YES _____ NO

Manufacturer: ___________________________________

X8.6.1.3.3			Exhaust pipe with rain cap or exhaust turn out	_____ YES _____ NO

X8.6.2		Jacob’s Engine Brake_____ Cummins C-Brake _____ Mack Power Leash _____

compression and exhaust _____or equal ________________________________

X8.6.3		Are engine components facing wheel areas, on both sides, and the areas to the rear of wheels 			shielded by means of rubber skirts supported by easily removable steel rods

_____ YES _____ NO

X8.6.4		Engine oil pan is zinc nickel plated _____ aluminum _____ or non-corrosive coated_____

X8.7	Clutch:

X8.7.1		Externally lubricated and manually adjusted with torque limiting clutch brake

_____ YES _____ NO

X8.7.2		Clutch adjustment set to specifications prior to delivery to the Department

_____ YES _____ NO

X8.7.3		Is clutch dual plate ceramic clutch _____ YES _____ NO

Size: _____ inch	Kwik adjust (manual feature)		_____ YES _____ NO

Manufacturer and model: ___________________with 7 spring damper___YES___NO

X8.7.4		Does clutch meet or exceed peak engine torque		_____ YES _____ NO

X8.8	Cooling System:  Is it capable of maintaining engine temperature within the manufacturer’s

recommended range during continuous operation 			_____ YES _____ NO

X8.8.1.		Does the system incorporate a thermostat and bypass for warm up _____ YES _____ NO

Is it filled with permanent type Dex Cool extended life or equal antifreeze rated to a

-30º F or lower						_____ YES _____ NO

Is it a low silicate type antifreeze for diesel engines only	_____ YES _____ NO

X8.8.2		Is it the largest factory available engine cooling capacity compatible with engines and

transmission referenced and for continuous high engine output under extreme temperatures

and/or operating conditions due to prolonged snow plowing operations in low gears

_____ YES _____ NO

X8.8.3		Is unit fitted with provisions for visually monitoring coolant without necessitating removal of the

cap from the radiator or expansion tank			_____ YES _____ NO

X8.8.4		Does the radiator mounting provide adequate clearance to facilitate the installation of a

crankshaft driven PTO drive shaft				_____ YES _____ NO

X8.8.5		Distance between the extreme tip of the radiator fan blade and the centerline of the

crankshaft to 	insure adequate clearance for PTO drive shaft: __________ inches

X8.8.6		Radiator and heater silicone hose manufacturer and model: __________________________

X8.9	Fuel Tanks:

X8.9.1		Safety type aluminum fuel tanks as required by FMVSS	_____ YES _____ NO

X8.9.2		Single aluminum usable: __________ U.S. gallon;  frame mounted_____ YES _____ NO

X8.9.3		Driver and passenger entrance steps-grated self cleaning safety step _____ YES _____ NO

X8.9.3.1		Are all edges banded (skirting) on the outer perimeter	_____ YES _____ NO

X8.9.3.2		Top of first step above ground: __________ inches

X8.9.4		Is a fuel draw system provided that meets all Federal 2010 emission standards													_____ YES _____ NO

X8.10	Electrical System:

X8.10.1	Type:  Manufacturer’s 12 volt negative ground system with manufacturers radio interference

Suppression								_____ YES _____ NO

X8.10.1.1		Circuit breaker equipped, in easily accessible location, weatherproof_____YES_____NO

X8.10.2	Three (3) ___ or four (4) ___ heavy duty – 12 volt batteries, maintenance free with sealed 			terminals								_____ YES _____ NO

X8.10.2.1		Reserve capacity: __________ minutes @ __________ degrees F

X8.10.2.2		Cold crank AMPS: __________ total @ __________ degrees F

X8.10.3	Alternator capacity: __________ AMPS with internal regulator_____ YES _____ NO

X8.10.4	Wiring:  Heavy duty hypalon type or equal in heavy duty sheathing, bundled with lacing cords or

non-metallic tie straps							_____ YES _____ NO

X8.10.5	Lighting:  Are provision made available for all required lighting on completed unit

(number, location, and color) to conform to the West Virginia Motor Vehicle Code

_____ YES _____NO

X8.10.6	Auxiliary snow plow/salt spreader lighting package		_____ YES _____ NO

X8.10.6.1		Will truck vendor provide rear tail lights	_____ YES _____ NO

Truck vendor will provide _____ feet of wiring bundled at the end of the frame for

body vendor hook up of tail lights and etc. in the dump bed body ____YES____ NO

X8.10.7	Will manufacturer _____ or successful vendor _____ make provisions for manufacture

approved wiring and weatherproof disconnect plug		_____ YES _____ NO

Manufacturer and Model: _________________________________

seven (7) pin connector _____ YES _____ NO with _____ foot “pigtail” to

operate combination left and right turn/park lights/auxiliary headlights _____ YES _____NO

X8.10.7.1		Are provisions for weatherproof disconnect plug located at lower left front grille-bumper

area								_____ YES _____ NO

All wiring connections weatherproof with wiring encased in wire looms

_____YES_____NO

X8.10.7.2		Is a 7 way trailer connection light socket mounted at rear of truck frame

_____ YES _____ NO

Manufacturer and Model: ___________________________

X8.10.7.3		Has manufacturer provided body builder circuit interface capability with

connection plug to be located at rear of frame for body builder connection to stop,

tail, and marker light circuits, ignition controlled auxiliary feed to ground to

provide splice free chassis wiring integrity			_____ YES _____ NO

X8.10.7.4		Has manufacturer provided body builder circuits – three (3) switches

_____ YES _____ NO

located in the dash instrument panel with one (1) weather protected body builder

connection box or module located at the rear under cab	_____ YES _____ NO

_____ amps per channel, _____ amp maximum output

_____ YES _____ NO

Do dash switches control the power module with LED backlighting _____YES _____NO

X8.11	Power Train Overview:

Do lubricants for front axle hubs and differentials, automatic transmission, transfer cases, and all

rear differentials meet or exceed all appropriate MIL and SAE specifications for synthetic lubricants 									_____YES _____ NO

all plugs identified as synthetic or painted red				_____ YES _____ NO

X8.11.1	Transmission: _____________________________________________

transmission oil cooler ____YES _____NO

X8.11.1.1		Does transmission torque capacity meet or exceed specified engine torque

_____ YES _____ NO

X8.12	Driveline:

X8.12.1	Manufacturer and Model: ________________________________________________________

X8.13	Rear Axle:

X8.13.1	Manufacturer and Model: ________________________________________________________

X8.13.2	Is each unit equipped with driver controlled main locking differential in forward and rear axle

that is manually cab controlled					_____ YES _____ NO

X8.13.3	Ratio: Does gear ratio determined give the vehicles the capability of a top speed of

approximately 70 MPH						_____ YES _____ NO

If not 70 MPH, please specify __________MPH

X8.13.4	Is housing aluminum or other lightweight material			_____ YES _____ NO

X8.13.5	Rear wheel seals: ____________________________________

X8.13.6	Drain plug, magnetic							_____ YES _____ NO

X8.14	Front suspension:

X8.14.1	Capacity at ground each front spring__________ lb.

Total spring capacity __________ lb.

X8.14.2	Are the front spring pins or bearings/bushing furnished with 360 degree grease grooves to insure

adequate lubricant penetration 					_____ YES _____ NO

X8.14.3	Are spring hangers heavy castings with sufficient pin and bearing surface to render trouble free

service									_____ YES _____ NO

X8.15	Rear suspension: __________________________________________

X8.16	Front Axle:

X8.16.1	Capacity: __________ lbs.

X8.16.1.1		Does the front axle, drag links, and tie rods have grease zerks installed

_____ YES _____ NO

X8.16.2	Heavy duty shock absorbers						_____ YES _____ NO

X8.16.3	Oil lubricated front wheel seals_____ YES _____ NO Manufacturer: ____________________

X8.16.4	Does unit provide adequate tire clearance at maximum turning angles ____ YES ____ NO

X8.17	Brakes

X8.17.1.1		Type:  Full air, with manufacturers ABS in compliance with the most current FMVSS

requirements							     _____ YES _____ NO

X8.17.2	Compressor: Manufacturer and Model: __________________	______ cu. ft.

X8.17.3	Service Brake Size:

X8.17.3.1		Front: _______________________________________  “S” cam ____ OR power front

disc brake system providing equal performance _____

X8.17.3.2		Quick change type single _____ OR double anchor pin if drum type brakes _____

X8.17.3.3		Rear: ________________________________ “S” cam with quick change type single___

OR double pin _____

X8.17.3.4		Are all brake chambers sealed brake chambers with epoxy exterior coat on front and rear

Chambers							_____ YES _____ NO

Manufacturer: _____________________________

X8.17.4	Do drum brakes have automatic slack adjusters and are clearance sensing type only, with

adjustment on application of the brake   				_____ YES _____ NO

X8.17.5	Parking Brake: Rear wheel spring type – severe service spring brakes _____ YES _____ NO

Manufacturer and Model: _____________________________

X8.17.5.1		Does parking brake provide modulated emergency braking via the foot valve in the event

of a rear service system failure				_____ YES _____ NO

X8.17.6	Air dryer with heater _____ inches above road service

Manufacturer and Model: ________________

with spin on desiccant cartridge or equal _____ YES _____NO

Is the installation made in concurrence with the air compressor manufacturer’s recommendations

_____ YES _____ NO

X8.17.6.l		Are all electrical connectors for drain valve and air dryer covered with heat shrink

material or have sealed connections				_____ YES _____ NO

X8.17.7	Manufacturer’s standard air tanks for service brakes			_____ YES _____ NO

Auxiliary tank for parking brake					_____ YES _____ NO

X8.17.8	Low air pressure warning light and buzzer				_____ YES _____ NO

X8.17.9	Rear service brake chambers and spring brake chambers mounted to provide adequate clearance

for tire chains and backing into bituminous paving machines	_____ YES _____ NO

Factory installed							_____ YES _____ NO

X8.17.10	Brake dust covers installed on all wheels				_____ YES _____ NO

X8.17.11	Unit equipped with hand control valve, tractor protection valve, with provisions for installation

of glad hands at rear of truck to enable unit to pull air brake operated equipment trailer

_____ YES _____ NO

X8.17.11.1		Are glad hands recessed as not to stick out past the end of frame rails

_____ YES _____ NO

X8.18	Tires and Wheels:

X8.18.1	Truck equipped with hub piloted steel disc wheels for tubeless tires _____ YES _____ NO

X8.18.2	Wheel end equipped with outboard cast brake drums		_____ YES _____ NO

15 degree tubeless steel wheels, hub piloted, 10 hole – 285.75mm bolt circle with 220mm

two-piece flange nuts							_____ YES _____ NO

X8.18.3	Front:

X8.18.3.1		Wheels: Size: ___________________________

10 hole 285.75 mm bolt circle with 220 mm bore, tubeless steel disc_____YES_____NO

Rated at __________ lbs. at a maximum inflation pressure of ______ PSIG.

Manufacturer and Model: _______________________________________

With 0.500 inch thick disc, non standard off set with steel hubs_____ YES _____ NO

Powder coated _____ YES _____ NO  Gray top coat _____ YES _____ NO

X8.18.3.2		Tires: ____________________________ Ply ______

X8.18.4	Rear:

X8.18.4.1		Wheels: Size: ___________________________

10 hole – 285.75 mm bolt circle with 220mm bore, tubeless steel disc

____YES_____NO

Rated at __________ lbs. at a maximum inflation pressure of ________PSIG

Manufacturer and Model: ________________________________________

With 0.472 inch thick disc					_____ YES _____ NO

Powder coated	_____ YES _____ NO   Gray top coat _____ YES _____ NO

X8.18.4.2		Tires: ____________________________

X8.18.4.3		Does the dual rear wheel/tire assembly have clearance between the tires, which

permits the use of dual tire chains				_____ YES _____ NO

X8.18.5	All wheels have wheel separators					_____ YES _____ NO

X8.18.6	Radial Tires:

Front Radial Tire: Manufacturer and Model: _______________________________________

Rear Radial Tire: Manufacturer and Model: ________________________________________

X8.19	Steering:

X8.19.1	Power steering:  Dual integral _____ OR single integral type _____ hydraulic power steering

with right wheel power-assist cylinder				_____ YES _____ NO

X8.19.2	Steering system: (flow, pressure, relief valve etc): _____________________________________

Manufacturer: ______________________________

X8.19.3	Hydraulic supply pump: Vane type ____ OR roller type ____ with sufficient oil flow to permit 			one (1) steering wheel revolution per second with front axle loaded to rated capacity, with plow

on, in a “park” condition						_____ YES _____ NO

Manufacturer and Model: ________________________________

X8.19.4	Is the pump the integral filter type unit				_____ YES _____ NO

X8.19.5	Power steering reservoir:

”Remote mounted”							_____ YES _____ NO

Capacity: _____ qt.	Filter is easy to remove and replace	_____ YES _____ NO

X8.19.6	Is the remote filter factory mounted, certified, and engineering approved in conjunction with the

appropriate pump							_____ YES _____ NO

X8.20	Features considered as standard equipment but not addressed:

__________________________________________________________________________________

X8.21	Paint: Describe proposed method of painting:

___________________________________________________________________________________

___________________________________________________________________________________

X8.21.3	Wheel Paint: _______________________________________________________________

X8.22	Detail/Decorative Stripes with Logo:

X8.22.1	Width: _____ inches

X8.22.2	Will WVDOH logo area comply with 8.22.2 of specification	_____ YES _____ NO

X8.22.3	Does conspicuity striping material provided meet requirements of Section 8.22.3 through

8.22.8 of specification						_____ YES _____ NO

X8.22.4	Does sheeting meet specification as stated is 8.22.4	_____ YES _____ NO

Does it come with aggressive high tack pressure sensitive adhesive _____ YES _____ NO

Manufacturer:___________________________________________

X8.23	Does unit offered meet or exceed “Occupational Safety and Health Act of 1970”

_____ YES _____NO

X8.24	Does unit conform to the advertising guidelines 			_____ YES _____ NO

X8.25	Preventive Maintenance and Operator’s Training School

X8.25.1	Will a preventive maintenance and operator’s training seminar be provided_____YES_____NO

Manuals _____ (OR) CD _____

X8.25.2	Will booklets and pamphlets be furnished to be used by the operators_____ YES _____ NO

Describe agenda_____________________________________________________________

X8.25.3	Will you furnish all training aids; i.e. videos, projectors, etc . required in conducting the

training								_____ YES _____ NO

X9.0	SPECIFICATIONS – 304 STAINLESS STEEL COMBINATION DUMP/SPREADER BODY

The bidder should complete the following schedule in order for the Division to compare the actual bid

unit to the specifications.  Should the bidder except a requirement, then such exception may be only on

the basis that such feature is not offered by the manufacturer.  The Division will have the sole discretion

as to whether the bidder’s substitution meets the requirements of the specifications.

Bidder: _____________________________________________________________________________

Address: ____________________________________________________________________________

Telephone Number: ___________________________________________________________________

Years company has been an authorized dealer for proposed unit: __________ years

Manufacturer, model, series, and date of manufacture of proposed combination dump/spreader body:

____________________________________________________________________________________

____________________________________________________________________________________

Is descriptive literature full describing proposed combination dump/spreader body attached to your bid

proposal?	 								_____ YES _____ NO

If NO, refer to specification statement Section 6.6

When will required number of operating manuals, service manuals, and complete parts list be delivered

to the Equipment Division at Buckhannon?__________ prior to deliver of unit or __________________

Does the combination dump/spreader body have a minimum two (2) year basic bumper to bumper

Warranty including parts and labor?					_____ YES _____ NO

X9.1	Body capacity: ________ cubic yards water level

X9.2	Sideboard pockets and tailgate height provides additional capacities of _____ to _____ cubic yards

X9.3	Front body bulkhead	_____ gauge 	Size: _____ inch 	_____ stainless steel

X9.3.1		Is head sheet vertical		_____ YES _____ NO

X9.4	Does cab shield have sufficient clearance to ensure shield will not hit exhaust when dumping on uneven

Terrain									_____ YES _____ NO

X9.5	Two (2) front truck frame mounted tow hooks or eyes accessible through bumper_____ YES _____ NO

X9.6	Dimensions:

X9.6.1		Inside length of body: _________ inches

X9.6.2		Inside width of body:  __________ inches wide to maximize capacity and lower the center of

gravity

X9.6.3		Outside width of body: _________ inches at the integral fenders

X9.6.4		Body spacing from cab __________ inch

X9.6.5		Basic side height: __________ inches (measure from the floor to top rail)

Two (2) dirt shedding horizontal 10 gauge 201 stainless steel side braces on each side of body

_____ YES _____ NO

X9.6.6		Tailgate height: __________ inches (measure from the floor to top rail)

X9.6.7		Body overhang: __________ inches (measure from center of hinge pin)

X9.6.8		Cab protector: __________ inches x __________ inches with adequate clearance for cab

mounted air horns

X9.7	Cab protector sloped rearward for drainage purposes		_____ YES _____ NO

X9.8	Construction of the body sides, front, head, and tailgate:

Steel types: __________________________________

X9.8.1		Floor: __________ inch thickness 304 stainless ___

OR

abrasion resistant AR400___		_____ inches thick

X9.8.2		Sides: _____ Gauge 	_____ inch thickness 	_____ stainless steel

X9.8.3		Tailgate plate: _____ gauge 	_____ stainless steel

X9.8.4		Top rail: _____ gauge _____ stainless steel

X9.8.5		Cab protector: _____ gauge _____ stainless steel

X9.8.6		Is inside formed longitudinal constructed of ¼ inch 201 stainless steel

_____ YES _____ NO

Outside formed long sill of 7 gauge 201 stainless steel 	_____ YES _____ NO

with overall combined height of _____ inches including internal stainless gussets

_____ YES _____ NO

A ¼ inch thick 201 stainless steel fish plate is welded to outside surface outside long sill above the rear hinge						_____ YES _____ NO

X9.9	Is all the welding inside the body continuous and not skip welded		_____ YES _____ NO

Are all rails and posts continuous welded					_____ YES _____ NO

X9.10	Are the rear corner posts full length, one (1) piece construction		_____ YES _____ NO

X9.11	Cab protector sides, formed with gussets, extending forward __________ inches

Clearance above highest point of cab is __________ inches

X9.12	Is body a unibody design – no crossmembers				_____ YES _____ NO

X9.12.1	Does the body have one (1) piece sides constructed of 7 gauge 201 stainless steel

_____ YES _____ NO

X9.13	Floor constructed of _____ inch 	__________ (steel) with _____ inch round floor to side radius												_____ YES _____ NO

X9.15	Is there an integrated center conveyor providing the ability of the body to convey granular

materials with the body down 						_____ YES _____ NO

X9.15.1	12.5 inches truck frame to body floor height for lower center of gravity and lower mounting

height									_____ YES _____ NO

X9.15.1.1		Will wood products be used between truck frame and bed	_____ YES _____ NO

X9.15.2	Abrasion resistant steel 3/16 inch AR400 conveyor floor		_____ YES _____ NO

X9.15.3	2 inch diameter front and rear shafts with eight (8) tooth sprockets	_____ YES _____ NO

X9.15.4	Drive sprockets are double keyed to shaft				_____ YES _____ NO

X9.15.5	Conveyor width: _________ inches

X9.15.6	¼ inch 201 stainless steel formed inner sill which also forms the conveyor chain guard												_____ YES _____ NO

X9.15.7	7 gauge 201 stainless steel formed over long sills			_____ YES _____ NO

X9.15.8	3/16 inch AR400 conveyor bed floor				_____ YES _____ NO

X9.15.9	Formed _____ inch thick tie plate fully extend between the left and right side of body, located at

rear of  unit								_____ YES _____ NO

Will tie plate provide additional structural support at the rear of the body to prevent

sagging at the rear corner posts					_____ YES _____ NO

X9.15.10	Are there two (2) inch diameter drive shafts with eight (8) tooth sprockets

_____ YES _____ NO

Will sprockets be heat treated to 50 Rockwell C hardness	_____ YES _____ NO

X9.15.11	Will conveyor be driven with 25:1 planetary gearbox drive on the rear shaft with approximately

_____ CIR hydraulic motor						_____ YES _____ NO

Will motor have an integral conveyor speed sensor		_____ YES _____ NO

X9.15.12	Conveyor chain __________ pintle type (_____ lb. tensile/strand) with

_____ inch x _____ inch conveyor crossbars spaced on every other link.

_____YES_____NO

X9.15.13	A _____ gauge _____ stainless steel bolt in pan under the conveyor to keep material off chassis frame									_____ YES _____ NO

X9.15.14	Does the rear apron have a bolt on cover plate which allows for easy access to gear case

_____ YES _____ NO

X9.16	Is tailgate have 7 gauge 201 stainless steel full perimeter dirt shredding boxed 7 panel with a 7 gauge

201 stainless steel 9 inch x 24 inch fully adjustable rear feed gate		_____ YES _____ NO

X9.16.1	Is rear feedgate lever operated _____ or screw adjustable _____  The feedgate capable of being

positively locked into position					_____ YES _____ NO

X9.16.2	Is tail gate hinged at top, flame cut hardware, pork chop type off-set hardware to achieve

maximum opening of tail gate					_____ YES _____ NO

Does it have provision for pivoting at bottom			_____ YES _____ NO

X9.16.3	Flush mount, ½ inch flame cut 304 stainless steel tail gate pivots	_____ YES _____ NO

X9.16.4	Heavy duty offset hinge plates, one (1) inch flame cut 304 stainless steel_____YES_____NO

X9.16.5	¼ inch 304 stainless steel latch hooks with 3/8 inch 304 stainless steel latch plates

_____ YES _____ NO

X9.16.6	Full perimeter 201 stainless steel boxing with all horizontal edges sloped outward

_____ YES _____ NO

X9.16.7	Are there three (3) 10 gauge 201 stainless steel sloped horizontal braces that are flush with

perimeter boxing							_____ YES _____ NO

X9.16.8	Stainless steel upper pins with grease zerks				_____ YES _____ NO

X9.16.9	Latching action at the bottom of gate is operable by the truck driver without leaving the

truck cab								_____ YES _____ NO

X9.16.10	Is gate self aligning							_____ YES _____ NO

X9.16.11	Are tailgate lower latch pins 304 stainless steel 1 ¼ inch diameter	_____ YES _____ NO

X9.17	Does the body have the capability to convey to the rear with a stainless steel material spinner for

distributing material								_____ YES _____ NO

X9.17.1	Does it have a rear chassis mounted stainless steel spinner assembly that is adjustable left

to right, and up and down to assure accurate placement of material on spinner disc to

facilitate control of spread pattern.					_____ YES _____ NO

X9.17.2	10 gauge stainless steel 20 inch diameter spinner disc to have replaceable fins

_____ YES _____ NO

X9.17.3	Are spinner disc vanes 304 stainless steel				_____ YES _____ NO

X9.17.4	Is spinner motor mounted on top of spinner disc	_____ YES _____ NO

Is it enclosed in removable material shedding protective cover	_____ YES _____ NO

X9.17.5	Is spinner disc driven by a 4-bolt 2.8 CIR hydraulic motor	_____ YES _____ NO

X9.17.6	Does spinner motor have an integral sensor capable of providing spinner disc feedback to

the in-cab console							_____ YES _____ NO

X9.18	Hydraulic Hoist:

X9.18.1	Is it trunnion mounted to bottom of dump body			_____ YES _____ NO

X9.18.2	Is telescopic hoist no less than N.T.E.A. Class 90 – Double Acting with 26 ton capacity

_____ YES _____ NO

X9.18.3	Is single hoist cylinder trunnion mount				_____ YES _____ NO

X9.18.4	Does hoist cylinder have three (3) stages with _____ inches of stroke _____ YES _____ NO

Manufacturer and model: ________________________________

X9.18.5	Does the cylinder have wear and corrosion resistant nitrided cylinder tubes

_____YES _____NO

X9.18.6	Cylinder warranty: _____ years

X9.18.7	Does a five (5) degree oscillating cylinder collar protect the cylinder against side stress, if

trunnion mount cylinder provided					_____ YES _____ NO

X9.18.8	Does the body have 6 inch x 8 inch x 1/2 inch formed angle rear hinge assembly installed

in the truck chassis frame						_____ YES _____ NO

X9.18.9	Does the rear hinge assembly have cold roll steel hinge pins connecting to 2 1/2 inch hinge

blocks with grease zerks						_____ YES _____ NO

X9.19	Are the following features included:

X9.19.1	Warning light (bed raised) console mounted			_____ YES _____ NO

X9.19.2	Hydraulic oil level reading						_____ YES _____ NO

X9.19.3	Safety decals as required						_____ YES _____ NO

X9.19.4	201 stainless steel mud guards, 10 gauge x 24 inches x 30 inches permanently attached in

front of rear wheels 							_____ YES _____ NO

Will body vendor align exhaust stack for body clearance	_____ YES _____ NO

X9.19.5	201 stainless steel shovel bracket					_____ YES _____ NO

X9.19.6	201 stainless steel gussets (board pockets) for 4 inch x 6 inch lumber (rough) located at

front and rear and mid-rail						_____ YES _____ NO

4 inch x 6 inch (rough) oak sideboards supplied and bolted through the gussets

_____ YES _____ NO

Painted aluminum to match the body				_____ YES _____ NO

X9.19.7	Does the unit have air operated tailgate spring applied air release mechanism

_____ YES _____ NO

Pivot shafts included stainless steel bushings to eliminate seizing_____ YES _____ NO

X9.19.8	1 1/2 inch 304 stainless steel grip strut walk rail installed on both sides of the body

_____ YES _____ NO

X9.19.9	OSHA approved backup alarm, electronic ambient, adjusts to background noise, 112 dba

shock mounted at the rear						_____ YES _____ NO

X9.19.10	OSHA approved body support, both sides				_____ YES _____ NO

X9.19.11	Unit equipped with 49,000 lb. capacity pintle hook centered between rear frame rails

_____ YES _____ NO

Manufacturer and Model: ___________________________________

Height from ground level to center line of pintle “eye”: _____ inches

X9.19.12	Air deflector-hood mounted, blue or smoke			_____ YES _____ NO

Deflector manufacturer’s standard width for truck mode	_____ YES _____ NO

Width: _________________

Access to front end hood tilt handle				_____ YES _____ NO

Extra handle								_____ YES _____ NO

X9.20	Lighting: Weather/shock resistant lights LED type with average amp draw between .045 - .72

_____ YES _____ NO

Manufacturer and Model: _____________________________________

All connections have sure snap plug assemblies and epoxy sealed electronics to protect against shock

and vibration									_____ YES _____ NO

X9.20.1	All marker lights 2 1/2 inch diameter flush mount sealed beam lights with integral reflector

mounted in rubber base						_____ YES _____ NO

X9.20.2	Are all lights connected to chassis through a weatherproof junction box located at the rear

of truck								_____ YES _____ NO

X9.20.3	Rear lights shock mounted, recessed oval stop, tail, turn, and recessed oval back up lights

mounted in back post							_____ YES _____ NO

Strobe lights marked and switched from dash board location	_____ YES _____ NO

Manufacturer and Part #: ______________________________

X9.20.4	Center rear I.D. lights three (3) located in truck chassis		_____ YES _____ NO

X9.20.5	Two (2) amber oval LED strobe lights mounted at the front corners of the cab protector, and two

(2) amber oval LED strobe lights mounted at each outside corner of the cab protector

_____ YES _____ NO

Manufacturer and Part # of Both Locations: _______________________________

Strobe lights marked and switched at dash board location		_____ YES _____ NO

X9.20.6	Auxiliary headlights for snowplowing application shock mounted on fender of unit

_____ YES _____ NO

Manufacturer and Part #: ________________________________

X9.20.7	Two (2) oval amber LED strobe lights mounted at top of rear corner posts right and left sides and

switched in combination with cab protector strobe			_____ YES _____ NO

Manufacturer and Model: ___________________________________

X9.20.8	Lighted license plate bracket						_____ YES _____ NO

X9.21	Are the following at the front or rear both sides of the body:

X9.21.1	304 stainless steel fold down ladder that locks into position when either in the down or up

position								_____ YES _____ NO

X9.21.2	Two (2) 304 stainless grab handles					_____ YES _____ NO

X9.21.3	Is the design and strength characteristics of entire body such that the unit structural members and

hoisting system will not suffer any deformation, damage, or structural failure resulting from

raising a distributed full payload					_____ YES _____ NO

X9.22	Bumper:

X9.22.1	Bumper formed out of 1/4 inch roll steel _____ YES _____ NO

Weighs _____ lbs. per square foot

X9.22.2	Bumper face covers all of truck frame (_____ inches) with two (2) flanges of _____ inches top

and bottom 								_____ YES _____ NO

X9.22.3	Overall width of bumper: ________ inches

X9.22.4	Bumper straight across front from centerline of truck chassis _____ inches each side of

Centerline, making bumper straight ______ inches long in center with ends swept back

______ degrees and ______ inches each side.

X9.22.5	Bumper has two (2) access holes for utilization of tow hooks	_____ YES _____ NO

X9.22.6	Upper and lower flanges cut and welded solid at point where bumper is bent and ground off

smooth									_____ YES _____ NO

X9.22.7	Bumper mounted by two (2) mounting angles bolted to front of truck frame with two (2)

5/8 inch bolts each side						_____ YES _____ NO

X9.22.8	Mount angle ______ inch x ______ inches x ______ long with four (4) 5/8 inch holes

_____ YES _____ NO

X9.22.9	Paint on front bumper: ______________________________________________________

X9.23	Underbody Tool Box:

X9.23.1	One (1) tool box mounted under body on right side frame rail	_____ YES _____ NO

X9.23.2	Tool box ______ inches high, ______ inches wide, ______ inches deep cradled by a heavy steel

angle frame attached to the truck frame				_____ YES _____ NO

X9.23.3	Construction _____ gauge, ______ galvanneal steel with all seams welded____YES____NO

X9.23.4	Tool box has horizontal hinged fold down door			_____ YES _____ NO

X9.23.5	Tool box door has cable or chain to hold the door in a horizontal position _____ YES _____ NO

X9.24	Load covering system electrically or air controlled				_____ YES _____ NO

X9.24.1	Electric motor assembly includes 12 volt direct drive motor with forward and reverse action, cab

mounted control switch, resettable circuit breaker			_____ YES _____ NO

X9.24.2	Pivot arm assembly constructed in a two (2) piece bent arm configuration of _____ inch

_____ gauge steel tubing						_____ YES _____ NO

X9.24.3	Bent arm extensions constructed of ______ inch ______ gauge steel tubing

X9.24.4	Rear cross constructed of _____ inch _____ gauge steel tubing

X9.24.5	Pivot arm rests included						_____ YES _____ NO

X9.24.6	Underbody spring extension spring ______ inches in length attached to base of pivot arm and of

body with articulating spring mounting bracket			_____ YES _____ NO

X9.24.7	All steel components finished with manufacturer’s recommended rust preventative system

with adequate primer and paint					_____ YES _____ NO

X9.24.8	Steel cab protector mounted triple bend wind deflector provided	_____ YES _____ NO

X9.24.9	Load covering system provided with a _____ oz. black vinyl tarp to fit 14 foot 6 inch body

_____ YES _____ NO

X9.24.10	Load covering system supplied with all necessary hardware and delivered to the West

Virginia Division of Highways as a complete and operational unit._____ YES _____ NO

X9.25	Paint:  Describe proposed method of painting

X9.25.1	Will the 304 stainless steel surfaces of the body be “paint free”	_____ YES _____ NO

X9.25.2 – X9.25.4

__________________________________________________________________________________________

__________________________________________________________________________________________

__________________________________________________________________________________________

X9.26	Detail/Decorative Stripes with Logo:

Will striping and detailing you provide comply with requirements of Section 9.26.1 through 9.26.7

_____ YES _____ NO

X9.27	All body features considered as standard, but not specifically addressed:

__________________________________________________________________________________________

__________________________________________________________________________________________

X9.28	Does the proposed unit meet or exceed the “OSHA OF 1970” and/or subsequent changes

_____ YES _____ NO

X10.0	SPECIFICATIONS - CENTRAL HYDRAULIC SYSTEM

Is the central hydraulic system designed to operate the following:

A front mounted telescopic dump body hoist cylinder, a hydraulically driven integrated salt and abrasive

spreader system requiring the simultaneous operation of two (2) hydraulic motors in two (2) different

modes with conveyor reverse, a single acting snowplow lifting cylinder, a snowplow power angle

system, plow balance system and an auxiliary equipment drive circuit	_____ YES _____ NO

Are provisions made for future add on pre-wet system		_____ YES _____ NO

Bidder: _____________________________________________________________________________

Address: ____________________________________________________________________________

Telephone Number: ___________________________________________________________________

Years company has been an authorized dealer for proposed unit: __________ years

Manufacturer, model, series, and date of manufacture of proposed central hydraulic system:

____________________________________________________________________________________

____________________________________________________________________________________

Is descriptive literature full describing proposed central hydraulic system attached to your bid

proposal?	 								_____ YES _____ NO

If NO, refer to specification statement Section 6.6

When will required number of operating manuals, service manuals, and complete parts list be delivered

to the Equipment Division at Buckhannon?__________ prior to deliver of unit or __________________

Describe: ___________________________________________________________________________

____________________________________________________________________________________

Are provisions made for a future add-on hydraulic driven pre-wet system_____ YES _____ NO

Pre-Wet System:

Does supplied spreader control contain the ability to control a closed loop pre-wet system

_____ YES _____ NO

Does system operate using a flow meter feedback circuit			_____ YES _____ NO

Does controller software allow for adjustability of pre wet output by the operator, represented in

gallons per ton								_____ YES _____ NO

Is information related to pre wet application rate and total flow in gallons displayed on the screen

while the pre wet system is active						_____ YES _____ NO

Does central hydraulic system have a minimum two (2) year basis bumper to bumper warranty

including parts and labor?							_____ YES _____ NO

X10.1	Pump System:

X10.1.1	Pump: Variable volume pressure compensated load sensing axial piston type

_____ YES _____ NO

X10.1.2	Front mounting flange and main housing/case of cast iron construction_____ YES _____ NO

Inlet and outlet port section of high strength ductile iron with SAE split flange porting or orb 			type porting								_____ YES _____ NO

X10.1.3	Is suction port and associated plumbing sized to allow for minimum inlet restriction

between the pump and the suction port on the reservoir?	_____ YES _____ NO

Does installation comply with pump manufacturers allowable inlet condition specifications

_____ YES _____ NO

Is suction plumbing equal to or greater than pump inlet or suction size____ YES ____ NO

X10.1.4	Is pressure port of the SAE split flange or ORB type side mounted for direct bolt mounting of

solenoid shut down valve assembly					_____ YES _____ NO

X10.1.5	Case drain and load sense signal ports of the SAE O-ring type	_____ YES _____ NO

Case drain line taken directly to tank without passing through the return line filter

_____ YES _____ NO

X10.1.6	Input shaft has a minimum continuous torque rating equal to _____% of the imposed load

when pump is operated at maximum engine rpm, maximum displacement and system

pressure								_____ YES _____ NO

Is it minimum SAE “C” keyed					_____ YES _____ NO

X10.1.7	Front input shaft bearing heavy duty ball or roller type designed for high axial and radial loading

_____ YES _____ NO

Rear shaft bearing of the high speed and load sleeve type design	_____ YES _____ NO

Bearings fully lubricated by flooded case oil				_____ YES _____ NO

X10.1.8	Ramp/swashplate supported by pressure lubricated bearings of the rocker cam or saddle type for

high piston load support						_____ YES _____ NO

Ramp angle positioning by means of dual servo control cylinders for rapid pump response and

precise pump output control						_____ YES _____ NO

X10.1.9	Adjustable load sense and high pressure compensator control valve assembly of the full cartridge

or of bolt on housing design for ease of replacement and repair	_____ YES _____ NO

X10.1.9.1		System design and components provide flow, pressure and performance

requirements with a maximum operating load sense differential pressure of

______ PSI and a maximum standby pressure of ______ PSI for maximum

efficiency.

If pilot control shifted valving is used, is it designed to be fully functional within this

pressure range  						_____ YES _____ NO

X10.1.9.2		High pressure compensator valve preset to limit the maximum pump output pressure to

maximum required operating pressure plus load sense differential and margin pressure to

prevent premature de-stroking of ramp resulting in reduced or insufficient pump output

_____ YES _____ NO

X10.1.10	Pump Output:  Is it capable of providing hoist cylinder extension required

____ YES _____ NO

Part number ______________________________________ - ______ gallons to fully extend but 			after filling _____ gallons is required to raise the cylinder:

10 GPM flow rate	_____ seconds to raise

15 GPM flow rate	_____ seconds to raise

20 GPM flow rate	_____ seconds to raise

25 GPM flow rate	_____ seconds to raise

30 GPM flow rate	_____ seconds to raise

35 GPM flow rate	_____ seconds to raise

40 GPM flow rate	_____ seconds to raise

Part number _______________________________________ - ______ gallons to fully extend

_____ gallons to fill and _____ gallons to extend

5 GPM flow rate	_____ seconds to raise

10 GPM flow rate	_____ seconds to raise

15 GPM flow rate	_____ seconds to raise

20 GPM flow rate	_____ seconds to raise

25 GPM flow rate	_____ seconds to raise

30 GPM flow rate	_____ seconds to raise

40 GPM flow rate	_____ seconds to raise

X10.1.11	Is the make and model bid in compliance with overall quality of construction, design, and

performance of the pump supplied 					_____ YES _____ NO

X10.1.12	Pump:

Manufacturer and Model: ______________________________________________________

X10.1.13	Is pump manufacturers standard product release and design	_____ YES _____ NO

X10.1.14	Is pump driveline assembly of the keyed shaft design utilizing a 4 bolt driveshaft flange and

matching drive yoke on the pump 					_____ YES _____ NO

X10.1.14.1		Does driveline have a minimum continuous torque rating equal to 200% of the

imposed load when pump is operating at maximum system requirements

_____ YES _____ NO

Manufacturer and Model: _________________________________________________

X10.1.14.2		Are dual journals and yokes incorporated to connect the pump shaft and engine drive

flange with an angular misalignment no greater than six (6) degrees and not less than two

(2) degrees							_____ YES _____ NO

X10.2	Pump Shutdown System:

X10.2.1	Normally closed, energize to open, solenoid operated control valve of the cartridge and

manifold design to be directly bolted to pump pressure port	_____ YES _____ NO

Is solenoid electrical connection of the Packard “Weatherpack” type with “SO” cable

wiring									_____ YES _____ NO

X10.2.2	Is valve controlled by a console mounted “Master On” switch with pilot lamp for normal system

operation and by a float switch located in hydraulic reservoir to automatically shut off pump

pressure port flow to all down stream functions in the event of low hydraulic oil level

_____ YES _____ NO

X10.2.3	Pressure drop across valve _____ PSI at _____ GPM flow when in the switched open position

Nominal valve rating _____ GPM at _____ PSI

X10.2.4	SAE #6 gauge port equipped with Parker Hannifin Model PD361 diagnostic coupling nipple and

protective cap provided for pump output pressure testing to be installed in valve manifold and

within an easily accessible mounting position			_____ YES _____ NO

X10.2.5	Valve designed to protect the pump from damage when the system is shut down at high pressure

and flow operation							_____ YES _____ NO

X10.2.6	Valve manufacturer and model: _________________________________________________

X10.2.7	Central control console mounted audio alarm and warning lamp indicating pump pressure/flow

shutdown								_____ YES _____ NO

X10.2.8	Warning lamp press-to-test light and incorporate a switching system into the automatic shutdown

assembly to simulate low oil level, shut off pump output flow and test float switch wiring and

connection								_____ YES _____ NO

X10.2.9	A console mounted electrical override function switch provided to allow momentary operation of

hydraulic functions in emergency situations				_____ YES _____ NO

X10.3	Directional Control Valve Assembly:

X10.3.1	Valve stacked section type and of closed center circuit design	_____ YES _____ NO

X10.3.2	Each work section pressure and flow compensated with fully integrated load sense network

_____ YES _____ NO

Flow output is relative to spool travel with preset maximum flow rate obtained at maximum

spool stroke providing feathering control of operated function	_____ YES _____ NO

X10.3.3	Dump body, snowplow lift, and snowplow power angle sections of the manual cable shift type

_____ 	YES _____ NO

Auxiliary circuit section of the electric solenoid shift type		_____ YES _____ NO

Both ends of each section valve spool sealed with weather resistant caps or cable entry bonnets

_____ YES _____ NO

X10.3.4	Valve assembly flow capacity rating and pressure drop characteristics sufficient to provide

for the required pump output and circuit flow rates at the specified maximum load sense differential pressure settings					_____ YES _____ NO

X10.3.5	All valve ports of the SAE o-ring seal type and of sufficient size to handle required section flow

rates at stated load sense differential pressure			_____ YES _____ NO

X10.3.6	Is valve a pre-compensated design					_____ YES _____ NO

A priority section installed to allow plow to raise in a system over demand situation

_____ YES _____ NO

X10.3.7	Main pressure inlet relief valve provided to reduce system pressure shock loads

_____ YES _____ NO

Is it preset at pressure so as not to interfere with pump pressure compensator and to prevent

premature relief opening at system high demand operation		_____ YES _____ NO

X10.3.8	If pilot pressure reducing valve is required for solenoid section control, design meets

operating requirements as set forth in Section 10.1.9.1		_____ YES _____ NO

Pilot supply and tank venting internal within the valve assembly section____ YES ____ NO

X10.3.9	Load sense network high pressure relief provided and preset to limit system maximum operating

pressure								_____ YES _____ NO

Set point provides proper pressure margin to pump pressure compensator and high pressure relief

valve as to prevent premature loss of required flow rates and pressure capability

_____ YES _____ NO

X10.3.10	SAE #6 gauge 0port equipped with Parker Hannifin PD361 diagnostic coupling nipple with

protective cap for load sense testing to be installed in an easily accessible location

_____ YES _____ NO

X10.3.11	Dump body control section 4-way three (3) position spring centered cylinder spool for operation

of a double acting hoist cylinder					_____ YES _____ NO

X10.3.11.1		Full flow workport relief valve installed in power up port	_____ YES _____ NO

Set point to prevent operating pressure from exceeding hoist cylinder normal operating

pressure rating							_____ YES _____ NO

X10.3.11.2		Is full flow work port relief valve installed in power down port set at 500 PSI to prevent

full system pressure on down stroke				_____ YES _____ NO

X10.3.12	Snowplow lift control section is 4-way three (3) position spring centered cylinder spool for

operation of a double acting lift cylinder 				_____ YES _____ NO

X10.3.12.1		Adjustable flow control installed to limit downward speed of snowplow														_____ YES _____ NO

Flow limiting control system preset for proper plow lift speed to be supplied to reduce

over demand operation and to increase system efficiency	_____ YES _____ NO

Will flow limit be determined at time of pilot model review	_____ YES _____ NO

X10.3.13	Snowplow power angle control section is 4 way three (3) position spring centered cylinder spool

for operation of cylinder type reversible plow			_____ YES _____ NO

X10.3.13.1		Flow limiting control system preset for proper plow reversing speed to be supplied to

reduce over demand operation and to increase system efficiency _____YES _____NO

Will flow limit be determined at time of pilot model review	_____ YES _____ NO

X10.3.14	Plow Balance Valve:

X10.3.14.1		Is hydraulic system supplied with a plow balance valve	_____ YES _____ NO

X10.3.14.2		Is valve designed to offset a specific (adjustable) plow weight when activated

_____ YES _____ NO

X10.3.14.3		Does plow balance system not alter the operation of any other hydraulic function or

have an adverse effect on the performance of other hydraulically operated

equipment including:

Wing Plow				_____ YES _____ NO

Body Hoist				_____ YES _____ NO

Plow Hoist or Angle			_____ YES _____ NO

Spreader functions			_____ YES _____ NO

Are all normal operations of the plow lift/lower functions maintained without

additional tasks						_____ YES _____ NO

X10.3.14.4		Will plow lift be immediate to guarantee safe operation of the vehicle

_____ YES _____ NO

X10.3.14.5		Are solenoid valve coils used				_____ YES _____ NO

Will they have manual override capabilities if needed for continued use when coils

fail								_____ YES _____ NO

X10.3.14.6		Does manifold valve include a pressure test point for use when checking balance

pressures							_____ YES _____ NO

X10.3.14.7		Is pressure test point capable of tapping into system at pressures of 5,000 PSI

_____ YES _____ NO

X10.3.15	Auxiliary equipment drive circuit control section 3-way three (3) position spring centered

solenoid operated motor spool					_____ YES _____ NO

Is the circuit separate and distinct from the spreader control system	_____ YES _____ NO

X10.3.15.1		Flow limiting control system preset to provide _____ GPM at a system load pressure

of

_____ PSI.  Pump is capable of supplying this flow rate with engine speed of

______ RPM

X10.3.15.2		Is an inline mounted control valve supplied for this operation in place of directional

control valve section						_____ YES _____ NO

If supplied, is proper interconnections and venting of load sense network system

provided							_____ YES _____ NO

X10.3.15.3		Is pressure line 3/4” SAE 100R2 hose and manifold mounted at rear of chassis and

equipped with Parker Hannifin SH6-62 quick disconnect coupler and protective metal

plug 								_____ YES _____ NO

Is mating nipple SH6-63 with protective cap supplied	_____ YES _____ NO

Will mounting location be determined at time of pilot model review _____YES_____NO

X10.3.15.4		Manufacturer and model of directional and auxiliary circuit valves:

_____________________________________________________________________

X10.3.16	Is directional control valve assembly located in a combination tank/valve stainless enclosure assembly to protect the hydraulic tank/valve from the elements

_____ YES _____ NO

Capacity of reservoir (tank) ______ gallon

X10.3.17	Pre-Wet Circuit:

X10.3.17.1		Is a separate circuit provided to control an add-on pre-wet system

_____YES _____NO

X10.3.17.2		Is hydraulic valve of the sectional type _____YES_____ NO OR of the cartridge style 				contained in a manifold _____ YES _____ NO

X10.3.17.3		If manifold type valve is supplied, it it attached to the main valve assembly

_____ YES _____ NO

X10.3.17.4		Is all wiring to pre-wet hydraulic circuit provided as part of the system contained in

the bid								_____ YES _____ NO

X10.3.17.5		Is wiring to the control console related to the rest of the pre-wet system (low level

float, flow meter connection, etc.) provided as part of the pre-wet package at the

time of pre-wet system install				_____ YES _____ NO

X10.4	Spreader Control Valve Assembly:

X10.4.1	Are spinner and conveyor solenoid flow controls of the PWM proportional solenoid type and

equipped with manual overrides 					_____ YES _____ NO

Are overrides manually adjustable over operating flow range in the event of electrical system

failure									_____ YES _____ NO

X10.4.2	Flow control circuits are pressure compensated			_____ YES _____ NO

Provides spinner and pre-wet flow rate of __________ GPM and a conveyor flow rate of

__________ GPM

Pressure relief valve system limit circuits to __________ PSI

X10.4.3	Load sense circuits connected to directional control valve network for proper pump control

_____ YES _____ NO

Does design prevent improper high pressure load sense signal and pressure line loading

when spreader valve is not in use and when spreader quick disconnects are uncoupled

_____ YES _____ NO

X10.4.4	Is PWM solenoid control supplied by microprocessor spreader control system

_____ YES _____ NO

Are solenoids capable of 100% PWM signal without failure		_____ YES _____ NO

X10.4.5	Solenoid operated directional control valve and in-cab mounted electrical switch operates

spreader conveyor reverse required for front or rear material discharge selection provided

_____ YES _____ NO

X10.4.6	Is electrical switching and indicator light for spreader clogged indication provided

_____ YES _____ NO

X10.4.7	Manufacturer and model of valve: _______________________________________________

X10.5	Spreader Control System:

X10.5.1	Dual flow, ground speed oriented spreader control system of the closed loop microprocessor

based type with nonvolatile control memory				_____ YES _____ NO

X10.5.2	Automatic calibration and flexibility of programming		_____ YES _____ NO

X10.5.3	System is capable of operation in ground speed oriented closed loop conveyor feed back,

open loop, manual set, blast and unload modes and fully functional in both front and rear

material discharge selection						_____ YES _____ NO

X10.5.4	Automatic switchover with display indication from closed loop to open loop operation in the

event of loss of feed rate sensor signal is provided			_____ YES _____ NO

X10.5.5	Control console digital readouts capable of displaying actual application rate, vehicle ground

speed, distance of spread route driven and total quantity of material spread

_____ YES _____ NO

X10.5.6	Programming and output cable connection for material and trip information printer and program

uploading is provided							_____ YES _____ NO

X10.5.7	Control unit capable of accumulating display information up to 999,999 miles and 999,999 tons

of discharged material							_____ YES _____ NO

X10.5.8	Console programming capable of selection, calibration and display of four (4) separate spread

materials with independent application rates of each material capable of being set to fixed rates

or to rate increments of a preset maximum application rate		_____ YES _____ NO

X10.5.9	A variable digital access code lockout for application rate selection and for system operating

perameters is provided						_____ YES _____ NO

Is it a key switch							_____ YES _____ NO

X10.5.10	Backlighted switches and LCD screen utilized for on-board programming and for display

readout and application rate selection				_____ YES _____ NO

X10.5.11	Is material spread width selectable by no less than 10 position switch with minimum and

maximum spinner speed totally programmable through entire flow range_____ YES _____ NO

Is spinner speed capable of linking to ground speed for on-off control _____ YES _____ NO

X10.5.12	Does display enunciate error message and sound audio alarm when microprocessor system

detects any loss of control or accuracy				_____ YES _____ NO

X10.5.13	Will system be fully functional at time of delivery			_____ YES _____ NO

X10.5.14	Is truck speed sensor compatible with type of speedometer drive system supplied on chassis

_____ YES _____ NO

X10.5.15	Is a built-in ground speed simulator provided either internal to the control or located in the

control console							_____ YES _____ NO

X10.5.16	Are all components required for proper installation and operation of control system onto

truck and spreader units supplied					_____ YES _____ NO

X10.5.17	Manufacturer and model of proposed control system	:

____________________________________________________________________________

X10.6	Central Control Console:

X10.6.1	Mounted between seats within easy access of the driver		_____ YES _____ NO

X10.6.1.1		Warning light (bed raised) control console mounted		_____ YES _____ NO

X10.6.2	Will all wiring, valve control cables and electrical harness entry into cab and console

sealed with grommets						_____ YES _____ NO

X10.6.3	Are remote control valve levers console mounted			_____ YES _____ NO

Are all levers clearly marked as to function and operation		_____ YES _____ NO

X10.6.3.1		Remote control levers to operate push-pull type cables with .250” diameter stainless steel

rod ends							_____ YES _____ NO

X10.6.3.2		Is inner cable member 18-8 stainless steel armor wrapped construction with a low

resistance nylon liner and polyethylene covered tempered steel wire conduit

_____ YES _____ NO

X10.6.3.3		Is cable to valve connection of the weather resistant bonneted type___YES___NO

X10.6.3.4		Hoist control lever OSHA compliant (hoist interlock)	_____ YES _____ NO

X10.6.4	Are central console or dash mounted rocker switches with indicator lamps provided for strobe

lights, spreader light and plow lights isolated from all hydraulic system control circuits													_____ YES _____ NO

X10.6.4.1		Are interconnections and cables installed and ready for operation _____ YES _____ NO

X10.6.4.2		Is hydraulic system automatic shutdown system and control switching relay controlled 												_____ YES _____ NO

X10.6.4.3		Relay(s) mounted within the cab				_____ YES _____ NO

X10.6.4.4		An access plate to internal wiring is provided 		_____ YES _____ NO

X10.7	Hydraulic Reservoir:

X10.7.1	Tank/valve enclosure flex mounted to the chassis frame rail		_____ YES _____ NO

X10.7.2	Tank constructed of _____ gauge ___ stainless steel		_____ YES _____ NO

X10.7.3	Tank equipped with a combination oil level sight glass and thermometer _____ YES _____ NO

X10.7.4	Tank equipped with a pressurized ten (10) micron filter/breather cap with removable 500 micron

Strainer								_____ YES _____ NO

X10.7.5	Is an internal stainless steel baffle provided within the tank		_____ YES _____ NO

X10.7.6	Tank stenciled with minimum of 1 1/2” high “Hydraulic Oil”	_____ YES _____ NO

X10.7.7	Tank level switch connection “SO” type wiring and flange mounted within the tank/valve 			enclosure to protect it from the elements				_____ YES _____ NO

X10.7.8	Reservoir supply suction port _____ inches NPT and system report port ______ inches

NPT

X10.8	Filtration:

X10.8.1	Manufacturers standard filtration to adequately protect the hydraulic system from damage

_____ YES _____ NO

X10.8.2	Return line filter isolated from reservoir by a full flow non-restrictive type quarter turn brass ball

valve if filter not installed in reservoir				_____ YES _____ NO

X10.8.3	Each filter equipped with a differential pressure switch to indicate filter clogged condition by

means of a console mounted indicator lamp				_____ YES _____ NO

X10.8.4	One (1) extra replacement filter for each assembly is provided for each truck

_____ YES _____ NO

X10.8.5	Filter assemblies positioned as close to reservoir as possible and in an easily accessible service

location								_____ YES _____ NO

X10.9	Hoses and Fittings:

X10.9.1	Each hose assembly (hose with hose ends) except for suction hose is fitted with JIC swivel

connections on ends where connection to system component is made _____ YES _____ NO

X10.9.2	All pressure line hoses meet or exceed SAE Specification 100R2 and are equal to Gates high

pressure hose, type C2AT for sizes up to and including 1 inch ID	_____ YES _____ NO

X10.9.3	Suction hose 2 inch nominal ID and meet SAE Specification 100R4, braided fiber, spiral wire

reinforced, rubber covered hose with replaceable bolt-on type fittings _____ YES _____ NO

X10.9.4	All hydraulic hoses fully cleaned on interior, installed, and ready for operation

_____ YES _____ NO

X10.9.5	Are grommets used when routing hoses through steel bracketing or frame members

_____ YES _____ NO

X10.9.6	Are Snap-Tite quick disconnects (manifold mounted) supplied for spinner 1/2 inch

pressure and return lines (VH Series Auger/Conveyor) 		_____ YES _____ NO

Is iron or galvanized iron pipe for fittings and connectors used	_____ YES _____ NO

X10.9.7	Are all fittings and connectors steel type designed for high pressure hydraulic system use

_____ YES _____ NO

X10.9.8	Pipe thread ported components and connectors are only used when the specific component is not

available with SAE or JIC porting					_____ YES _____ NO

X10.9.9	Are all pipe thread connectors used coated with liquid Teflon pipe sealer prior to assembly

_____ YES _____ NO

X10.9.10	Hoses that run to the front of truck chassis for snowplow functions are manifold mounted behind

the front bumper with sufficient access for pump service and snowplow hitch installation

_____ YES _____ NO

X10.9.11	Are snowplow lines equipped with complete 1/2 inch “VH” series Snap-tite quick disconnects

(coupler and nipple supplied) and metal caps and plugs		_____ YES _____ NO

X10.10	 Items not specifically stated but are necessary for proper system installation and operation are

supplied and comply with recommended hydraulic industry standards:

___________________________________________________________________________________

___________________________________________________________________________________

X10.11	Will initial servicing and pre-testing of hydraulic system be included for:

X10.11.1	Initial fill of reservoir with a high grade 32 AW hydraulic fluid to approximately 40 gallon

level, marked on sight glass			:			_____ YES _____ NO

X10.11.2	Start-up and initial run of hydraulic system, checking for leaks, excessive heat, system

efficiency								_____ YES _____ NO

Will you replace any defective component				_____ YES _____ NO

Will you cover any defects discovered at time of plow installation if equipment is not

available at time of initial test of plow circuits			_____ YES _____ NO

X10.11.3	Refill reservoir to the 40 gallon operating level			_____ YES _____ NO

X10.12	 If any hydraulic lines are located within 10 inches of exhaust system are they metal lines and insulated

_____ YES  ____ NO

X10.13	 Are detailed component specifications, product literature, system component layout drawing with

bill of  materials and full functional hydraulic system schematics in accordance with JIC and

ANSI-Y32 format attached with your bid					_____ YES _____ NO

X10.14	 If successful vendor, will you provide WVDOH with a complete list of all filters required for

normal maintenance on proposed unit					_____ YES _____ NO

X10.15	 Explain your training sessions with each purchase order covering the operation, maintenance,

trouble shooting and calibration/programming of the hydraulic system and spreader controls and

where will they be held:

___________________________________________________________________________________

___________________________________________________________________________________