1.	SPECIFICATIONS

The following sections of the West Virginia Department of Transportation, Division of Highways Standard Specification Roads and Bridges, adopted 2010, as modified by the January 1, 2011 Supplemental Specifications shall apply to the administration of this Contract:  101, 102.4, 102.5, 105.1, 105.3, 105.4, 105.10, 105.11, 105.12, 105.13, 106.3, 106.4, 106.5, 106.6, 106.7, 106.9, 107.1, 107.2, 107.3, 107.14, 107.19, 107.20, 108.8, 109.1, 109.2, and 109.20.

The terms "Contractor" and "Vendor" used in the above specifications or this contract are interchangeable.  Contractor shall mean Vendor and Vendor shall mean Contractor.

West Virginia Department of Transportation, Division of Highways Standard Specifications Roads and Bridges, adopted 2010 and the January 1, 2011 Supplemental Specifications may be obtained from:

West Virginia Division of Highways

Contract Administration

Building 5, Room 722

1900 Kanawha Boulevard, East

Charleston, West Virginia  25305

Phone:  304-558-2885

http://www.transportation.wv.gov/highways/contractadmin/specifications/2010StandSpec/Pages/default.aspx

2.	SCOPE OF WORK

To provide all labor, equipment, services, articles and incidentals necessary for Herbicide Spray System	with Operator, to provide herbicide application in the form of guardrail spraying, brush-spraying and	wildflower plot spraying for all ten (10) Districts throughout the State of West Virginia.

3.	BIDDING INSTRUCTIONS

Vendors may quote on any or all of the items listed on Bid Schedule, Section 20.

Unit price per acreage sprayed utilizing the spray boom truck or the articulated spray boom truck using herbicide material supplied by the Division of Highways shall be quoted on items one (1) through three (3) on the Bid Schedule.

Unit price per acreage sprayed utilizing a handheld or backpack style sprayer, or similar sprayer, provided by the vendor, using herbicide material supplied by the Division of Highways shall be quoted on item four (4) on the Bid Schedule.

Unit price per acreage sprayed utilizing the spray boom truck or the articulated spray boom truck using herbicide material supplied by the vendor shall be quoted on items five (5) through eight (8) on the Bid Schedule.  Herbicide material furnished under this contract, items five (5) through eight (8) on the Bid Schedule, shall conform to the physical and chemical properties set out in the EPA Registration of the product.

Vendors may quote Product Name requested or provide an “or equal” product for items five (5) through eight (8) on the Bid Schedule.  The vendor shall list the trade name and EPA Registration Number for items five (5) through eight (8) on the Bid Schedule.  Failure to list this information will result in the disqualification of the vendor’s bid on that product.

Equivalency, chemical name, equal or equivalent shall mean equal to and not necessarily identical.  At the time of bid, if the vendor is bidding an “or equal” product, the vendor shall provide the label from the product to eliminate any confusion in determining equivalency to Product Name requested.   Additional pertinent product specifications and technical information should be submitted with the bid and may also be used to determine equivalency.

Prior to award of low bid, the Division of Highways may require samples of equivalent herbicide for evaluation to determine equivalency.  The Division of Highways reserves the right to reject any product it deems to pose a potential environmental or safety related problem.  The final determination of equivalency will be made by the Division of Highways.

Upon notification of award, the successful vendor shall furnish the Division of Highways, Maintenance Division Director two product labels for each product awarded of items five (5) through eight (8).  The labels shall provide pertinent information regarding product storage and handling.  Product storage and handling information and product label shall also be provided with each shipment.

Chemical containers must arrive on the job site with their seals unbroken.

The vendor is responsible for making arrangements to obtain a clean water source outside of the Division	of Highways’ right-of-way for mixing with herbicides.  Delivery or storage of the vendor’s equipment or 	chemical at the Division of Highways is prohibited.

4.	EQUIPMENT REQUIREMENTS

1.	Equipment shall be a spray boom truck to be used on a majority of the spraying (see item A below), while an articulated spray boom truck will be used for treating wider right-of-ways mainly in conjunction with median and brush control operations (see item B below).  Two trucks must be available at any time upon the request by the Division of Highways during the pendency of this contract.

A.  Spray Boom Truck

The Spray Unit must be a minimum 800 gallon unit and must be equipped with

the following:  1)  a sprayer control system capable of automatically maintaining

application rate; 2) a vehicle speed sensor which is either connected to the vehicle

speedometer or a radar type sensor; 3) minimum of eight (8) separate boom widths;

4)  two (2) different application ratios; and 5) a manual setting for spot spraying.

The herbicide application unit is to be equipped with an eight (8) boom nutating

spray head, using all brass or stainless steel nozzles capable of delivering a

no-streak pattern of two feet (2’) to thirty-two feet (32’) in width.  All booms shall

operate 	independently or simultaneously to apply the necessary spray widths as

needed.  The application system shall have oscillating motion on booms one (1)

through four (4); these nozzles must be electrically driven by a 12-volt system.

The unit shall provide a uniform spray pattern while providing spray drift control.

The above equipment shall be mounted on a suitable flat-bed type truck.  The

operator/driver shall possess herbicide applicators certification meeting the

requirements of the State of West Virginia.  Refer to Section 6.

B.  Articulated Spray Boom Truck

The Spray Unit must be a minimum 800 gallon unit and must be equipped with

the following:  1)  a sprayer control system capable of automatically maintaining

application rate; 2) a vehicle speed sensor which is either connected to the

vehicle speedometer or a radar type sensor; 3) having the capability of spraying

a minimum of ten (10) separate boom widths; 4) two (2) different application ratios;

and 5) a manual setting for spot spraying.

The herbicide application unit is to be equipped with nine (9) boom nutating

multiple spray head systems, using all brass or stainless steel nozzles capable of

delivering a no-streak pattern up to a minimum of fifty feet (50’) in width.  All booms

shall operate independently or simultaneously to apply the necessary spray widths

as needed.  The application system shall have oscillating motion on booms one

(1) through four (4); these nozzles must be electrically driven by a 12-volt system.

The unit shall provide a uniform spray pattern while providing spray drift control.

The articulated spray boom shall be mounted in the centerline of the truck.  The

boom shall be capable of rotating 90 degrees to the left and right of the centerline

of the truck and have a minimum vertical arc of 80 degrees.  The boom shall be a

minimum of 18 feet (18’) when fully extended and shall be equipped with a Norstar

spray head application system or equal.  If an or equal spray head system is proposed,

specifications for that system shall accompany the bid for Division of Highways

evaluating equivalency purposes.

All controls for the movement of the boom and spray heads shall be controlled by

a joy stick or switches from within the cab of the truck.

The above equipment shall be mounted on a suitable flat-bed type truck.  The

operator/driver shall possess herbicide applicators certification meeting the

requirements of the State of West Virginia.  Refer to Section 6..

2.	A handheld or backpack style sprayer or similar shall be used when control path spraying of Wild Flower Plots is needed.

3.	The vendor shall provide two-way communications between the spray unit and Division of Highways inspector monitoring the work, in order to optimize project quality.

The successful vendor(s) shall be responsible for all fuel, repair, maintenance and insurance for the	equipment and operator.

The successful vendor(s) shall comply with all laws, rules and regulations of the State of West

Virginia.

5.	CONTRACT AWARD

Qualified vendors who submit a valid low bid will be awarded a contract for the District(s) for which their bid

is low, provided that the vendor has listed the product trade name and EPA Registration Number for items five (5) through eight (8) on the Bid Schedule, as indicated in Section 3.  Failure to list this information will result in the disqualification of the vendor's bid on that product.

The award for each item will be based on the bid price per unit of measure as requested on the Bid Schedule.  Vendors are cautioned that the quantities on the Bid Schedule are estimates only.

The State of West Virginia reserves the right to make multiple awards on this contract when it is in the best interest of the State.

6.	ACCEPTANCE PLAN

Within thirty (30) days from the date of award, the successful vendor(s) must assemble all proposed equipment and personnel to demonstrate to the satisfaction of the Division of Highways District Maintenance Engineers or their designee, that the equipment and personnel meet the requirements of this contract.  This demonstration is to take place at a time and date mutually agreed upon by the Division of Highways District Maintenance Engineer or their designee and the vendor.  See Division of Highways District locations and Maintenance Engineers’ contact information, Section 19.

The Division of Highways reserves the right to terminate immediately the usage of any herbicide spray	system and/or personnel which does not perform to reasonable production standards.  These reasonable	production standards will be based on historical performance data under similar circumstances as	determined by the Division of Highways.

At a mandatory pre-bid conference, vendors must show evidence of employment of qualified and 	experienced operator/certified herbicide applicators meeting the requirements of the State of West

Virginia to be eligible to bid on items contained in this RFQ.

7.	MOBILIZATION

Mobilization will be incurred for equipment by the Division of Highways to the initial job site from the vendor’s base station.  The vendor’s base station shall be construed to be his permanent established headquarters or in the case of moving from one Division of Highway’s job site to the next, the present location or whichever will cost less.

In-state delivery route mileage will be calculated by the Division of Highways from the vendor’s base station to the Division of Highways’ job site by utilizing the Division of Highways Straight Line Diagrams.  These Diagrams for WV Primary Routes and WV Secondary Routes are available in each Division of Highways District office and the Division of Highways Central Office.  The Division of Highways will determine the route to be taken due to bridge and/or road restrictions.

Out-of-state delivery route mileage will be calculated by the Division of Highways utilizing “Mapquest” or a similar source for routing from the vendor’s base station to the WV State line at which time, the Straight Line Diagrams will be sourced to the Division of Highways job site.

Mobilization is only paid one-way per mile.

8.	TRAFFIC CONTROL

Traffic control will be provided by the Division of Highways with the exception of the work vehicles provided

by the vendor.  Reference can be made to Traffic Control Case A8 which applies to two lane/two-way traffic roads as well as one lane/two-way traffic roads and Traffic Control Case A15 which applies to two-way/two lane traffic roads (expressways).  See Appendix A.

All work vehicles provided by the vendor shall be equipped with two flags, one rotating high-intensity amber light and a “Slow Moving” triangle mounted on the rear of the vehicle.

9.	PERFORMANCE CLAUSE

In areas where the expected results were not attained, the Division of Highways may require the vendor re-apply to the area.  There may be a number of reasons that the herbicide may not eliminate the target vegetation, some of which may or may not be the vendor’s fault; however, the Division of Highways will not pay labor, equipment or material expense for herbicide re-applied.

If threatening weather is forecast on scheduled application days, it will be the vendor’s decision whether or not to apply herbicides on that day.  The Division of Highways recommends that no spraying be performed, but will not make the final decision, on any given-day, when threatening weather is forecast.  If the vendor makes the decision to spray and rain does develop that renders the spraying ineffective, the Division of Highways will not pay labor, equipment or material expense for herbicide re-applied.

10.	BID QUANTITIES

Vendors are cautioned that the quantities listed on the Bid Schedule are estimates only.  Actual requests will be placed to the awarded vendor from the Division of Highways by an Agency Release at the time of need.

11.	DELIVERY

The successful vendor shall be prepared to mobilize and begin work within thirty (30) days after receipt of an Agency Release from the Division of Highways; however, the Division of Highways shall have the option of accepting an alternative delivery schedule provided by the awarded vendor which shall be established at the time of the Agency Release.

If delivery has not been received at the Division of Highways within thirty (30) days after receipt of an	Agency Release from the Division of Highways and an alternative delivery schedule has not been established	for this delivery, the Division of Highways reserves the right to cancel the Agency Release and proceed 	to obtain the service from the next low bid vendor.

12.	BASIS OF PAYMENT

The vendor shall invoice the Division of Highways for acres sprayed and/or mobilization charges on a bi-monthly basis.  Mobilization miles and acres sprayed must be verified on a daily basis by an authorized representative of the Division of Highways.  The vendor must provide a daily receipt ticket, easily identified as such by a reference ticket number, date of service and the acreage sprayed.  The date and ticket number must be referenced on the invoice in order for proper payment to be made.

13.	VENDOR'S INVOICES

Vendor's invoices must be submitted in original and four copies and contain the following:

a.	Division of Highways Agency Release Number and Contract Number.

b.	Total acres sprayed and/or mobilization charges on a bi-monthly basis.

Mobilization miles and acres sprayed must be verified on a daily basis

by an authorized representative of the Division of Highways.

c.	Unit price with the total cost of each type of item provided.

d.	A daily receipt ticket, easily identified as such by a reference ticket,

date of service and the acreage sprayed.  The date and ticket number

must be referenced on the invoice in order for proper payment to be

made.

Note:  Under no circumstance will the Division of Highways accept, or pay for,

quantities of material in excess of the quantity stated on the Agency Release.

14.	WAGE RATES

The Contractor or Subcontractor shall pay the higher of the U.S. Department of Labor minimum wage rates	or the West Virginia Department of Labor minimum wage rates as established for applicable counties, 	pursuant to West Virginia Code §21-5A, ET SEQ.

15.	WORKER’S COMPENSATION

Successful vendor(s) is required to provide a certificate from Worker’s Compensation.

16.	INSURANCE

The successful vendor(s) shall furnish proof of commercial General Liability insurance prior to issuance of a contract with the minimum required amount of coverage to be $250,000.00.

17.	PURCHASING CARD ACCEPTANCE

The State of West Virginia currently utilizes a VISA Purchasing Card Program which is issued through a	bank.  The successful vendor(s) must accept the State of West Virginia VISA Purchasing Card for payment	of all orders placed by the Division of Highways as a condition of award.

18.	MANDATORY PRE-BID

There will be a mandatory pre-bid meeting on _______________________________________.

Location:	Purchasing Division Conference Room

2019 Washington Street, East, Building 15

Charleston, WV 25305

19.	DISTRICT LOCATIONS AND DISTRICT MAINTENANCE ENGINEERS

District 1		Raymond J. Scites

Charleston WV	304-558-3002

District 2		Ed Armbruster

Huntington WV	304-528-5630

District 3		Dave Brabham

Parkersburg WV	304-420-4648

District 4		Jeff Pifer

Clarksburg WV	304-842-1558

District 5		Barry Knotts

Burlington WV	304-289-2208

District 6	     	Lloyd Adams

Moundsville WV    304-843-4017

District 7	     	Ron Smith

Weston WV	304-269-8940

District 8	     	Shelton Barger

Elkins WV	    	304-637-0220

District 9	     	Nathan Thomas

Lewisburg WV	304-647-7839

District 10	     	Alan Reed

Princeton WV	304-487-5231